| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-05-16 |
| Contact:* | As above |
| Reason for Change/s:* | This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to obtain an receiverESPRimRandObject from a Receiver. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0019 Dynamic Authorization MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.5.0 |
| Clauses/Sub Clauses* | New clause 7.5.1.2.x “Notification for receiverESPRimRandObject Retrieval” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to obtain an receiverESPRimRandObject from a Receiver.

R00 to R01 delta: Editorial (correcting typographical errors and incorrect italics emphasis)

R01 to R02 delta: Editorial – several occurences of “receiverESPRimRandObject” changed to “receiverESPrimRandObject”

### ----------------------- Start of change 1---------------

##### 7.5.1.2.x Notification for receiverESPrimRandObject Retrieval

Originator:

When the Originator is triggered to perform receiverESPrimRandObject Retrieval as part of establishing sessionESPrimKey with a Receiver, it performs the following steps in order:

- Configure the To parameter with the address of the Receiver.

- Configure the From parameter with the ID of the Originator.

- The securityInfoType element of the securityInfo element of the notification data shall be configured as “3” (receiverESPrimRandObject Request) in the Notify request primitive

- The Originator shall send the notification request for dynamic authorization to the targeted Receiver.

Receiver:

When a Receiver receives a notification request, it processes the securityInfoType element of the securityInfo element and determines that the notification is for receiverESPrimRandObject Retrieval. The Receiver generates an receiverESPrimRandObject as specified in TS-0003 [7]. Then the Receiver sends a notification response to the Originator, with the securityInfo element containing the following elements

- The securityInfoType element shall be configured as “4” (receiverESPrimRandObject Response) in the Notify request primitive

- The esprimRandObject shall contain the receiverESPrimRandObject.

When the Originator receives a notification response for dynamic authorization, it performs the following steps in order:

- The Originator shall verify that the securityInfoType element of the securityInfo element of the notification is as configured as “4” (receiverESPrimRandObject Response).

- The Originator shall check whether the securityInfo element contains an esprimRandObject element.  If it does, the Originator shall use the receiverESPrimRandObject in esprimRandObject element in the generation of sessionESPrimKey.

### ----------------------- End of change 1 -------------