| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-05-15 |
| Contact:* | As above |
| Reason for Change/s:* | This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to exchange ESPrim Objects. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 End-to-End Security and Group Authentication MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.5.0 |
| Clauses/Sub Clauses* | New clause 7.5.1.2.x “Notification for ESPrimObject exchange” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to exchange ESPrim objects with a Receiver.

### ----------------------- Start of change 1---------------

##### 7.5.1.2.x Notification for ESPrimObject Exchange

Originator:

When the Originator is to use ESPrim to secure an inner request primitive targeting the Receiver, then the Originator performs the following steps in order:

- Configure the To parameter with the address of the Receiver.

- Configure the From parameter with the ID of the Originator.

- Form the ESPrimObject from the inner request primitive as specified in TS-0003.

- The securityInfoType element of the securityInfo element of the notification data shall be configured as “5” (ESPrim Object) in the Notify request primitive

- The esprimObject element of the securityInfo element of the notification data shall be set to the value of the ESPrim Object in the Notify request primitive

- Send the notification request for ESPrimObject exchange to the targeted Receiver.

Receiver:

When a Receiver receives a notification request for ESPrimObject exchange, then the Originator performs the following steps in order:

- Process the securityInfoType element of the securityInfo element and determine that the notification is an ESPrim Object Retrieval.

- Extract the esprimObject.

- Processes the ESPrim Object (contained in esprimObject) as specified in TS-0003 [7]. In the successful case, this produces a representation of the inner request primitive which can then be processed as described in clause 7.2.2.2.

- Generates an inner response primitive in reply to the inner request primitive.

- Forms a second ESPrim Object from the inner response primitive as specified in TS-0003 [7].

- The securityInfoType element of the securityInfo element of the notification data shall be configured as “5” (ESPrim Object) in the Notify response primitive.

- The esprimObject element of the securityInfo element of the notification data shall be set to the value of the second ESPrim Object in the Notify response primitive.

- Send the notification request for ESPrimObject exchange to the Originator.

When the Originator receives a notification response for ESPrimObject exchange, it shall perform the following steps in order:

- Verify that the securityInfoType element of the securtyInfo element of the notification is as configured as “4” (ESPrim Object).

- Process the securityInfoType element of the securityInfo element and determine that the notification is an ESPrim Object Retrieval.

- Extract the esprimObject.

- Process the ESPrim Object (contained in esprimObject) as specified in TS-0003 [7]. In the successful case, this produces a representation of the inner response primitive which can then be processed as described in clause 7.2.2.1.

### ----------------------- End of change 1 -------------