| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-05-15 |
| Contact:* | As above |
| Reason for Change/s:* | This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to exchange ESPrim Objects. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 End-to-End Security and Group Authentication MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.5.0 |
| Clauses/Sub Clauses* | New clause 7.5.1.2.x “Notification for End-to-End Security of Primitives (ESPrim)” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to exchange ESPrim objects with a Receiver.

### ----------------------- Start of change 1---------------

##### 7.5.1.2.x Notification for End-to-End Security of Primitives (ESPrim)

Introduction. The End-to-End Security of Primitives (ESPrim) provides end-to-end protection of a Request primitive and corresponding Response primitives (called the inner request primitive and inner response primitive) by encrypting the primitives and forming an ESPrim Object. A Notify Request and corresponding Notify Response primitives (called the outer request primitive and outer response primitive) are used to transport the ESPrim Objects containing this encrypted inner request primitive and inner response primitive respectively.

Communication Mode: The Notify Request and corresponding Notify Response may be communicated using any of the Communication Modes. The selected Communication Mode is indicated in the Notify Request: for details see Step Orig-3.0 in clause 7.2.2.1 and Recv-2.0 in clause 7.2.2.2. The inner request primitive shall not include the Response Type parameter.

Table 7.5.1.2.X-1 describes the process using notification for ESPrim. The Receiver in this description is the Hosting CSE. The procedure for transit CSEs is not affected.

This description assumes that the Originator and Receiver have established a pairwiseESPrimKey and steps have been performed for establishing a sessionESPrimKey at the Originator (phases A and B in clause 8.4.2 of oneM2M TS-0003 [7]) .

Table 7.5.1.2.x-1: Using notification for End-to-End Security of Primitives (ESPrim)

| Inner primitive Step | ESPrim process | Outer primitive step | Additional detail to clause 7.2.2.1 or 7.2.2.2 or other clauses referenced from there |
| --- | --- | --- | --- |
| Orig-1.0 |  |  | “Compose of a Request primitive” The inner request primitive shall not include the Response Type parameter. |
| Orig-2.0 |  |  | "Send a Request primitive to the Receiver CSE" No step corresponding to Orig-2.0 for inner request primitive |
| Orig-3.0 |  |  | "Check Response Type". Communication mode shall be blockingRequest for inner request primitive |
| Orig-4.0 |  |  | “Wait for Response primitive”: no additional details. |
|  | Orig Encrypt |  | Encrypt inner request primitive as specified in oneM2M TS-0003 [7] to form an ESPrim Object |
|  |  | Orig-1.0 | “Compose of a Request primitive” Mandatory and optional parameters are described in clause 11.4.2 of TS-0001 [6]. To = esprimPoA in e2eSEcInfo of Receiver Form Notification data = securityInfo with securityInfoType = “5” (ESPrim Object) and esprimObject containing ESPrim Object. |
|  |  | Orig-2.0 | "Send a Request primitive to the Receiver CSE". No additional details |
|  |  | Orig-3.0 | "Check Response Type". No additional details |
|  |  | Orig-4.0 | Steps for blockingRequest: No additional details |
|  |  | Orig-4.1 to Orig-5.3 | Steps for nonBlockingRequestSynch: No additional details |
|  |  | Orig-4.1 to Orig-9.1 | Steps for nonBlockingRequestAsynch: No additional details |
|  |  | Recv-1.0 to Recv-6.4 | No additional details |
|  |  | Recv-6.5 | “Create/Update/Retrieve/Delete/Notify operation is performed”, with details for “Notify Re-targeting” in clause 7.3.3.9. Extract the securityInfo element from the notification data Parse notification data examines the securityInfoType element of the securityInfo element and determines from its value “6” (ESPrim Object) that the securityInfo includes an ESPrim Object Extract ESPrim Object from esprimObject element of securityInfo |
|  | Recv Decrypt |  | Decrypt ESPrim Object as specified in oneM2M TS-0003 [7] to form an inner request primitive |
| Recv-1.0 |  |  | "Check the validity of received request primitive": No additional details |
| Recv-2.0 |  |  | "Communication method?". Shall be blockingRequest |
| Recv-6.0 to Recv-6.7 |  |  | "Resource handling procedure": No additional details |
| Recv-6.8 |  |  | “Send Response Primitive” No step corresponding to Orig-2.0 for inner request primitive |
|  | Recv Encrypt |  | Encrypt inner response primitive as specified in oneM2M TS-0003 [7] to form an ESPrim Object |
|  |  | Recv-6.6 | “Announce/De-announce the resource”. Not applicable for Notify |
|  |  | Recv-6.6 to Finish | No additional details |
|  |  | Orig-6.0 | “Process Response primitive” Extract the securityInfo element from the notification data Parse notification data examines the securityInfoType element of the securityInfo element and determines from its value “6” (ESPrim Object) that the securityInfo includes an ESPrim Objec Extract ESPrim Object from esprimObject element of securityInfo |
|  | Orig Decrypt |  | Decrypt ESPrim Object as specified in oneM2M TS-0003 [7] to form an inner response primitive |
| Orig-6.0 |  |  | “Process Response primitive”: No additional details |

### ----------------------- End of change 1 -------------