| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.0 |
| Source:* | KETI |
| Date:* | 2016-05-16 |
| Contact:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr Sungchan Choi, KETI, csc@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Reason for Change/s:* | Adding m2m:aggregatedResponse format support for response of conditional retrieve operations |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v1.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces a issue regarding the format for response of conditional retrieval operations when filter usage parameter is not present as a querystring in the To parameter.

According to the TS-0004, when filter usage is set to 2 (default value for filter usage parameter) in a retrieve request, the CSE receiver will handle the request as a conditional retrieval operation and respond the request originator with resources that met with provided filter criterias such as offset, limit, and level etc. condition, if any.

The response may be represented as an aggregated response including all discovered resources, if any, but the problem is in TS-0004, it is not clear to define the format of response for this case. In addition, the data type of m2m:aggregatedResponse is only defined for CRUD operations on a <fanOut> child resource of a <group> parent resource.

We propose to apply the data type of m2m:aggregatedResponse to be used as the data type for the response for conditional retrieval operation.

### -------------Start of change 1--------------------------------------------------------

## Primtive format and generic procedure

7.2.1	Primitive format

#### 7.2.1.2 Response primitive format

The Content parameter in a Response shall contain one of the following:

- A complete or partial Resource. This applies to a response primitive sent in reply to create and retrieve request message. In this case the Content parameter shall contain a single root element whose name is the name of the Resource and whose content consists of one or more attributes, child resources or childResource references. In this case the resource type is as defined in clause 7.4. However if a partial resource is being transferred, it is not required to be valid according to the XSD for that resource, in terms of the presence of resource attributes. Any attribute that is present, however, shall comply to the data type defined in the XSD of that resource.

The URI of a resource. This is included directly as the content of the Content parameter (like in case 6)

A partial resource and its hierarchical URI. These are included in a root element called m2m:resource defined in clause 7.5.2. The URI is included as an attribute of m2m:resource.

A list of URIs. This can be used for transferring the childResource URIs only or in a Discovery response. These are included in an element called m2m:URIList defined in clause 7.5.2.

An Aggregated Response. This is sent as a result of a Group or a conditional retrieve operation. This uses the element m2m:aggregatedResponse defined in clause 7.5.2.

Raw data. This could be a simple data value, or structured data (an XML complex type or JSON object)

### -------------End of change 1--------------------------------------------------------

### -------------Start of change 2-------------------------------------------------------

### Elements contained in the Content primitive parameter

Clauses 7.2.1.1 and 7.2.1.2 enumerate the forms that the Content primitive parameter takes in various Request and Response cases. Note that the Content primitive parameter is denoted as primitiveContent in both, CDT-requestPrimitive-v1_7_0.xsd and CDT-responsePrimitive-v1_7_0.xsd.

This clause details the Objects (elements) used in some of these cases in the tables below.

The following elements are defined for use in the Content parameter of a request:

Table 7.5.2-1: Elements used for request content

| Element Name | Applicable Operations | Data Type | Defined in |
| --- | --- | --- | --- |
| m2m:<resourceType> | C U | m2m:<resourceType> | CDT-<resourceType>-v1_7_0.xsd |
| m2m:notification | N | m2m:notification | CDT-notification-v1_7_0.xsd |
| m2m:aggregatedNotification | N | m2m:aggregatedNotification | CDT-notification-v1_7_0.xsd |
| m2m:attributeList | R | m2m:attributeList | CDT-requestPrimitive-v1_7_0.xsd |
| m2m:responsePrimitive | N | m2m:responsePrimitive | CDT-responsePrimitive-v1_7_0.xsd |

The following elements are defined for use in the Content parameter of a response sent in reply to a request message with Operation and Result Content (rcn) parameters as given in the column "Applicable Operations" (the settings of the Result Content parameters are defined in clause 6.3.3.2.7; NP means the rcn parameter is not present)::

Table 7.5.2-2: Elements used for response content

| Element Name | Applicable Operations/rcn | Data Type | Element is Defined in |
| --- | --- | --- | --- |
| m2m:<resourceType> | C/1, 7,NP R/1,4,5,6,7,NP U/1,NP D/1,NP See NOTE 1 | m2m:<resourceType> | CDT-<resourceType>-v1_7_0.xsd |
| m2m:resource | C/3 | m2m:resourceWrapper | CDT-responsePrimitive-v1_7_0.xsd |
| m2m:URIList | R/NP See NOTE 2 | m2m:listOfURIs | CDT-responsePrimitive-v1_7_0.xsd |
| m2m:aggregatedResponse | C R U D See NOTE 3 | m2m:aggregatedResponse | CDT-responsePrimitive-v1_7_0.xsd |
| m2m:URI | C/2 See NOTE 4 | xs:anyURI | CDT-responsePrimitive-v1_7_0.xsd |
| Raw data | See NOTE 5 |  |  |
| NOTE 1: The case rcn = 7 applies to Retrieve operation only (R/7). It retrieves the original resource in case the To parameter points to an announced resource. NOTE 2: This applies to ordinary retrieve operation when the Result Content parameter is not present and for discovery operation. For discovery, the format of the URIList elements (structured, unstructured) depends on the Discovery Result Type parameter setting (see clause 6.3.3.2.8). NOTE 3: This applies to both CRUD operations on a <fanOut> child resource of a <group> parent resource and conditional retrieve operations to resources. The Content parameter of each response primitive included in aggregatedResponse is set as given in one of the other rows of this table. In conditional retrieve operation case, the Content parameter of the response primitive included in aggregatedResponse is set as a list of resources starting with a root and including attributes and/or desendants according to the rule set by result content parameter, if provided by request originator. An example for the response of the conditional retrieve operation looks like as below: <m2m:agr xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance”> <rsp> <m2m:ae rn=”cae1”> <ty>2</ty> <ri>/in-cse/cae01234</ri> <ct>20160503T115238</ct> <lt>20170503T115238</lt> </m2m:ae> <m2m:ae rn=”cae2”> <ty>2</ty> <ri>/in-cse/cae01235</ri> <ct>20160503T115240</ct> <lt>20170503T115240</lt> </m2m:ae> </rsp> </m2m:agr> NOTE 4: This also applies to the response ("acknowledgement") to non-blocking requests in asynchronous mode for any CRUD operation NOTE 5: Raw data could e.g. be included as debugging information into error responses |

-----------------------End of change 2------------------------------------------------------------