| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-05-15 |
| Contact:* | As above |
| Reason for Change/s:* | Changes the encodingType enumerated data type to allow contentInfo to indicate when and how the content has been secured using ESData. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0019 Dynamic Authorization MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.5.0 |
| Clauses/Sub Clauses* | 6.3.4.2.28 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This change was previously part of in PRO-2016-0183, but concerns were raised that this change alters how contentInfo is being used. This change was moved to the present CR so the other changes in PRO-2016-0183 could be agreed independently.

The references in the notes are already provided in PRO-2016-0183.

### -----------------------Start of change 1 ---------------

##### 6.3.4.2.28 m2m:encodingType

Used for describing encoding type which is applied on the content attribute of the contentInstance resource.

Table 6.3.4.2.28-1: Interpretation of encodingType

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | Plain - no transfer encoding is applied |  |
| 1 | base64 encoding (see [9]) is applied on string data |  |
| 2 | base64 encoding (see [9]) is applied on binary data |  |
| 10 | JWE Compact Serialization for Encryption-Only End-to-End Security of Data (ESData) Security Class | See [i.RFC7516] |
| 11 | JWS Compact Serialization for Signature-Only ESData Security Class | See [i.RFC7515] |
| 12 | JWE Compact Serialization for Nested-Sign-then-Encrypt ESData Security Class | See [i.RFC7516] |
| 20 | Plain JWE JSON Serialization for Encryption-Only ESData Security Class- no transfer encoding is applied | See [i.RFC7516] |
| 21 | Plain Plain JWS JSON Serialization for Signature-Only ESData Security Class- no transfer encoding is applied | See [i.RFC7515] |
| 22 | JWE JSON Serialization for Nested-Sign-then-Encrypt ESData Security Class- no transfer encoding is applied | See [i.RFC7516] |
| 30 | base64 encoding (see [9]) applied on JWE JSON Serialization for Encryption-Only ESData Security Class | See [i.RFC7516] |
| 31 | base64 encoding (see [9]) applied on JWS JSON Serialization for Signature-Only ESData Security Class | See [i.RFC7515] |
| 32 | base64 encoding (see [9]) applied on JWE JSON Serialization for Nested-Sign-then-Encrypt ESData Security Class | See [i.RFC7516] |
| 40 | Plain XML Encryption v1.1 Serialization for Encryption-Only ESData Security Class - no transfer encoding is applied | See [i.XML-ENCv1.1] |
| 41 | Plain XML Encryption v1.1 Serialization for Signature-Only ESData Security Class - no transfer encoding is applied | See [i.XML-SIGv1.1] |
| 42 | Plain XML Encryption v1.1 for Nested-Sign-then-Encrypt ESData Security Class - no transfer encoding is applied | See [i.XML-ENCv1.1] |
| 50 | base64 encoding (see [9]) is applied on XML Encryption v1.1 Serialization for Encryption-Only ESData Security Class | See [i.XML-ENCv1.1] |
| 51 | base64 encoding (see [9]) applied on XML Encryption v1.1 Serialization for Signature-Only ESData Security Class | See [i.XML-SIGv1.1] |
| 52 | base64 encoding (see [9]) applied on XML Encryption v1.1 for Nested-Sign-then-Encrypt ESData Security Class | See [i.XML-ENCv1.1] |

### -----------------------End of change 1 ---------------