| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.4 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-06-23 |
| Contact:* | As above |
| Reason for Change/s:* | Provides the procedures for a Notify request operating on a <CSEBase> resource |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.6.0 |
| Clauses/Sub Clauses* | 7.2.2.2, 7.3.3.9, title of 7.4.3.2, new 7.4.3.2.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides the changes to supporting the <CSEBase> resource specific procedure for the Notify operation. A new clause 7.4.3.2.5 is created, and the title of clause 7.4.3.2 is updated to include “+N” for notification.

R01 delta to R00:

- added changes to clause 7.3.3.9 “Notify re-targeting” to allow for Notify targeting a <CSEBase> resource

R02 delta to R01

- Changed title of clause 7.3.3.9 to “Notify processing”. Changed step Recv-6.5 in clause 7.2.2.2 to align with name change.

- Separated cases for <AE> and <CSEBase> into sub-clauses of 7.3.3.9.

### Update the following step in clause 7.2.2.2 “Generic request procedure for receiver”

### ----------------------Start of change 1 (clause 7.2.2.2)----------------------------------

Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed": The step represents five common operations which are "Create the resource (clause 7.3.3.5)", "Retrieve the resource (clause 7.3.3.6)", "Update the resource (clause 7.3.3.7)", "Delete the resource (clause 7.3.3.8)" and "Notify processing (clause 7.3.3.9)".

### ------------------------End of change 1 -------------------------------------------

### -----------------------Start of change 2 -------------------------------------------

#### 7.3.3.9 Notify Processing

#### 7.3.3.9.1 Notify Processing when To parameter is an <AE> resource

If the Operation Excution Time is given in the request, the Hosting CSE should perform the following procedures at the time and shall not perform the procedures before the time.

When the Hosting CSE receives a Notify request primitive targeting (i.e., To parameter) its <AE> resource, the Hosting CSE re-targets the primitive to the AE if the <AE> resource does not have any <pollingChannel> resource as a child.

- Get pointOfAccess attribute value of the corresponding <AE> resource. If there is no available pointOfAccess address then the Hosting CSE shall send the Notify response primitive with a Response Status Code indicating "TARGET_NOT_REACHABLE" error.

Forward the Notify request primitive to the first address retrieved from pointOfAccess value

If the forwarding is failed due to "Target not reachable", iterate 2) with the next address.

- If the Hosting CSE cannot forward it in the end, then it send the Notify response primitive with a Response Status Code indicating "TARGET_NOT_REACHABLE" error.

#### 7.3.3.9.2 Notify Processing when To parameter is the <CSEBase> resource

If the Operation Excution Time is given in the request, the Hosting CSE should perform the following procedures at the time and shall not perform the procedures before the time.

When the Hosting CSE receives a Notify request primitive targeting (i.e., To parameter) its <CSEBase> resource, the Hosting CSE shall process the Content of the Notify request primitive. See clause 7.5.1.

### ------------------------End of change 2 -------------------------------------------

### ----------------------Start of change 3 -------------------------------------------

#### 7.4.3.2 	<CSEBase> resource specific procedure on CRUD+N operations

### -----------------------End of change 3 -------------------------------------------

### -----------------------Start of change 4 -------------------------------------------

##### 7.4.3.2.5 	Notify

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

### ----------------------- End of change 4 ------------------------------------------