| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.5 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-06-29 |
| Contact:* | As above |
| Reason for Change/s:* | Providing information about End-to-End Security of Data (ESData) processing when applied to content attribute of the <contentInstance> resource type. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 End-to-End Security MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.6.0 |
| Clauses/Sub Clauses* | 6.3.3, new subclause of 6.3.4.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Rather than changing m2m:encodingType  enumerated data type (see PRO-2016-0218), the changes proposes optionally extending contentInfo by adding m2m:contentSecurity providing the appropriate information about End-to-End Security of Data (ESData) applied to the content, if any, and any subsequent transfer encoding.  The  media type and m2m:encodingType is information about the content data to which the End-to-End Security of Data processing, if any, was applied as indicated by m2m:contentSecurity. The enumeration of 0 for m2m:contentSecurity is interpreted as “ESData has not been applied to the content data”. If the m2m:contentSecurity is not present, then this is interpreted the same as the enumeration of 0 for m2m:contentSecurity, that is, “ESData has not been applied to the content data”.

The m2m:contentSecurity value is optional, in order that the Release 2 m2m:contentInfo provides backwards compatibility with Release 1 m2m:contentInfo.

This contribution also makes m2m:encodingType a mandatory part of m2m:contentInfo, as implied by the existing note at the end of table 6.3.3-1. The existing note is then deleted as it no longer applies.

R01 delta from R00. Changes suggested at “PRO23.4 with SEC” conference call

- Corrected the example in change 1 from “application/xml:2” to “application/xml:1” since the existing example did not make sense since encoding type 2 applies only to binary data.

- Note 1 in change 2 was expanded to explain that the values in the contentInfo indicate a sequence of processes to be applied to the retrieved content attribute.

- Added notes 3, 4 and 5 to the table in change 3.

R02 delta to R01

- Previously the new data type was called m2m:esdataInfo. As requested at PRO23.4, the data type has been given a new name – it is now m2m:contentSecurity (including in this Introduction text). The authors forgot to incorporate this change in the previous revision.

- Other minor editorial corrections.

### Alter the following row of Table 6.3.3-1.

### -----------------------Start of change 1 (clause 6.3.3)---------------

| m2m:contentInfo | Content Information | application/xml:1 application/xml:1:0 application/xml:1:5 | A string consisting of a media type followed by a m2m:encodingType and optional m2m:contentSecurity, each separated by ':' character. If the m2m:contentSecurity value is not present, then the preceding ':' shall also be not present. If the m2m:contentSecurity value is not present then this has the same interpretation as a value of 0 for m2m:contentSecurity. See Note-1 |
| --- | --- | --- | --- |

### -----------------------End of change 1 ---------------

### Alter the following row of Table 6.3.3-1.

### -----------------------Start of change 2 (clause 6.3.3)---------------

NOTE 1: The media type and m2m:encodingType in m2m:contentInfo describe the content data to which the End-to-End Security of Data (ESData) processing, if any, was applied as indicated by m2m:contentSecurity. The m2m:contentInfo indicates a sequence of processes to be applied to the content after being obtained from the CSE. First, the ESData processing (if any) as indicated by m2m:contentSecurity is applied. The result of this processing then has transfer decoding (if any) applied as indicated by m2m:encodingType. The result of this processing is then processed according to the media type.

### -----------------------End of change 2 ---------------

### Add as a sub-clause of clause 6.3.4.2 “Enumeration Type Definitions”

### -----------------------Start of change 2 (new clause) ---------------

##### 6.3.4.2.a m2m:contentSecurity

Used in m2m:contentInfo.

Table 6.3.4.2.a-1: Interpretation of contentSecurity

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | ESData has not been applied to the content data. |  |
| 1 | ESData using JWE and/or JWS with Compact Serialization has been applied to the content data with no subsequent transfer encoding. See Note 2. | See Note 3 |
| 2 | ESData using JWE and/or JWS with JSON Serialization has been applied to the content data with no subsequent transfer encoding. | See Note 4 |
| 3 | ESData using JWE and/or JWS with JSON Serialization has been applied to the content data and subsequent base64 encoding (see [9]) has been applied. | See Note 4 |
| 4 | ESData using XML encryption and/or XML-Signature has been applied to the content data has been applied with no subsequent transfer encoding. | See Note 5 |
| 5 | ESData using XML encryption and/or XML-Signature has been applied to the content data and subsequent base64 encoding (see [9]) has been applied. | See Note 5 |
| NOTE 1: See oneM2M TS-0003 [7] for details on these security protocols NOTE 2: JWE and/or JWS with Compact Serialization is almost entirely base64URL encoded by default - see m2m:e2eCompactJWS and m2m:e2eCompactJWE in Table 6.3.3. Consequently, there is no option for additional base64 encoding of JWE and/or JWS with Compact Serialization. NOTE 3: The ESData envelope (see oneM2M TS-0003 [7]) in this case has media type application/jose. NOTE 4: The ESData envelope in this case has media type application/jose+json. NOTE 5: The ESData envelope in this case has media type application/xenc+xml or application/xml (the latter is the media type for XML Signature). |

### -----------------------End of change 2 ---------------