| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#23.6 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-07-07 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | There are minor erros in m2m:mgmtResource and m2m:announcedMgmtResource datra types. |
| CR against: Release* | R2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / <Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.6.0 |
| Clauses/Sub Clauses* | 6.3.5.34, 6.3.5.35, 6.3.6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: PRO-2016-0239 : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This is a mirror CR of PRO-2016-239. There is one addition pertaining to the dynamicAuthorizationConsultationIDs, which is specific to release 2 and only appears in this CR.

This CR proposes minor corrections to two data types, m2m:mgmtResource and m2m:announcedMgmtResource.

For the m2m:mgmtResource, m2m:announceableResource are used as the extension base. However, there are differences in multiplicity for some elements between those two data types. These shall be the same. No change required in the XSD.

| Element Path | Element Data Type | Multiplicity |
| --- | --- | --- |
|  |  | m2m:announceableResource | m2m:mgmtResource |
| @resourceName | xs:NCName | 1 | 1 |
| resourceType | m2m:resourceType | 1 | 1 |
| resourceID | m2m:ID | 1 | 1 |
| parentID | m2m:nhURI | 1 | 1 |
| accessControlPolicyIDs | m2m:acpType | 0..1 | 0..1 |
| creationTime | m2m:timestamp | 1 | 0..1 |
| expirationTime | m2m:timestamp | 1 | 0..1 |
| lastModifiedTime | m2m:timestamp | 1 | 0..1 |
| labels | m2m:labels | 0..1 | 0..1 |
| announceTo | list of xs:anyURI | 0..1 | 0..1 |
| announcedAttribute | list of xs:NCName | 0..1 | 0..1 |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 | missing |
| mgmtDefinition | m2m:mgmtDefinition | - | 1 |
| objectIDs | m2m:listOfURIs | - | 0..1 |
| objectPaths | m2m:listOfURIs | - | 0..1 |
| description | xs:string | - | 0..1 |

Likewise, for the m2m:announcedMgmtResource, m2m:announcedResource are used as the extension base. However, there are differences in multiplicity for some elements between those two data types. These shall be the same. No change required in the XSD.

| Element Path | Element Data Type | Multiplicity |
| --- | --- | --- |
|  |  | m2m:announcedResource | m2m:announcedMgmtResource |
| @resourceName | xs:NCName | 1 | 1 |
| resourceType | m2m:resourceType | 1 | 1 |
| resourceID | m2m:ID | 1 | 1 |
| parentID | m2m:nhURI | 1 | 1 |
| creationTime | m2m:timestamp | 1 | 0..1 |
| lastModifiedTime | m2m:timestamp | 1 | 0..1 |
| labels | m2m:labels | 0..1 | 0..1 |
| accessControlPolicyIDs | m2m:acpType | 0..1 | 0..1 (m2m:announcedResource needs correction. This is mandatory in the announced variant.) |
| expirationTime | m2m:timestamp | 1 | 0..1 |
| link | xs:anyURI | 1 | missing |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 | missing |
| mgmtDefinition | m2m:mgmtDefinition | - | 1 |
| objectIDs | m2m:listOfURIs | - | 0..1 |
| objectPaths | m2m:listOfURIs | - | 0..1 |
| description | xs:string | - | 0..1 |

### -----------------------Start of change 1---------------------------------------------

#### m2m:mgmtResource

This data type is used as base type of all <mgmtObj> specializations specified in Annex D. It includes the attributes commonly used by all <mgmtObt> resource type specializations.

It consists of the common attributes included in m2m:announceableResource as defined Table 6.3.6-2 and the additional common attributes shared by all <mgmtObj> specializations shown in Table 6.3.5.34-1.

Table 6.3.5.34-1: Type Definition of m2m:mgmtResorce

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| @resourceName | xs:NCName | 1 | common attributes as defined in m2m:announceableResource, see Table 6.3.6-2 |
| resourceType | m2m:resourceType | 1 |  |
| resourceID | m2m:ID | 1 |  |
| parentID | m2m:nhURI | 1 |  |
| accessControlPolicyIDs | m2m:acpType | 0..1 |  |
| creationTime | m2m:timestamp | 1 |  |
| expirationTime | m2m:timestamp | 1 |  |
| lastModifiedTime | m2m:timestamp | 1 |  |
| labels | m2m:labels | 0..1 |  |
| announceTo | list of xs:anyURI | 0..1 |  |
| announcedAttribute | list of xs:NCName | 0..1 |  |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 |  |
| mgmtDefinition | m2m:mgmtDefinition | 1 |  |
| objectIDs | m2m:listOfURIs | 0..1 |  |
| objectPaths | m2m:listOfURIs | 0..1 |  |
| description | xs:string | 0..1 |  |

NOTE: objectAttribute is defined in the specializations of mgmtObj. See Annex D.

#### m2m:announcedMgmtResource

This data type is used as base type of the announced variants of announceable <mgmtObj> specializations specified in Annex D. It includes the attributes commonly used by all announced <mgmtObj> resource type specializations. Note that some specializations of the <mgmtObj> resource are announceable while others are not announceable.

It consists of the common attributes included in m2m:announcedResource as defined Table 6.3.6-2 and the additional common attributes shared by all announced <mgmtObj> specializations shown in Table 6.3.5.35-1.

Table 6.3.5.35-1: Type Definition of m2m:announcedMgmtResorce

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| @resourceName | xs:NCName | 1 | common attributes as defined in m2m:announcedResource, see Table 6.3.6-2 |
| resourceType | m2m:resourceType | 1 |  |
| resourceID | m2m:ID | 1 |  |
| parentID | m2m:nhURI | 1 |  |
| accessControlPolicyIDs | m2m:acpType | 1 |  |
| creationTime | m2m:timestamp | 1 |  |
| expirationTime | m2m:timestamp | 1 |  |
| lastModifiedTime | m2m:timestamp | 1 |  |
| labels | m2m:labels | 0..1 |  |
| link | xs:anyURI | 1 |  |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 |  |
| mgmtDefinition | m2m:mgmtDefinition | 1 |  |
| objectIDs | m2m:listOfURIs | 0..1 |  |
| objectPaths | m2m:listOfURIs | 0..1 |  |
| description | xs:string | 0..1 |  |

NOTE: objectAttribute is defined in the specializations of mgmtObj. See Annex D.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### Universal and Common attributes

TS-0001 [6] defines a number of Universal Attributes (which appear in all resources) and Common Attributes (which appear in more than one resource and have the same meaning whenever they do appear). The type and values shall be supported according to the description given inTable 6.3.6-1.

If a Resource is represented as an XML document then the resource attributes (if present) appear in the order listed in this table. They appear before any resource-specific attributes.

Table 6.3.6-1: Universal and Common Attributes

| Attribute Name | Data Type | Value restrictions and Notes |
| --- | --- | --- |
| resourceType | m2m:resourceType | This attribute is only determined at creation time by the hosting CSE |
| resourceID | m2m:ID | This attribute is determined at creation time by the hosing CSE and used for non hierarchical addressing method |
| parentID | m2m:nhURI | This attribute is determined by the hosting CSE and specified in all resource types.For <CSEBase> however, the value of this attribute shall be an empty string. |
| creationTime | m2m:timestamp | This attribute is determined by the hosting CSE when the resource is locally created |
| lastModifiedTime | m2m:timestamp | This attribute is determined by the hosting CSE when the addressed resource is modified by means of the UPDATE operation |
| labels | m2m:labels | Absence of this attribute means there are no labels |
| accessControlPolicyIDs | m2m:acpType | accessControlPolicyIDs |
| expirationTime | m2m:timestamp | expirationTime |
| link | xs:anyURI | Absence of this attribute means that this is not an announced resource |
| announceTo | list of xs:anyURI | Absence of this attribute means that this is not an announced resource |
| announcedAttribute | list of xs:NCName | Absence of this attribute means that this is not an announced resource |
| stateTag | xs:nonNegativeInteger | This attribute is determined by the hosting CSE. When a resource is created this counter is set to '0' and it will be incremented on every modification of the resource |
| resourceName | xs:NCName |  |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | dynamicAuthorizationConsultationIDs |
| creator | m2m:ID | The AE-ID or CSE-ID of the entity which created the resource containing this attribute. |

Table 6.3.6-2 describes some complex types that group together the universal and common attributes, to be used by Resource Type definitions. Note that stateTag and creator only appear in a limited number of resource types, and therefore are not included in these definitions, instead they are declared in the corresponding XSD files of the resources that support them.

Table 6.3.6-2: Complex Data Types declaring groups of resource common attributes

| XSD type name | Child Elements | Child Element Datatype | Multiplicity | Description |
| --- | --- | --- | --- | --- |
| m2m:resource | @resourceName | xs:NCName | 1 |  |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | m2m:nhURI | 1 |  |
|  | creationTime | m2m:timestamp | 1 |  |
|  | lastModifiedTime | m2m:timestamp | 1 |  |
|  | labels | m2m:labels | 0..1 |  |
| m2m:regularResource | @resourceName | xs:NCName | 1 | Declares the universal / common attributes included in the non-announceable resource types. |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | m2m:nhURI | 1 |  |
|  | accessControlPolicyIDs | m2m:acpType | 0..1 |  |
|  | creationTime | m2m:timestamp | 1 |  |
|  | expirationTime | m2m:timestamp | 1 |  |
|  | lastModifiedTime | m2m:timestamp | 1 |  |
|  | labels | m2m:labels | 0..1 |  |
|  | dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 |  |
| m2m:announceableResource | @resourceName | xs:NCName | 1 | Declares the universal / common attributes included in the majority of announceable resource types. |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | xs:anyURI | 1 |  |
|  | accessControlPolicyIDs | m2m:acpType | 0..1 |  |
|  | creationTime | m2m:timestamp | 1 |  |
|  | expirationTime | m2m:timestamp | 1 |  |
|  | lastModifiedTime | m2m:timestamp | 1 |  |
|  | labels | m2m:labels | 0..1 |  |
|  | announceTo | list of xs:anyURI | 0..1 |  |
|  | announcedAttribute | list of xs:NCName | 0..1 |  |
|  | dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 |  |
| m2m:announcedResource | @resourceName | xs:NCName | 1 | Declares the universal / common attributes in the announced variant of the preceding resources |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | m2m:nhURI | 1 |  |
|  | creationTime | m2m:timestamp | 1 |  |
|  | lastModifiedTime | m2m:timestamp | 1 |  |
|  | labels | m2m:labels | 0..1 |  |
|  | accessControlPolicyIDs | m2m:acpType | 1 |  |
|  | expirationTime | m2m:timestamp | 1 |  |
|  | link | xs:anyURI | 1 |  |
|  | dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 |  |
| m2m:subordinateResource | @resourceName | xs:NCName | 1 | Declares the universal / common attributes included in the non-announceable resource types without accessControlPolicyIDs |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | m2m:nhURI | 1 |  |
|  | creationTime | m2m:timestamp | 1 |  |
|  | lastModifiedTime | m2m:timestamp | 1 |  |
|  | labels | m2m:labels | 0..1 |  |
|  | expirationTime | m2m:timestamp | 1 |  |
| m2m:announceableSubordinateResource | @resourceName | xs:NCName | 1 | Declares the universal / common attributes used by resource types that are subordinate children of other resources |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | xs:anyURI | 1 |  |
|  | creationTime | m2m:timestamp | 1 |  |
|  | lastModifiedTime | m2m:timestamp | 1 |  |
|  | labels | m2m:labels | 0..1 |  |
|  | expirationTime | m2m:timestamp | 1 |  |
|  | announceTo | list of xs:anyURI | 0..1 |  |
|  | announcedAttribute | list of xs: NCName | 0..1 |  |
| m2m:announcedSubordinateResource | @resourceName | xs:NCName | 1 | Declares the common / universal attributes used in the announced variants of the subordinate resource types |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | m2m:nhURI | 1 |  |
|  | creationTime | m2m:timestamp | 1 |  |
|  | lastModifiedTime | m2m:timestamp | 1 |  |
|  | labels | m2m:labels | 0..1 |  |
|  | expirationTime | m2m:timestamp | 1 |  |
|  | link | xs:anyURI | 1 |  |

NOTE: In the above table, names of XML schema attributes are prefixed with a "@" character to differentiate these from Resource attribute names. The "@" character is not part of the actual attribute name.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?