| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#24 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-07-22 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | It needs to be defined how <flexContainer> specializations should be represented as children of its applicable parent resource types and in the primitive Content parameter in related XML schema definitions in order to enable schema validation of data that includes instantiations of such specializations. The solution also implies some other corrections and clarifications related to the Content primitive Parameter. |
| CR against: Release* | R2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / <Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.6.0 |
| Clauses/Sub Clauses* | 6.3.5.25, 7.5.2, 7.4.29 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR addresses issues related to handling of <flexContainer> specializations in the XSD of schema elements which shall allow to include <flexContainer> specializations as their children. It is proposed to incorporate <flexcontainer> specializations as children by means of the XML wildcard element xs:any.

The use of  XML wildcard element has some consequences on schema validation procedures which need to be understood and clarified in TS-0004. Therefore the following discussion starts with a review of some important concepts related to XML schema definition.

Each of the current XSD files referenced in TS-0004 includes one or more Global Element Declaration(s) (cf. Annex F of TS-0004).

XML instances of any of these Global Elements can be included into the Content parameter of request or response primitives, either directly or as a child element of some parent Global Element.

A schema-valid XML object includes the name of its respective Global Element as “root element” starting with the namespace prefix of the targetNamespace defined in the schema (e.g. prefix  m2m:).

As an example, consider the file CDT-AE-v2_6_0.xsd, which includes two Global Element Declarations, AE and AEAnnc. A schema-valid XML instantiation compliant with CDT-AE-v2-6_0.xsd must include either a m2m:AE or a m2m:AEAnnc root element.

Global schema elements (i.e. parent elements) can have other global schema elements as children (or even the same global element, i.e. m2m:container can have a m2m:container as child).

In the current oneM2M XSD, this applies to any resource type which can have child resources. It also applies to the m2m:resourceWrapper  Global Element defined in CDT-responsePrimitive-v2_6_0.xsd and a few other Global Elements which can included into the Content primitive parameter, e.g. m2m:aggregatedResponse (as defined in clause 7.5.2 of TS-0004).

In order to enable schema-validation, any of these XSD files must include explicit references to each applicable child resource defined in other XSD file(s).

This is illustrated in the following excerpt of the file CDT-container-v2_6_0.xsd:

<xs:schema targetNamespace="http://www.onem2m.org/xml/protocols" xmlns:m2m="http://www.onem2m.org/xml/protocols"
	elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">
	<xs:include schemaLocation="CDT-commonTypes-v2_6_0.xsd" />
	<xs:include schemaLocation="CDT-contentInstance-v2_6_0.xsd" />
	<xs:include schemaLocation="CDT-subscription-v2_6_0.xsd" />
	<xs:include schemaLocation="CDT-semanticDescriptor-v2_6_0.xsd" />

	<xs:element name="container">
		<xs:complexType>
			<xs:complexContent>
				<xs:extension base="m2m:announceableResource">
					<xs:sequence>
						<!-- Common Attribute, specific to <container> -->
						<xs:element name="stateTag" type="xs:nonNegativeInteger" />
						<xs:element name="creator" type="m2m:ID" minOccurs="0" />
						<!-- Resource Specific Attributes -->
						<xs:element name="maxNrOfInstances" type="xs:nonNegativeInteger" minOccurs="0" />
						<xs:element name="maxByteSize" type="xs:nonNegativeInteger" minOccurs="0" />
                                      ...

						<!-- Child Resources -->
						<xs:element name="latest" type="xs:anyURI" />
						<xs:element name="oldest" type="xs:anyURI" />
						<xs:choice minOccurs="0" maxOccurs="1">
							<xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />
							<xs:choice minOccurs="1" maxOccurs="unbounded">
								<xs:element ref="m2m:contentInstance" />
								<xs:element ref="m2m:container" />
								<xs:element ref="m2m:subscription" />
								<xs:element ref="m2m:semanticDescriptor" />
							</xs:choice>
						</xs:choice>
					</xs:sequence>
				</xs:extension>
			</xs:complexContent>
		</xs:complexType>
	</xs:element>
      ….
</xs:schema>

Resource types <container>, <CSEBase>, <remoteCSE>, and <AE>  as well as the resourceWrapper Global Element need to be enabled to contain <flexContainer> specializations as their children.

It is impractical to include the names of all flexContainer specializations explicitly into their potential parent Global Elements since its number will be growing with time. Also it can be expected that CSE implementations will only support a dedicated subset of flexContainer specializations, if any.

The current definition of datatype m2m:primitiveContent which is applied to CDT-requestPrimitive-v2_6_0.xsd the Content primitive parameter gives an example how it is possible to insert XML wildcard elements with yet unspecified underlying XSD.

<xs:complexType name="primitiveContent" mixed=”true”>
	<xs:sequence>
		<xs:any namespace="http://www.onem2m.org/xml/protocols" processContents="lax" minOccurs="0" maxOccurs="unbounded" />
	</xs:sequence>
</xs:complexType>

This datatype definition allows to include a sequence of XML elements that have a root element starting with an m2m: prefixed name. Other namespace prefixes are not allowed. The processContents attribute set to "lax" means that schema-validation is skipped if the schema definition of the given Global Element is not found.

This means that any strings as shown in the following example will be accepted as schema-valid with respect to the current definition of a response primitive in CDT-responsePrimitive-v2_6_0.xsd:

<m2m:responsePrimitive>
        <responseStatusCode>1000</responseStatusCode>
        <requestIdentifier>ABC123</requestIdentifier>
        <primitiveContent>
              <m2m:arbitraryname>arbitrary string value</m2m: arbitraryname >
        </primitiveContent>
</m2m:aggregatedResponse>

This example reveals following issues with the present definition of m2m:primitiveContent, which need to be clarified in TS-0004:

- This current definition does not allow to validate a primitive which contains “raw data” in error response messages as specified in clauses 7.2.1.2 and 7.5.2 of TS-0003.

- Any garbage that starts with an m2m: prefixed XML root element would pass schema-validation with respect to the XSD that defines the responsePrimitive Global Element (the same applies to requestPrimitive) unless there exists an XSD which defines a Global Element with that name and schema validation is explicitly mandated and performed for this element.

- We need to enable validation of XML objects defined in other namespace domains. Currently, XSD using the hd: prefix already exists (using sec: prefix on the TEF interface is being considered).

The changes listed below address the above issues.

Furthermore it is proposed to enable <flexContainer>  specializations as children of its applicable parent resource types and in the primitive Content parameter by reusing the xs:any wildcard element approach.

Clarifications also needs to be added how schema validation should be handled for wildcarded children.

It needs to be defined how <flexContainer>  specializations should be represented as children of its applicable parent resource types and in the primitive Content parameter in related XML schema definitions in order to enable schema validation of data that includes instantiations of such specializations

Any XML data, representing a global schema element which starts with a  well-defined namespace identifier, i.e. currently the prefixes “m2m:” and “hd:” needs to be schema valid against the schema which defines this global element.

It is generally not sufficient to perform validation against a schema definition which includes a given global element as a child of another global element.

Revision R01:

- Proposed changes affecting the XSD only have been removed (changes 1 to 3).

- Part of the text proposed for clause 7.4.9 (flexContainer) which describes specifics of the XSD implementation and impact on schema validation has been removed

- It needs to be further investigated to what extent the use of XML substitution groups can help to simplify the XSD, while resolving the issues raised in the above discussion, and keeping compatibilty with the current schema.  It is expected that these changes will not have a significant impact on TS-0004.

-----------------------Start of change 4---------------------------------------------

#### m2m:resourceWrapper

This data type is used for the m2m:resource Global Element of the Content primitive parameter as defined in clause 7.5.2. It allows insertion of Global Elements prefixed with the m2m: namespace identifier, or of Global Elements defined in another namespace.

Table 6.3.5.25-1: Type Definition of m2m:resourceWrapper

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| m2m:<resourceType> {other namespace identifier}:<resourceType> | (anonymous) | 1 | A representation of a Resource with specific type as described in clause 7.4 |
| URI | xs:anyURI | 1 | Hierarchical URI of the resource |

-----------------------End of change 4---------------------------------------------

-----------------------Start of change 5---------------------------------------------

### Elements contained in the Content primitive parameter

Clauses 7.2.1.1 and 7.2.1.2 enumerate the forms that the Content primitive parameter takes in various Request and Response cases. Note that the Content primitive parameter is denoted as primitiveContent in both, CDT-requestPrimitive-v2_6_0.xsd and CDT-responsePrimitive-v2_6_0.xsd.

This clause details the Objects (elements) used in some of these cases. in the tables below.

The following elements are defined for use in the Content parameter of a request:

Table 7.5.2-1: Elements used for request content

| Element Name | Applicable Operations | Data Type | Defined in |
| --- | --- | --- | --- |
| m2m:<resourceType> {other namespace identifier}:<resourceType> | C U | m2m:<resourceType> {other namespace identifier}:<resourceType> | CDT-<resourceType>-v2_6_0.xsd |
| m2m:notification | N | m2m:notification | CDT-notification-v2_6_0.xsd |
| m2m:aggregatedNotification | N | m2m:aggregatedNotification | CDT-notification-v2_6_0.xsd |
| m2m:securityInfo | N | m2m:securityInfo | CDT-notification-v2_6_0.xsd |
| m2m:attributeList | R | m2m:attributeList | CDT-requestPrimitive-v2_6_0.xsd |
| m2m:responsePrimitive | N | m2m:responsePrimitive | CDT-responsePrimitive-v2_6_0.xsd |

The following elements are defined for use in the Content parameter of a response sent in reply to a request message with Operation and Result Content (rcn) parameters as given in the column "Applicable Operations" (the settings of the Result Content parameters are defined in clause 6.3.3.2.7; NP means the rcn parameter is not present)::

Table 7.5.2-2: Elements used for response content

| Element Name | Applicable Operations/rcn | Data Type | Element is Defined in |
| --- | --- | --- | --- |
| m2m:<resourceType> {other namespace identifier}:<resourceType> NOTE 6 | C/1, 7,NP R/1,4,5,6,7,NP U/1,NP D/1,NP See NOTE1 | m2m:<resourceType> {other namespace identifier}:<resourceType> | CDT-<resourceType>-v2_6_0.xsd |
| m2m:resource | C/3 | m2m:resourceWrapper | CDT-responsePrimitive-v2_6_0.xsd |
| m2m:URIList | R/NP See NOTE 2 | m2m:listOfURIs | CDT-responsePrimitive-v2_6_0.xsd |
| m2m:aggregatedResponse | C R U D See NOTE 3 | m2m:aggregatedResponse | CDT-responsePrimitive-v2_6_0.xsd |
| none (raw data) | C/2 See NOTE 4 | none (raw data) |  |
| m2m:securityInfo | N/NP | m2m:securityInfo | CDT-responsePrimitive-v2_6_0.xsd |
| NOTE 1: The case rcn = 7 applies to Retrieve operation only (R/7). It retrieves the original resource in case the To parameter points to an announced resource. NOTE 2: This applies to ordinary retrieve operation when the Result Content parameter is not present and for discovery operation. For discovery, the format of the URIList elements (structured, unstructured) depends on the Discovery Result Type parameter setting (see clause 6.3.3.2.8). NOTE 3: This applies to CRUD operations on a <fanOutPoint> child resource of a <group> parent resource. The Content parameter of each response primitive included in aggregatedResponse is set as given in one of the other rows of this table. NOTE 4: This also applies to the response ("acknowledgement") to non-blocking requests in asynchronous mode for any CRUD operation. NOTE 5: Raw data could e.g. be included as debugging information into error responses. NOTE 6: “{other namespace identifier}” refers to a namespace other than m2m: |

The XML schema definition of the Content primitive parameter (i.e. datatype m2m:primitiveContent) allows to include XML wildcard elements. An XML representation of the  Content primitive parameter shall include a root element which is associated with an XSD Global Element. The root element shall be prefixed with a namespace prefix identifier (e.g. m2m:) specified in the associated XSD which defines the respective Global Element. The Content primitive parameter allows to include namespaces other than m2m:.

-----------------------End of change 5---------------------------------------------

-----------------------Start of change 6---------------------------------------------

### Resource Type <flexContainer>

#### Introduction

This resource represents a customizable container for data instances. It is a template for the definition of flexible specializations of data containers.

The detailed description can be found in clause 9.6.35 in TS-0001 [6].

There are multiple specializations of  <flexContainer> specified by oneM2M. Each of these specializations has its own schema file. There is no separate schema file just for <flexContainer>, however the XML schema types for the specializations all conform to the pattern described in this clause. The XSD of <flexContainer> specializations may use a targetNamespace other than the one identified by the m2m: prefix. Specializations of  <flexContainer> which employ the namespace prefix m2m: are defined in Annex J. Specialization of  <flexContainer> which employ the namespace prefix hd: for Home Domain use cases are specified in TS-0025 [x].

The following resource types are allowed to include <flexContainer> specializations as children: <CSEBase>, <AE>, <remoteCSE> and <container>.

Table 7.4.37.1-1: Universal/Common Attributes of <flexContainer> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| stateTag | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |
| creator | O | NP |
| dynamicAuthorizationConsultationIDs | O | O |

Table 7.4.37.1-2: Resource Specific Attributes of <flexContainer> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| containerDefinition | M | NP | xs:anyURI | No default |
| ontologyRef | O | O | xs:anyURI | No default |
| [customAttribute] | O | O | Name and data type are defined in the specification document or XSD file identified by the value of containerDefinition attribute. | No default. |

Table 7.4.37.1-3: Child Resources of <flexContainer> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <semanticDescriptor> | [variable] | 0..n | Clause 7.4.34 |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <container> | [variable] | 0..n | Clause 7.4.6 |
| <flexContainer> | [variable] | 0..n | Clause 7.4.37 |

-----------------------End of change 6---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?