| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#24 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-07-10 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | This CR introduces the binding of the new security related primitive parameters for Rel-2 |
| CR against: Release* | R2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / <Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009 V2.5.0 |
| Clauses/Sub Clauses* | 6.2.2.2, 6.4.x (new subclause), 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR specifies the binding of following primitive parameters introduced for Rel-2:

Request Primitive:   Tokens, Token IDs, LocalTokenIDs, Token Request Indicator

Response Primitive: Assigned Token Identifiers Token Request Information

R01 changes:

- Add Role IDs request primitive parameter to list of elements mapped into the query string

- Tokens mapped to HTTP authorisation header, example moved into that section

- Changed description of mapping  Assigned Token Identifiers into  X-M2M-ATI header

### -----------------------Start of change 1---------------------------------------------

#### 6.2.2.2	Query component

The query component (e.g. query-string) may include  the optional primitive parameters listed in Table 6.2.2-1 compliant with RFC 7230 [1]. Each applicable request primitive parameters and elements of Filter Criteria parameter shown in Table 6.2.2-1 shall be represented as pair of field-name and value in query-string. Multiple such pairs shall be concatenated with an ampersand ‘&’ character used as separator between two pairs.

Table 6.2.2-1 also shows the permitted multiplicity of occurrence of field names in the query-string. Multiplicity ‘0..1’ means that a  parameter  is optional and can occur at most once. Parameters with multiplicity ‘0..n’, may occur multiple times in the query-string in the form of  <query field name> = value.  For example, if the resourceType element of the Filter Criteria parameter is represented by a list of 3 values ‘2 3 4’ (see clause 6.3.4.7 in TS-0004 [3]), it would be mapped to ty=2+3+4 in the query-string. At the receiver side, this query string can be reverted back into the list type of representation. The same representation shall be applied for multiple occurrences of contentType and labels elements.

The ‘attribute’ element of the Filter Criteria request primitive parameter consists of two elements, name and value, which in XML notation would look for example as follows in case of multiplicity 2 (see clause 6.2.4.8 in TS-0004 [3]):

<attribute>

<name>attname1</name>

<value>attvalue1</value>

</attribute>

<attribute>

<name>attname2</name>

<value>attvalue2</value>

</attribute>

Each name (e.g. attname1 and attname2) shall represent a valid resource attribute name of the resource types indicated in the ty field of the query-string. The sequence of attribute elements as shown in the above example will be mapped into the query-string as attname1=attvalue1&attname2=attvalue2. The attribute names (i.e. attname1 and attname2 in the above example) shall be expressed in the form of short names as defined in clause 8.2.3 of TS-0004 [3].  Note that the <attribute> tag of the XML representation is omitted in the HTTP binding.

Examples of valid Request-Target representations are the following:

Example 1): Request-Target for ‘nonBlockingRequestSynch

Primitive parameters: 	To:						/CSE1234/RCSE78/container234        (SP-Relative-Resource-ID)

Response Type:	      responseType = 1     						(nonBlockingRequestSynch)

Result Persistence:	P1Y2M3DT10H1M0S	Request-Target:			/CSE1234/RCSE78/container234?rt=1&rp=P1Y2M3DT10H1M0S

Example 2):  Request-Target for Discovery

When the entity wants to discover container resources where the creator attribute has the value ‘Sam’:

Primitive parameters:	To:						/CSE1234/RCSE78

Filter Criteria:		resourceType = 3           (container)

attribute name:  creator

attribute value: Sam

filterUsage = discovery

Request-Target:			/CSE1234/RCSE78?ty=3&cr=Sam&fu=1

Example 3): Semantic Discovery

The entity wants to discover resources whose semantic description stored in the descriptor attribute of a <semanticDescriptor> child resource fulfils the semantic filter specified in SPARQL. In this case, the semantic  descriptor of the resource to discover has to contain information about a Thing of type Car based on the concept defined in the “myOnt” ontology.

Due to the use of reserved characters in SPARQL, the semanticsFilter requires “percent-encoding” [9].

Primitive parameters:		To:						/CSE1234/RCSE78

Filter Criteria: 	semanticsFilter = 
PREFIX rdf: http://www.w3.org/1999/02/22-rdf-syntax-ns#
PREFIX myOnt: http://www.onem2m.org/ontology/myontology#
SELECT ?car WHERE { ?car  rdf:type myOnt:Car }

Request-Target:    /CSE1234/RCSE78?smf=PREFIX%20rdf%3A%20%3Chttp%3A%2F%2

Fwww.w3.org%2F1999%2F02%2F22-rdf-syntax-ns%23%3E%20PREFI                                                                                                X%20myOnt%3A%20%3Chttp%3A%2F%2Fwww.onem2m.org%2Fonto                                                                                               logy%2Fmyontology%23%3E%20SELECT%20%3Fcar%20WHERE%20                                                                                              %7B%20%3Fcar%20%20rdf%3Atype%20myOnt%3ACar%20%7D

Table 6.2.2.2-1: oneM2M request parameters mapped as query-string field

| Request Primitive Parameter | Query Field Name | Multiplicity | Note |
| --- | --- | --- | --- |
| Response Type | rt | 0..1 | responseType element of data type responseTypeInfo (cf. clause 6.3.4.29 of TS-0004 [3]) |
| Result Persistence | rp | 0..1 |  |
| Result Content | rcn | 0..1 |  |
| Delivery Aggregation | da | 0..1 |  |
| createdBefore | crb | 0..1 | filterCriteria condition |
| createdAfter | cra | 0..1 | filterCriteria condition |
| modifiedSince | ms | 0..1 | filterCriteria condition |
| unmodifiedSince | us | 0..1 | filterCriteria condition |
| stateTagSmaller | sts | 0..1 | filterCriteria condition |
| stateTagBigger | stb | 0..1 | filterCriteria condition |
| expireBefore | exb | 0..1 | filterCriteria condition |
| expireAfter | exa | 0..1 | filterCriteria condition |
| labels | lbl | 0..n | filterCriteria condition |
| resourceType | ty | 0..n | filterCriteria condition |
| sizeAbove | sza | 0..1 | filterCriteria condition |
| sizeBelow | szb | 0..1 | filterCriteria condition |
| contentType | cty | 0..n | filterCriteria condition |
| limit | lim | 0..1 | filterCriteria condition |
| attribute | atr | 0..n | filterCriteria condition |
| filterUsage | fu | 0..1 | filterCriteria condition |
| semanticsFilter | smf | 0..n | filterCriteria condition, shall use “percent-encoding” [9] where required, see Example 3) |
| Discovery Result Type | drt | 0..1 |  |
| Role IDs | rids | 0..n |  |
| Token IDs | tids | 0..n |  |
| LocalTokenIDs | ltids | 0..n |  |
| Token Request Indicator | tqi | 0..n |  |

For partial Retrieve request primitives, the To parameter may include the name of a single attribute separated by a ‘#’ character from the resource ID. If multiple resource attributes are to be retrieved with a partial retrieve request primitive, these attributes are included in form of an attributeList object (as specified in clause 6.3.4.9 of TS-0004 [3] with empty values) in the Content parameter.

In both cases, the short resource attribute name(s) shall be included into the fragment component of request-target, i.e. it shall follow any required query-string separated by ‘#’ character. If more than a single attribute name is included into the fragment component, these shall be separated by a ‘+’ character.

For example, if three resource attributes with long names resourceID, labels and requestReachability are indicated in the Content primitive parameter, the query component atrl=ri+lbl+rr is attached to the request-target. In case just a single attribute “rr” is indicated in the To parameter separated by ‘#’ character, the query component atrl=rr is attached to the request-target. The ‘#’ character and following attribute name shall be omitted from the path component of the request line.

At the HTTP server side, the reverse operation shall take place, when constructing the retrieve request primitive from the receive HTTP request message. Single attribute names in the query component may either be mapped back into the To parameter following a ‘#’ character, or included into the Content parameter using the attributeList format with just a single list element included. Multiple attributes shall be included into the Content parameter as specified in [3].

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### 6.4.x	X-M2M-ATI

The X-M2M-ATI header in a HTTP response message shall be mapped to the Assigned Token Identifiers parameter of response primitives and vice versa.

The format of the X-M2M-ATI header shall be represented as a sequence of  lti-value:tkid-value pairs separated by a colon “:’ and  multiple pairs appended with ‘+’ character.

For example, the header looks as follows:

X-M2M-ATI: lti-value1:tkid-value1 + lti-value2:tkid-value2 + …

if the XML representation of the Assigned Token Identifiers parameter is given as (using short element names):

<ati>

<ltia>

<lti>lti-value1</lti>

<tkid>tkid-value1</tkid>

</ltia>

<ltia>

<lti>lti-value2</lti>

<tkid>tkid-value2</tkid>

</ltia>

…

</ati>

The datatype m2m:dynAuthlocalTokenIdAssignments of the Assigned Token Identifiers parameter is defined in clause 6.3.5.43 of TS-0004 [3].

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

## 6.5	Message-body

Message-body shall be mapped to the Content parameter of request and response primitives, and vice versa, if applicable. This applies to the Content parameter of all primitives with the following exceptions:

- For partial Retrieve request primitives. Attributes contained in the Content parameter of a Retrieve request primitive shall be mapped to the fragment component of request-target, as specified in clause 6.2.2.2, and vice versa.

- A Token Request Information parameter included in a reponse primitive shall be mapped into the message-body either as a XML or JSON serialized object. The Content-Type and Content-Length headers shall be set compliant with the data representation (i.e.  Content-Type: application/xml or application/json depending on the serialization format). Note that the Token Request Information parameter is used in oneM2M error response primitives (X-M2M-RSC: 4103 “ACCESS DENIED”) only, which do not carry any other primitive content.

Error response messages which include the Token Request Information parameter in the Message-Body shall not include any debugging  information.

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4---------------------------------------------

### 6.4.y	Authorization

If a request primitive includes a Tokens parameter it shall be mapped to the Authorization header.

The Tokens primitive parameter is represented as a space separated list of  JSON Web Signature (JWS) and JSON Web Encryption (JWE) strings in Compact Serialization format of datatype m2m:dynAuthJWT as defined in clause 6.3.3 of TS-0004 [3].

When mapped into the Authorization header, each individual token in the Tokens primitive parameter shall be separated by ‘+’ character.

For example, if the Tokens parameter consists of a list of two JWS/JWE Tokens,

eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiLA0KIC.dBjftJeZ4CVP  eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiLA0KIC.dBjftJeZ4CVP.5eym8TW_c8SuK.SdiwkIr3a.XFBoMYUZo

the Authorization header looks as follows

Authorization: eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiLA0KIC.dBjftJeZ4CVP+ eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiL

A0KIC.dBjftJeZ4CVP.5eym8TW_c8SuK.SdiwkIr3a.XFBoMYUZo

The line break in the above example is for illustrative purposes and shall not be included into the Authorization header.

### -----------------------End of change 4---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?