| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#24 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-07-14 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Cleanup on parent/child relationship for announced resources; Alignment with ARC-2016-0349 (R2) 0350 (R1) |
| CR against: Release* | R2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / <Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.6.0 |
| Clauses/Sub Clauses* | 7.4.3, 7.4.4, 7.4.26 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

At the 2nd interoperability test event, an issue has been raised about the presence of a <node> resource as child resource of a <remoteCSE> resource, see issue #5 in TP-2016-0118R01.

In the discussions it was noted that the XSD of <remoteCSE> (i.e. CDT-remoteCSE-v2_6_0) does not show <node> resource as child of remoteCSE (which is in alignment with Table 7.4.4.1 4: Child resources of <remoteCSE> resource), but it has nodeAnnc has child resource of remoteCSEAnnc.

Further discussion has led to a major CR to TS-0001 which corrects the assignment of announced resource types to its parent resources.

This CR shall provide alignment of TS-0004 with TS-0001 taking into account the mentioned CR ARC-2016-0349 for Rel-2 (and CR ARC-2016-0349, R1 mirror, for Rel-1).

This initial version of CR to TS-0004 provides a first overview on the expected changes.

The final revision of this CR requires alignment with the eventually agreed revision of ARC-2016-0349.

Issues addressed in this CR:

Change 1:  Lists the changes required in the XSD (otherwise no impact on TS-0004)

Change 2:  Addition of  <remoteCSEAnnc> as child resource of <CSEBase>  in clause 7.4.3

Change 3:  Update of list of child resources of <remoteCSE> in clause 7.4.4,

Correction to multiplicity of <schedule> child resource

Change 4: Clarifications to clause 7.4.26	“Announced resource types”

TS-0004 does not define the parent-child relationship for announced resource types. This information is provided in  Table 9.6.26.1-1 of TS-0001.  A reference to this table is included into clause 7.4.26.  A general cleanup of this clause is proposed.

Revision R01:

- Removed trafficCharacteristicsAnnc

- @resourceName:  presence changed from “O” to “NP” for Create operation of announced resource types

- Minor editorials fixed at presentation of the initial version

-----------------------Start of change 1---------------------------------------------

Changes affecting the XSD:

CDT-CSEBase-v2_6_0.xsd:     add <remoteCSEAnnc> child resource

CDT-remoteCSE-v2_6_0.xsd:  update child resource of m2m:remoteCSE as in 7.4.4.1 4

The announced Global Elements m2m:xxxxAnnc of the following files need to be aligned with the child resources listed in Table 9.6.26.1-1 of TS-0001 (after update ARC-2016-0349R0x has been agreed):

CDT-remoteCSE-v2_6_0.xsd

CDT-accessControlPolicy-v2_6_0.xsd

CDT-AE-v2_6_0.xsd

CDT-container-v2_6_0.xsd

CDT-contentInstance-v2_6_0.xsd

CDT-schedule-v2_6_0.xsd

CDT-locationPolicy-v2_6_0.xsd

CDT-group-v2_6_0.xsd

CDT-node-v2_6_0.xsd

CDT-semanticDescriptor-v2_6_0.xsd

CDT-timeSeries-v2_6_0.xsd

CDT-timeSeriesInstance-v2_6_0.xsd

-----------------------End of change 1---------------------------------------------

-----------------------Start of change 2---------------------------------------------

### Resource Type <CSEBase>

#### Introduction

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE. The detailed description can be found in clause 9.6.3 in TS-0001 [6]).

Table 7.4.3.1-1: Data type definition of <CSEBase> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| CSEBase | CDT-CSEBase-v2_6_0.xsd |  |

The value of the parentID attribute for the <CSEBase> resource shall be  an empty string since the <CSEBase> resource does not have a parent.

Table 7.4.3.1-2: Resource Specific Attributes of <CSEBase> resource

| Attribute Name | Data Type | Default Value and Constraints |
| --- | --- | --- |
| cseType | m2m:cseTypeID | No default |
| CSE-ID | m2m:ID | No default |
| supportedResourceType | list of m2m:resourceType | No default |
| pointOfAccess | m2m:poaList | No default |
| nodeLink | xs:anyURI | No default |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | No default |

Table 7.4.3.1-3: Child resources of <CSEBase> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <remoteCSE> | [variable] | 0..n | Clause 7.4.4 |
| <remoteCSEAnnc> | [variable] | 0..n | Clause 7.4.4 |
| <node> | [variable] | 0..n | Clause 7.4.18 |
| <AE> | [variable] | 0..n | Clause 7.4.5 |
| <container> | [variable] | 0..n | Clause 7.4.6 |
| <group> | [variable] | 0..n | Clause 7.4.13 |
| <accessControlPolicy> | [variable] | 0..n | Clause 7.4.2 |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <mgmtCmd> | [variable] | 0..n | Clause 7.4.16 |
| <locationPolicy> | [variable] | 0..n | Clause 7.4.10 |
| <statsConfig> | [variable] | 0..n | Clause 7.4.23 |
| <statsCollect> | [variable] | 0..n | Clause 7.4.25 |
| <request> | [variable] | 0..n | Clause 7.4.12 |
| <delivery> | [variable] | 0..n | Clause 7.4.11 |
| <schedule> | [variable] | 0..1 | Clause 7.4.9 |
| <m2mServiceSubscriptionPolicy | [variable] | 0..n | Clause 7.4.19 |
| <serviceSubscribedAppRule> | [variable] | 0..n | Clause 7.4.29 |
| <notificationTargetPolicy> | [variable] | 0..n | Clause 7.4.31 |
| <dynamicAuthorizationConsultation> | [variable] | 0..n | Clause 7.4.36 |
| <flexContainer> | [variable] | 0..n | Clause 7.4.37 |
| <timeSeries> | [variable] | 0..n | Clause 7.4.38 |
| <role> | [variable] | 0..n | Clause 7.4.40 |
| <token> | [variable] | 0..n | Clause 7.4.41 |

-----------------------End of change 2---------------------------------------------

-----------------------Start of change 3---------------------------------------------

### Resource Type <remoteCSE>

#### Introduction

A <remoteCSE> resource shall represent a remote CSE that is registered to the Registrar CSE. <remoteCSE> resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCSE> resource in the registering CSE's <CSEBase>.

The detailed description can be found in clause 9.6.4 in Architecture TS.

Table 7.4.4.1-1: Data type definition of <remoteCSE> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| remoteCSE | CDT-remoteCSE-v2_6_0.xsd |  |

Table 7.4.4.1-2: Universal/Common Attributes of <remoteCSE> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |
| dynamicAuthorizationConsultationIDs | O | O |

Table 7.4.4.1-3: Resource Specific Attributes of <remoteCSE> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| cseType | O | NP | m2m:cseTypeID | No default |
| pointOfAccess | O | O | m2m:poaList | No default |
| CSEBase | M | NP | xs:anyURI | No default |
| CSE-ID | M | NP | m2m:ID | No default |
| M2M-Ext-ID | O | O | m2m:externalID | No default |
| Trigger-Recipient-ID | O | O | m2m:triggerRecipientID | No default |
| requestReachability | M | O | xs:boolean | No default |
| nodeLink | O | O | xs:anyURI | No default |

Table 7.4.4.1-4: Child resources of <remoteCSE> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <container> | [variable] | 0..n | Clause 7.4.6 |
| <containerAnnc> | [variable] | 0..n | Clause 7.4.6 |
| <flexContainer> | [variable] | 0..n | Clause 7.4.37 |
| <flexContainerAnnc> | [variable] | 0..n | Clause 7.4.37 |
| <group> | [variable] | 0..n | Clause 7.4.13 |
| <groupAnnc> | [variable] | 0..n | Clause 7.4.13 |
| <accessControlPolicy> | [variable] | 0..n | Clause 7.4.2 |
| <accessControlPolicyAnnc> | [variable] | 0..n | Clause 7.4.2 |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <pollingChannel> | [variable] | 0..1 | Clause 7.4.21 |
| <schedule> | [variable] | 0..1 | Clause 7.4.9 |
| <nodeAnnc> | [variable] | 0..n | Clause 7.4.36 |
| <dynamicAuthorizationConsultation> | [variable] | 0..n | Clause 7.4.36 |
| <flexContainer> | [variable] | 0..n | Clause 7.4.37 |
| <timeSeries> | [variable] | 0..n | Clause 7.4.38 |
| <timeSeriesAnnc> | [variable] | 0..n | Clause 7.4.38 |
| <remoteCSEAnnc> | [variable] | 0..n | Clause 7.4.4 |
| <AEAnnc> | [variable] | 0..n | Clause 7.4.5 |
| <locationPolicyAnnc> | [variable] | 0..n | Clause 7.4.10 |

-----------------------End of change 3---------------------------------------------

-----------------------Start of change 4---------------------------------------------

### Announced resource types

#### Introduction

Instances of certain resource types can be announced by the hosting CSE to one or more remote CSEs to inform the remote CSEs of the existence of the original resource instance. Table 7.4.26.1-1 lists the resource types which are announceable together with its resource type identifier and the name of the XSD file that specifies its data type.

Resource-specific attributes of a resource type may be declared announceable (mandatory or optional) or not announceable. Clause 9.6 in TS-0001 [6] defines which attributes of each resource type are announceable.

The universal/common attributes of an announced resource type are listed in table 7.4.26.1-2, together with their request optionality in Create and Update requests (cf. clause 7.4.1). The announced resource includes a common attribute link which represents a link to the original resource hosted by the original resource-hosting CSE.

The child resources applicable to each announced resource type are listed in Table 9.6.26.1-1 of TS-0001 [6]

Table 7.4.26.1-1: Data type definition of announced Resource types

| Data Type ID | File Name | Note |
| --- | --- | --- |
| accessControlPolicyAnnc | CDT-accessControlPolicy-v2_6_0.xsd |  |
| remoteCSEAnnc | CDT-remoteCSE-v2_7_0.xsd |  |
| AEAnnc | CDT-AE-v2_7_0.xsd |  |
| containerAnnc | CDT-container-v2_7_0.xsd |  |
| [flexContainer]Annc | See Annex J and TS-0023 | Announced variants of flexContainer specializations |
| contentInstanceAnnc | CDT-contentInstance-v2_7_0.xsd |  |
| scheduleAnnc | CDT-schedule-v2_7_0.xsd |  |
| locationPolicyAnnc | CDT-locationPolicy-v2_7_0.xsd |  |
| groupAnnc | CDT-group-v2_7_0.xsd |  |
| nodeAnnc | CDT-node-v2_7_0.xsd |  |
| semanticDescriptorAnnc | CDT-semanticDescriptor-v2_7_0.xsd |  |
| timeSeriesAnnc | CDT-timeSeries-v2_6_0.xsd |  |
| timeSeriesInstanceAnnc | CDT-timeSeriesInstance-v2_7_0.xsd |  |
| trafficPatternAnnc | CDT-trafficPattern-v2_7_0.xsd |  |

Table 7.4.26.1-2: Universal/Common Attributes of announcedResource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | M | O |
| lastModifiedTime | NP | NP |
| labels | O | O |
| link | M | O |

Each announced resource type has the resource specific attributes that is the subset of the original resource.

Table 7.4.26.1-3: Resource Specific Attributes of announcedResource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| Name of attribute specified as MA | M | O | same data type as defined for the original resource | This attribute shall be set to the same value with the attribute at the original resource |
| Name of attribute specified as OA | O | O | same data type as defined for the original resource | This attribute shall be set to the same value with the attribute at the original resource |

The procedures defined in the following clause 7.4.27.2 apply to all announced resources regardless of the resource type.

-----------------------End of change 4---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?