| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#25 |
| Source:* | InterDigital |
| Date:* | 2016-10-09 |
| Contact:* | Dale Seed (dale.seed@InterDigital.com), Bob Flynn (bob.flynn@InterDigital.com) |
| Reason for Change/s:* | See the introduction. |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V1.9.0 |
| Clauses/Sub Clauses* | Section 6.3.5.12 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This STE CR proposes to add requestID into the aggregated notification request.

For the case when there is an AE that issues two or more separate requests targeted to the fanoutPoint of the same group within a small window of time, then there exists a scenario where a group hosting CSE may receive notifications for the request in parallel and return aggregated notifcations to the AE in a different order than the requests made by the AE.     Hence there is no way to associate which original request is associated with which aggregated notification.

For example, a <group> resource is created with 3 members and these members are subscribed to (e.g. an AE issues a subscription request to the fanoutPoint of the group).  If an AE subsequently sends an UPDATE request followed by another UPDATE request in a short period of time targeting the fanoutPoint of the group, this will result in group member resources being updated twice and notifications being sent from the group member hosting CSEs to the group hosting CSE. The group hosting CSE will in turn aggregate the notifications from the two UPDATEs into separate aggregated notifications that each contain 3 notification elements; one for each of the members.  Currently however, there is no way to associate which aggregated notification pertains to which original UPDATE request issued by the AE. Hence an attribute to reflect the original request ID should be added to the aggregated notification element to identify the original request.

After the proposed change, an aggregated notification request payload is shown below where rd5 is the request ID of an original fanout request which triggered the aggregated notification.

<?xml version="1.0" encoding="UTF-8" ?>

<m2m:agn xmlns:m2m="http://www.onem2m.org/xml/protocols">

<ori>rd5</ori>

<m2m:sgn>

<nev>

<rep>&lt;?xml version="1.0" encoding="UTF-8"?&gt; &lt;m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols"&gt;&lt;lt&gt;20160311T222235&lt;/lt&gt;&lt;et&gt;20160311T222305&lt;/et&gt;&lt;st&gt;2&lt;/st&gt;&lt;mni&gt;4&lt;/mni&gt;&lt;mbs&gt;60000000&lt;/mbs&gt;&lt;mia&gt;1600&lt;/mia&gt;&lt;/m2m:cnt&gt;

</rep>

</nev>

<sur>sub_20160311T202234_2</sur>

</m2m:sgn>

<m2m:sgn>

<nev>

<rep>&lt;?xml version="1.0" encoding="UTF-8"?&gt; &lt;m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols"&gt;&lt;lt&gt;20160311T222235&lt;/lt&gt;&lt;et&gt;20160311T222305&lt;/et&gt;&lt;st&gt;3&lt;/st&gt;&lt;mni&gt;4&lt;/mni&gt;&lt;mbs&gt;60000000&lt;/mbs&gt;&lt;mia&gt;1600&lt;/mia&gt;&lt;/m2m:cnt&gt;

</rep>

</nev>

<sur>sub_20160311T214438_5</sur>

<m2m:sgn>

<nev>

<rep>&lt;?xml version="1.0" encoding="UTF-8"?&gt; &lt;m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols"&gt;&lt;lt&gt;20160311T222235&lt;/lt&gt;&lt;et&gt;20160311T222305&lt;/et&gt;&lt;st&gt;3&lt;/st&gt;&lt;mni&gt;4&lt;/mni&gt;&lt;mbs&gt;60000000&lt;/mbs&gt;&lt;mia&gt;1600&lt;/mia&gt;&lt;/m2m:cnt&gt;

</rep>

</nev>

<sur>sub_20160311T222324_5</sur>

</m2m:sgn>

</m2m:agn>

## ----------------------- Start of change 1 -----------------------

#### m2m:aggregatedNotification

Used in the Notification Data Object.

Table 6.3.5.12-1: Type Definition of m2m:aggregatedNotification

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| notification | m2m:notification | 1..n |  |
| originalRequestID | m2m:requestID | 1 |  |

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

    - Resource attributes

In protocol bindings resource attributes names shall be translated into short names of Table 8.3-1.

Table 8.2.3-5: Resource attribute short names (5/5)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| minReqVolume | cmdhNwAccessRule | mrv |
| backOffParameters | cmdhNwAccessRule | bop |
| otherConditions | cmdhNwAccessRule | ohc |
| maxBufferSize | cmdhBuffer | mbfs |
| storagePriority | cmdhBuffer | sgp |
| applicableCredIDs | serviceSubscribedAppRule | apci |
| allowedApp-IDs | serviceSubscribedAppRule | aai |
| allowedAEs | serviceSubscribedAppRule | aae |
| originalRequestID | aggregatedNotification | ori |
| NOTE: marked short names have been already assigned in Table 8.2.2-1. |

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?