| CHANGE REQUEST |
| --- |
| Meeting:* | TP25 |
| Source:* | InterDigital |
| Date:* | 2016-10-09 |
| Contact:* | Dale Seed (dale.seed@InterDigital.com), Bob Flynn (bob.flynn@InterDigital.com) |
| Reason for Change/s:* | See the introduction. |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | CDT-accessControlPolicy=v2_7_0.xsd |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This document proposes to add details to the XSD regarding accessControlObjectDetails attribute in accessControlRules. This attribute is a part of accessControlRules present in accessControlPolicy resource. This is defined in Section 9.6.2.4 of TS0001 v 2.10 and corresponding details are not present in the XSD.

## ----------------------- Start of change 1 -----------------------

<?xml version="1.0" encoding="utf-8"?><!--

--><xs:schema elementFormDefault="unqualified" targetNamespace="http://www.onem2m.org/xml/protocols" xmlns="http://www.w3.org/2001/XMLSchema" xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xs="http://www.w3.org/2001/XMLSchema">

<xs:include schemaLocation="CDT-commonTypes-v1_9_0.xsd"/>

<xs:include schemaLocation="CDT-sub-v1_9_0.xsd"/>

<xs:element name="acp">

<xs:complexType>

<xs:complexContent>

<!-- Inherit Announceable Attributes from announceableSubordinateResource type -->

<xs:extension base="m2m:announceableSubordinateResource">

<xs:sequence>

<!-- Resource Specific Attributes -->

<xs:element name="pv" type="m2m:setOfAcrs"  minOccurs="0" />

<xs:element name="pvs" type="m2m:setOfAcrs" minOccurs="0" />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="ch" type="m2m:childResourceRef"

maxOccurs="unbounded"/>

<xs:element ref="m2m:sub" maxOccurs="unbounded"/>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

<xs:element name="acpA">

<xs:complexType>

<xs:complexContent>

<!-- Inherit Announceable Attributes from announceableSubordinateResource type -->

<xs:extension base="m2m:announcedSubordinateResource">

<xs:sequence>

<!-- Resource Specific Attributes -->

<xs:element name="pv" type="m2m:setOfAcrs"  minOccurs="0" />

<xs:element name="pvs" type="m2m:setOfAcrs" minOccurs="0" />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="ch" type="m2m:childResourceRef"

maxOccurs="unbounded"/>

<xs:element ref="m2m:sub" maxOccurs="unbounded"/>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

<!-- TODO: define short names for "setOfAcrs" and all its elements names (CR to TS-0004 for next PRO WG meeting)   -->

<xs:complexType name="setOfAcrs">

<xs:sequence>

<xs:element name="acr" type="m2m:acr" minOccurs="0"

maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="acr">

<xs:sequence>

<xs:element name="acor" type="m2m:listOfURIs" />

<!-- accessControlOperations defined as enumerated list 1 ... 63 -->

<xs:element name="acop" type="m2m:acop" />

<!-- TODO: mismatch with TS-0004 where "acco" has multiplicity 0..1 -->

<xs:element name="acco" minOccurs="0" maxOccurs="unbounded">

<xs:complexType>

<xs:sequence>

<!-- TODO: mismatch with TS-0003 where element is called "accessControlTimeWindows" -->

<!-- TODO: mismatch with TS-0001 where element is called "accessControlTimeWindow" -->

<xs:element name="actw" type="m2m:scheduleEntry" minOccurs="0" maxOccurs="unbounded" />

<!-- TODO: mismatch with TS-0001: element is called accessControlIpAddress in TS-0001" in TS-0003 -->

<xs:element name="acip" minOccurs="0">

<xs:complexType>

<xs:sequence>

<!-- TODO: it should be possible to include both IPv6 and IPv4 address. Present text in TS-0004 is ambiguous. Not

clear if "or" in TS-0001 is inclusive or exclusive. Below it is interpreted as inclusive. -->

<!-- TODO: the element names ipv4Addresses and ipv6Addresses are not explicitly mentioned in TS-0004 -->

<xs:element name="ipv4" minOccurs="0" maxOccurs="1">

<!-- space separated list of IPv4 addresses -->

<xs:simpleType>

<xs:restriction>

<xs:simpleType>

<xs:list itemType="m2m:ipv4"/>

</xs:simpleType>

<xs:minLength value="1"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="ipv6" minOccurs="0" maxOccurs="1">

<!-- space separated list of IPv6 addresses -->

<xs:simpleType>

<xs:restriction>

<xs:simpleType>

<xs:list itemType="m2m:ipv6"/>

</xs:simpleType>

<xs:minLength value="1"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

</xs:sequence>

</xs:complexType>

</xs:element>

<!-- TODO: mismatch with TS-0003 and TS-0004 where element is called "accessControlLocationRegions" -->

<!-- TODO: mismatch with TS-0004 where element has multiplicity [0..n] -->

<xs:element name="aclr" type="m2m:locationRegion" minOccurs="0" />

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="acod" minOccurs="0" maxOccurs="unbounded">

<xs:complexType>

<xs:sequence>

<xs:element name="acodTy" type="m2m:resourceType" minOccurs="0" maxOccurs="1" />

<xs:element name="spid" type="xs:anyURI" minOccurs="0" maxOccurs="1" />

<xs:element name="chty">

<xs:simpleType>

<xs:restriction>

<xs:simpleType>

<xs:list itemType="m2m:resourceType"/>

</xs:simpleType>

<xs:minLength value="1"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

</xs:sequence>

</xs:complexType>

</xs:element>

</xs:sequence>

</xs:complexType>

<xs:complexType name="locationRegion">

<xs:choice>

<xs:element name="accc">

<!-- Space separated list of 2-digit country codes -->

<xs:simpleType>

<xs:restriction>

<xs:simpleType>

<xs:list itemType="m2m:accc"/>

</xs:simpleType>

<xs:minLength value="1"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="accr">

<!-- "circularRegion" is an ordered list of following three parameters of data type float ´ 1) longitude in the range

+/-180 degrees 2) latitude in the range +/-90 degrees, 3) radius in meters -->

<xs:simpleType>

<xs:restriction>

<xs:simpleType>

<xs:list itemType="xs:float" />

</xs:simpleType>

<xs:length value="3"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

</xs:choice>

</xs:complexType>

<!-- countryCode as defined in TS-0004 -->

<xs:simpleType name="accc">

<xs:annotation>

<xs:documentation>2-character country code as defined by ISO-3166</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:pattern value="[A-Z]{2}" />

</xs:restriction>

</xs:simpleType>

<!-- Initial IPv4 and IPv6 address representation types were found here:

http://lists.w3.org/Archives/Public/www-xml-schema-comments/2005OctDec/0138.html, CIDR suffix has been added  -->

<!--  TODO: Need to add more descriptive text into TS-0004 about structure of IPv4 and IPv6 addresses with optional CIDR suffix -->

<xs:simpleType name="ipv4">

<xs:annotation>

<xs:documentation> An IP version 4 address, with optional CIDR suffix in the range /0

... /32. </xs:documentation>

</xs:annotation>

<xs:restriction base="xs:token">

<xs:pattern value="(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])\.(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])\.(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])\.(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])(/([0-9]|[1-2][0-9]|3[0-2]))?"/>

<xs:pattern value="[0-9A-Fa-f]{8}(/([0-9]|[1-2][0-9]|3[0-2]))?"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="ipv6">

<xs:annotation>

<xs:documentation> An IP version 6 address, based on RFC 1884, with optional CIDR suffix

in the range /0 ... /128. </xs:documentation>

</xs:annotation>

<xs:restriction base="xs:token">

<!-- Fully specified address -->

<xs:pattern

value="[0-9A-Fa-f]{1,4}(:[0-9A-Fa-f]{1,4}){7}(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<!-- Double colon start -->

<xs:pattern value=":(:[0-9A-Fa-f]{1,4}){1,7}"/>

<!-- Double colon middle -->

<xs:pattern

value="([0-9A-Fa-f]{1,4}:){1,6}(:[0-9A-Fa-f]{1,4}){1}(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<xs:pattern

value="([0-9A-Fa-f]{1,4}:){1,5}(:[0-9A-Fa-f]{1,4}){1,2}(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<xs:pattern

value="([0-9A-Fa-f]{1,4}:){1,4}(:[0-9A-Fa-f]{1,4}){1,3}(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<xs:pattern

value="([0-9A-Fa-f]{1,4}:){1,3}(:[0-9A-Fa-f]{1,4}){1,4}(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<xs:pattern

value="([0-9A-Fa-f]{1,4}:){1,2}(:[0-9A-Fa-f]{1,4}){1,5}(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<xs:pattern

value="([0-9A-Fa-f]{1,4}:){1}(:[0-9A-Fa-f]{1,4}){1,6}(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<!-- Double colon end -->

<xs:pattern value="([0-9A-Fa-f]{1,4}:){1,7}:(/([0-9]|[1-9][0-9]|1[0-1][0-9]|12[0-8]))?"/>

<!-- Embedded IPv4 addresses without CIDR suffix. Should IPv4 CIDR suffix be added?-->

<xs:pattern

value="((:(:0{1,4}){0,3}(:(0{1,4}|[fF]{4}))?)|(0{1,4}:(:0{1,4}){0,2}(:(0{1,4}|[fF]{4}))?)|((0{1,4}:){2}(:0{1,4})?(:(0{1,4}|[fF]{4}))?)|((0{1,4}:){3}(:(0{1,4}|[fF]{4}))?)|((0{1,4}:){4}(0{1,4}|[fF]{4})?)):(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])\.(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])\.(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])\.(25[0-5]|2[0-4][0-9]|[0-1]?[0-9]?[0-9])"/>

<!-- The unspecified address -->

<xs:pattern value="::(/0)?"/>

</xs:restriction>

</xs:simpleType>

</xs:schema>

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?