| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 26 |
| Source:* | C-DOT |
| Date:* | 2016-11-18 |
| Contact:* | Poornima(poornima@cdot.in), Deepak(deepakkr@cdot.in) |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004_v2_8_0 |
| Clauses/Sub Clauses* | CDT-node-v2_8_0.xsd |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR:<> : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR brings inconsistency in TS-0004 and TS-0001 for <node> resource by adding the missing attributes announceTo, announcedAttribute, and mgmtClientAddress.

TS-0001: highlighted attribute is missing in TS-0004

Table 9.6.18-2: Attributes of <node> resource Attributes of <node> Multiplicity RW/ RO/ WO Description <nodeAnnc> attributes resourceType 1 RO See clause 9.6.1.3. NA resourceID 1 RO See clause 9.6.1.3. NA resourceName 1 WO See clause 9.6.1.3. NA parentID 1 RO See clause 9.6.1.3. NA expirationTime 1 RW See clause 9.6.1.3. MA accessControlPolicyIDs 0..1 (L) RW See clause 9.6.1.3. MA creationTime 1 RO See clause 9.6.1.3. NA lastModifiedTime 1 RO See clause 9.6.1.3. NA labels 0..1 (L) RW See clause 9.6.1.3. MA announceTo 0..1 (L) RW See clause 9.6.1.3. NA announcedAttribute 0..1 (L) RW See clause 9.6.1.3. NA dynamicAuthorizationConsultationIDs 0..1 (L) RW See clause 9.6.1.3. OA nodeID 1 RW The M2M-Node-ID of the node which is represented by this <node> resource. MA hostedCSELink 0..1 RW The hostedCSELink attribute allows to find the <CSEBase> or <remoteCSE> resource representing the CSE that is residing on the node that is represented by this <node> resource. The attribute contains the resource ID of a resource where all of the following applies: The resource is a <CSEBase> resource or a <remoteCSE> resource. The resource represents the CSE which resides on the specific node that is represented by the current <node> resource. In case the node that is represented by this <node> resource does not contain a CSE, this attribute must not be present. OA mgmtClientAddress 0..1 RW Represents the physical address of management client of the node which is represented by this <node> resource. This attribute is absent if management server is able to acquire the physical address of the management client. OA

### -----------------------Start of change 1-------------------------------------------

### Resource Type <node>

#### 7.4.18.1	Introduction

The <node> resource represents specific information that provides properties of an oneM2M Node that can be utilized by other oneM2M operations. The <node> resource has <mgmtObj> as its child resources.

Table 7.4.18.1-1: Data type definition of <node> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| node | CDT-node-v2_8_0v2_8_0.xsd |  |

Table 7.4.18.1-2: Universal/Common Attributes of <node> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |
| dynamicAuthorizationConsultationIDs | O | O |

Table 7.4.18.1-3: Resource Specific Attributes of <node> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| nodeID | M | O | m2m:nodeID |  |
| hostedCSELink | O | NP | m2m:ID |  |
| mgmtClientAddress | O | O | xs:string |  |

Table 7.4.18.1-4: Child resources of <node> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <mgmtObj> | [variable] | 0..n | Clasue 7.4.15, See Annex D |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <semanticDescriptor> | [variable] | 0..n | Clause 7.4.34 |
| <trafficPattern> | [variable] | 0..n | Clause 7.4.42 |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| objectPaths | mgmtObj | obps |
| nodeID | node | ni |
| hostedCSELink | node | hcl |
| mgmtClientAddress | node | mgca |
| CSEBase | remoteCSE | cb* |
| M2M-Ext-ID | remoteCSE | mei |
| Trigger-Recipient-ID | remoteCSE | tri |
| requestReachability | remoteCSE | rr |
| triggerReferenceNumber | remoteCSE | trn |
| originator | request | org |
| metaInformation | request | mi |
| requestStatus | request | rs |
| operationResult | request | ors |
| operation | request | op* |
| requestID | request | rid |
| scheduleElement | schedule | se |
| deviceIdentifier | serviceSubscribedNode | di |
| ruleLinks | serviceSubscribedNode | rlk |
| statsCollectID | statsCollect | sci |
| collectingEntityID | statsCollect | cei |
| collectedEntityID | statsCollect | cdi |
| devStatus | areaNwkDeviceInfo | ss |
| statsRuleStatus | statsCollect | srs |
| statModel | statsCollect | sm |
| collectPeriod | statsCollect | cp |
| eventNotificationCriteria | subscription | enc |
| expirationCounter | subscription | exc |
| notificationURI | subscription | nu |
| groupID | subscription | gpi |
| notificationForwardingURI | subscription | nfu |
| batchNotify | subscription | bn |
| rateLimit | subscription | rl |
| preSubscriptionNotify | subscription | psn |
| pendingNotification | subscription | pn |
| notificationStoragePriority | subscription | nsp |
| latestNotify | subscription | ln |
| notificationContentType | subscription | nct |
| notificationEventCat | subscription | nec |
| subscriberURI | subscription | su |
| version | firmware, software, token | vr |
| URL | firmware, software | url |
| update | firmware | ud |
| updateStatus | firmware | uds |
| install | software | in |
| uninstall | software | un |
| installStatus | software | ins |
| activate | software | act |
| deactivate | software | dea |
| activeStatus | software, areaNwkInfo | acts |
| memAvailable | memory | mma |
| memTotal | memory | mmt |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

<?xml version="1.0" encoding="UTF-8"?>

<!--

Copyright Notification

The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices

contained in the original materials on any copies of the materials and that you comply strictly with these terms.

This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of

any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document.

Â© 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand

and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations.

No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE,

GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY

PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS.

NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO

ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES.

oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

-->

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols"

xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">

<xs:include schemaLocation="CDT-commonTypes-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-memory-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-battery-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-areaNwkInfo-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-areaNwkDeviceInfo-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-firmware-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-software-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-deviceInfo-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-deviceCapability-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-reboot-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-eventLog-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-cmdhPolicy-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-activeCmdhPolicy-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-subscription-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-semanticDescriptor-v2_8_0.xsd" />

<xs:include schemaLocation="CDT-trafficPattern-v2_8_0.xsd" />

<xs:element name="node" substitutionGroup="m2m:sg_announceableResource">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announceable Resources -->

<xs:extension base="m2m:announceableResource">

<!-- Resource Specific Attributes -->

<xs:sequence>

<xs:element name="nodeID" type="m2m:nodeID" />

<xs:element name="hostedCSELink" type="m2m:ID" minOccurs="0" />

<xs:element name=" mgmtClientAddress" type="xs:string" minOccurs="0" />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:memory" />

<xs:element ref="m2m:battery" />

<xs:element ref="m2m:areaNwkInfo" />

<xs:element ref="m2m:areaNwkDeviceInfo" />

<xs:element ref="m2m:firmware" />

<xs:element ref="m2m:software" />

<xs:element ref="m2m:deviceInfo" />

<xs:element ref="m2m:deviceCapability" />

<xs:element ref="m2m:reboot" />

<xs:element ref="m2m:eventLog" />

<xs:element ref="m2m:cmdhPolicy" />

<xs:element ref="m2m:activeCmdhPolicy" />

<xs:element ref="m2m:subscription" />

<xs:element ref="m2m:semanticDescriptor" />

<xs:element ref="m2m:trafficPattern" />

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

<xs:element name="nodeAnnc" substitutionGroup="m2m:sg_announcedResource">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announceable Resources -->

<xs:extension base="m2m:announcedResource">

<!-- Resource Specific Attributes -->

<xs:sequence>

<xs:element name="nodeID" type="m2m:nodeID" />

<xs:element name="hostedCSELink" type="m2m:ID" minOccurs="0" />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:memoryAnnc" />

<xs:element ref="m2m:batteryAnnc" />

<xs:element ref="m2m:areaNwkInfoAnnc" />

<xs:element ref="m2m:areaNwkDeviceInfoAnnc" />

<xs:element ref="m2m:firmwareAnnc" />

<xs:element ref="m2m:softwareAnnc" />

<xs:element ref="m2m:deviceInfoAnnc" />

<xs:element ref="m2m:deviceCapabilityAnnc" />

<xs:element ref="m2m:rebootAnnc" />

<xs:element ref="m2m:eventLogAnnc" />

<xs:element ref="m2m:subscription" />

<xs:element ref="m2m:semanticDescriptor" />

<xs:element ref="m2m:semanticDescriptorAnnc" />

<xs:element ref="m2m:trafficPatternAnnc" />

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

</xs:schema>

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?