| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#26 |
| Source:* | Convida Wireless |
| Date:* | 2016-12-06 |
| Contact:* | Michael Starsinic, Starsinic.Michael@ConvidaWireless.com Dale Seed, Seed.Dale@ConvidaWireless.com Catalina Mladin, Mladin.Catalina@ConvidaWireless.com |
| Reason for Change/s:* | 3GPP Payload Definition |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <WI-0058> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* | 5.2.1, 9 (new), B.1.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

ARC-2016-044R02-3GPP_Trigger_Payload updated TS-0001 provided the details of the contents of the trigger Payload.  A stage 3 binding has not yet been created.

This contribution provides the stage 3 biding of the payload contents.  JSON, XML, and CBOR formats are allowed.

### -----------------------Start of change 1-------------------------------------------

### Interfaces to the underlying networks

The CSEs access the network service functions provided by the underlying networks such as 3GPP, 3GPP2 and WLAN via Mcn reference point. Protocol bindings to the Mcn reference point are described in clause 9.2. The following services are provided by the underlying networks:

Device triggering (see Annex B)

Location request (see Annex G)

Device Management (see clause 7.3.4)

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# Mcn procedures

## Introduction

The following clauses describe procedural details and message format binding for various Mcn procedures.

## Triggering

### Introduction

A trigger request to an underlying network may include an optional payload. If the trigger has no optional trigger payload, the trigger recipient shall take the following action:

- If the trigger recipient is not currently registered with a CSE, it shall register with a CSE.

  - Note: The identity of the registrar CSE is provisioned in the trigger recipient.  The provisioning method is outside the scope of this specification.

- If the trigger recipient is currently registered with a CSE, it shall update its pointOfAccess on its registrar CSE.

If the trigger has an optional trigger payload, the trigger recipient shall use the trigger payload fields to determine the appropriate action and perform the necessary steps.  The trigger payload fields are described in Table 9.2-1.

Table 9.2-1: Trigger payload short names and field descriptions

| Field Name | Short Name | Mandatory/Optional | Type | Values |
| --- | --- | --- | --- | --- |
| triggerPurpose | tpe | Mandatory | Unit32 | 0: establishConnection 1: registrationRequest 2: executeCRUDN |
| triggerInfoUri | tiu | Optional The triggerInfoUri field is mandatory when triggerPurpose is “executeCRUDN”. Otherwise, it is optional. When the triggerPurpose is “establishConnection” and triggerInfoUri is not included, the target URI is the trigger recipient’s pointOfAccess. When the triggerPurpose is “registrationRequest” and triggerInfoUri is not included, the target URI is assumed to be the URI of a CSE that the trigger recipient shall register with. It is assumed that the URI is provisioned in the trigger recipient. The provisioning method is outside the scope of this specification. | URI |  |
| triggerInfoOperation | tio | Optional The triggerInfoOperation field is mandatory when the triggerPurpose is “executeCRUDN”. Otherwise, it is not included. | Unit32 | 0: CREATE 1: RETRIEVE 2: UPDATE 3: DELETE 4: NOTIFY |

Note: Mandatory payload fields are only mandatory if the trigger payload is present.

The trigger payload may be serialized in XML format as defined in Section 8.3, serialized in JSON format as defined in Section 8.4, or serialized in CBOR format as described in Section 8.5. How the trigger sender knows what serialization method is used is outside the scope of this document and is assumed to be via provisioning.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

(normative): 3GPP MTC Interworking

  - Device triggering

    - Providing device triggering service by means of 3GPP networks

Introduction

3GPP Underlying Network has defined a dedicated interface for requesting device triggering. The normative references for applicable interfaces are as follows: 3GPP TS 23.682 [15]. The specification for the interface Tsp is described in 3GPP TS 29.368 [16]. Tsp interface uses Diameter Base Protocol as specified in IETF RFC 3588 [13], in order to use such an interface the CSE shall act as a Diameter client as described in IETF RFC 6733 [14].

Before the CSE initiates the device triggering, the CSE and MTC-IWF shall execute the procedures once as specified in 3GPP TS29.368 [16].

Device action request command

When a CSE needs to issue a device triggering request to the MTC-IWF, the CSE shall send a Device-Action-Request (DAR) command (for detail, see TS 29.368 [16]). The following list provides the parameters mapping between the oneM2M and 3GPP.

Either External-Id or MSISDN:  the CSE maps it to the M2M-Ext-ID, see clause 6.2.

SCS identifier: the CSE maps it to the CSE-ID, see clause 6.2.

Application Port Identifier: the CSE maps it to Trigger-Recipient-ID, see clause 6.2.

Payload: the CSE maps it to the Trigger Payload, see clause 9.2.  The payload is provided to the 3GPP network as an OctetString via the payload AVP of the DAR command.

Device action answer command

As a result of device triggering request to MTC-IWF, the CSE receives a Device-Action-Answer (DAA) command (for detail, see TS 29.368 [16]).

Device notification request command

As a report of the result for device triggering delivery by 3GPP network, the CSE receives a Device-Notification-Request (DNR) command (for detail, see TS 29.368 [16]).

Device notification answer command

As a result of device notification request to MTC-IWF, the CSE sends a Device-Notification-Answer (DNA) command (for detail, see TS 29.368 [16]).

### -----------------------End of change 3-------------------------------------------