| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 26.2 |
| Source:* | C-DOT |
| Date:* | 01/30/17 |
| Contact:* | Preeti Rani <preetir@cdot.in>, Suman Sheoran <ssheoran@cdot.in> |
| Reason for Change/s:* | It is proposed to add missing attributes in TS-0004 and XSD for Location Policy Resources which are there in TS-0001 |
| CR against: Release* | Release-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.8.0 |
| Clauses/Sub Clauses* | Section 7.4.10 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

- Attributes locationInformationType, geographicalTargetArea, geoFenceEventArea and aggregationForward of <locationPolicy> resource are not present in the topic 7.4.10 Resource Type locationPolicy of the document TS-0004 v2.8.0  and the latest XSD of LocationPolicy Resource whereas these are explained as the important parameters while describing the resource in the topic 9.6.10 Resource Type locationPolicy of the document TS-0001 v2.11.1.

- Thus it is proposed to add the above mentioned attributes in the document TS-0004 and the latest XSD. Also, additional enumerated data types need to be defined to typecast the attributes  locationInformationType and geoFenceEventArea as m2m: locationInformationType and m2m: geoFenceEventArea respectively in the “Topic 6.3.4.2 Enumerated data types” of the document TS-0004 v2.8.0 .

- Also, the description of the attribute aggregationForward is not clear in the topic 9.6.10 Resource Type locationPolicy of the document TS-0001.

TS-0001 v2.11.1 9.6.10 Resource Type locationPolicy The <locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M Node. The actual location or event result (in case Geo-fence-Based method) information shall be stored in a <contentInstance> resource which is a child resource of the <container> resource. The <container> resource includes the locationID attribute which holds the ID of this <locationPolicy> resource. A CSE can obtain location information based on the attributes defined under <locationPolicy> resource, and store the location information in the target <container> resource. Based on the locationSource attribute, the method for obtaining location information of an M2M Node can be differentiated. The methods for obtaining location information shall be as follows: Network-based method: where the CSE on behalf of the AE obtains the target M2M Node's location information from an Underlying Network. Device-based method: where the ASN is equipped with any location capable modules or technologies (e.g. GPS) and is able to position itself. Sharing-based method: where the ADN has no GPS nor an Underlying Network connectivity. Its location information can be retrieved from either the associated ASN or a MN. NOTE: Geographical location information could include more than longitude and latitude. Figure 9.6.10-0 shows the graphical information regarding the event types for the Geo-fence feature defined as the geofenceEventCriteria attribute. The time diffence between t1 and t2 described in the figure below is defined by locationUpdatePeriod attribute. Figure 9.6.10-0: The Event Types for the Geo-fence The <locationPolicy> resource shall contain the child resources specified in table 9.6.10-1. Table 9.6.10-1: Child resources of <locationPolicy> resource Child Resources of <locationPolicy> Child Resource Type Multiplicity Description <locationPolicyAnnc> Child Resource Types [variable] <subscription> 0..n See clause 9.6.8 None The <locationPolicy> resource shall contain the attributes specified in table 9.6.10-2. Table 9.6.10-2: Attributes of <locationPolicy> resource Attributes of <locationPolicy> Multiplicity RW/ RO/ WO Description <locationPolicyAnnc> Attributes resourceType 1 RO See clause 9.6.1.3. NA resourceID 1 RO See clause 9.6.1.3. NA resourceName 1 WO See clause 9.6.1.3. NA parentID 1 RO See clause 9.6.1.3. NA expirationTime 1 RW See clause 9.6.1.3. MA accessControlPolicyIDs 0..1 (L) RW See clause 9.6.1.3. MA creationTime 1 RO See clause 9.6.1.3. NA lastModifiedTime 1 RO See clause 9.6.1.3. NA labels 0..1 (L) RW See clause 9.6.1.3. MA announceTo 0..1 (L) RW See clause 9.6.1.3. NA announcedAttribute 0..1 (L) RW See clause 9.6.1.3. NA dynamicAuthorizationConsultationIDs 0..1 (L) RW See clause 9.6.1.3. OA locationSource 1 RW Indicates the source of location information: Network Based; Device Based; Sharing Based. OA locationInformationType 1 RW Indicate the types of location information: Position fix (e.g. longitude and latitude); Geo-fence event (e.g. entering and leaving). OA locationUpdatePeriod 0..1(L) RW Indicates the period for updating location information. If the value is marked '0' or not defined, location information is updated only when a retrieval request is triggered. If the attribute has more than one value and the hosting CSE of the resource is the target device, the value could be selected within listed values depending on device's local context information(e,q,, velocity, status of battery, range of the location etc). Zero('0') shall not be stored with non zero value(s). When the value is read, the first value in the list is the current active update period. OA locationTargetID 0..1 RW The identifier to be used for retrieving the location information of a remote Node and this attribute is only used in the case that location information is provided by a location server. OA locationServer 0..1 RW Indicates the identity of the location or Geo-fence server. This attribute is only used in that case location information is provided by a location server or Geo-fence server. OA locationContainerID 1 RO ID of the <container> resource where the actual location information or event result of a M2M Node is stored. OA locationContainerName 0..1 RW A name of the <container> resource where the actual location information of a M2M Node is stored. If it is not assigned, the Hosting CSE automatically assigns a name of the resource (see note). OA locationStatus 1 RO Contains the information on the current status of the location request (e.g. location server fault). OA geographicalTargetArea 0..1 RW Indicates area information where the Geo-fence feature is applied. OA geofenceEventCriteria 0..1 RW Indicate the event type of Geo-fence feature: Entering; Leaving; Inside; Outside. OA aggregationForward 0..1 RW Indicate how Geo-fence relevant information (e.g. measurement or position fix) from the target node is forwarded to Geo-fence server: True/False; Number of Events; Time-based Accmulation. OA NOTE: The created <container> resource related to this policy shall be stored only in the Hosting CSE.

### -----------------------Start of change 1---------------------------------------------

##### 6.3.4.2.46	m2m:locationInformationType

Used for locationInformationType attribute of <locationPolicy> resource.

Table 6.3.4.2.46-46 Interpretation of  locationInformationType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Position fix |  |
| 2 | Geo-fence event |  |
| NOTE: See clause 7.4.11 “Resource Type locationPolicy” |

##### 6.3.4.2.47	m2m:geofenceEventCriteria

Used for geofenceEventCriteria attribute of <locationPolicy> resource.

Table 6.3.4.2.47-47	Interpretation of geofenceEventCriteria

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Entering |  |
| 2 | Leaving |  |
| 3 | Inside |  |
| 4 | Outside |  |
| NOTE: See clause 7.4.11 “Resource Type locationPolicy” |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### 7.4.10 Resource Type <locationPolicy>

#### 7.4.10.1 Introduction

The <locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M Node. The detailed description can be found in the clause 9.6.10 in TS-0001 v2.11.1 [6] .

Table 7.4.10.1 Introduction-160: Data type definition of <locationPolicy> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| locationPolicy | CDT-locationPolicy-v2_8_0.xsd |  |

Table 7.4.10.1 Introduction-161: Universal/Common Attributes of <locationPolicy> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| expirationTime | O | O |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| lastModifiedTime | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |
| dynamicAuthorizationConsultationIDs | O | O |

Table 7.4.10.1 Introduction-162: Resource Specific Attributes of <locationPolicy> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| locationSource | M | NP | m2m:locationSource | No default |
| locationInformationType | M | NP | m2m:locationInformationType | No default |
| locationUpdatePeriod | O | O | xs:duration | No default |
| locationTargetID | O | NP | m2m:nodeID | No default |
| locationServer | O | NP | xs:anyURI | No default |
| locationContainerID | NP | NP | xs:anyURI | No default |
| locationContainerName | O | O | xs:string | No default |
| locationStatus | NP | NP | xs:string | No default |
| geographicalTargetArea | O | O | xs:string | No default |
| geofenceEventCriteria | O | O | m2m:geofenceEventCriteria | No default |
| aggregationForward | O | O | xs:string | No default |

- Table 7.4.10.1Introduction-163: Child resources of <locationPolicy> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause : 7.4.8 |

### -----------------------End  of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?