| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO 28 |
| Source:* | Francisco Sang-Eon Kim, KT (TTA), kim.sangeon@kt.com |
| Date:* | 2017-03-19 |
| Reason for Change/s:* | The response primitive parameter specified at 7.2.1.2 in TS-0004 is not consistent with 8.1.3 in TS-0001. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / WI-0049 Is this a mirror CR? Yes No mirror CR number: (PRO-2017-0064) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V2.10.0 |
| Clauses * | 7.2.1.2 Response primitive format |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | Not identified |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The response primitive parameter specified at 7.2.1.2 in TS-0004 is not consistent with 8.1.3 in TS-0001 as following.

| parameters | TS-0001 8.1.3 | TS-0004 7.2.1.2 |
| --- | --- | --- |
| Response Status Code | Specified | Specified |
| Request Identifier | Specified | Specified |
| Content | Specified | Specified |
| To | Specified | Specified |
| From | Specified | Specified |
| Originating Timestamp | Specified | Specified |
| Result Expiration Timestamp | Specified | Specified |
| Event Category | Specified | Specified |
| Content Status | Specified | Specified |
| Content Offset | Specified | Specified |
| Token Request Information | Specified | Specified |
| Assigned Token Identifier | Not specified | Specified |

It is different case of response status code between TS-0001 and TS-0004

| Response category | TS-0001 8.1.3 | TS-0004 7.2.1.2 |
| --- | --- | --- |
| ACK | Specified | Specified |
| Success | Create | Specified | Specified |
|  | Retrieve | Specified | Specified |
|  | Update | Specified | Specified |
|  | Delete | Specified | Specified |
|  | Notify | Specified | Specified |
| Error | Create/ Retrieve/ Update/ Delete | Specified | Not clear |
|  | Notify | Specified |  |

-----------------------Start of change 1-------------------------------------------

#### Response primitive format

Table7.2.1.2-1 summarizes the primitive parameters for Response primitive, indicating their presence depending on the C, R, U, D or N operations of the associated Request primitive and whether this operation was successful or caused an error. "M" indicates mandatory, "O" indicates optional, "NP" indicates not present.

Refer to clause 8.1.3 of TS-0001 [6] for additional information on the request primitive parameters.

NOTE:	Response Code and Status Code parameters are merged into the Response Status Code parameter.

Table7.2.1.2-1 : Response Primitive Parameters

| Primitive parameter | Ack | Success | Error |
| --- | --- | --- | --- |
|  |  | CREATE | RETRIEVE | UPDATE | DELETE | NOTIFY | C/R/U/D | N |
| Response Status Code | M | M | M | M | M | M | M | M |
| Request Identifier | M | M | M | M | M | M | M | M |
| Content | O | O | M | O | O | O | O | O |
| To | O | O | O | O | O | O | O | O |
| From | O | O | O | O | O | O | O | O |
| Originating Timestamp | O | O | O | O | O | O | O | O |
| Result Expiration Timestamp | O | O | O | O | O | O | O | O |
| Event Category | O | O | O | O | O | O | O | NP |
| Content Status | NP | NP | O | NP | NP | NP | NP | NP |
| Content Offset | NP | NP | O | NP | NP | NP | NP | NP |
| Token Request Information | NP | NP | NP | NP | NP | NP | O | O |

The Content parameter in a Response shall contain one of the following:

- A complete or partial Resource. This applies to a response primitive sent in reply to create and retrieve request message. A partial resource also applies to a response primitive sent in reply to update request message. The Content parameter shall contain a single root element whose name is the name of the Resource and whose content consists of one or more attributes, child resources or childResource references. In this case the resource type is as defined in clause 7.4. However if a partial resource is being transferred, it is not required to be valid according to the XSD for that resource, in terms of the presence of resource attributes. Any attribute that is present, however, shall comply to the data type defined in the XSD of that resource.

The URI of a resource. This is included directly as the content of the Content parameter (like in case 6)

A partial resource and its hierarchical URI. These are included in a root element called m2m:resource defined in clause 7.5.2. The URI is included as an attribute of m2m:resource.

A list of URIs. This can be used for transferring the childResource URIs in a Discovery response. These are included in an element called m2m:URIList defined in clause 7.5.2.

A list of childResourceRef. This can be used for transferring the child resource references in a Discovery response. These are included in an element called m2m:resourceRefList defined in clause 7.5.2.

An Aggregated Response. This is sent as a result of a Group operation. This uses the element m2m:aggregatedResponse defined in clause 7.5.2.

Human-readable error message. This is included in an element called m2m:debugInfo defined in clause 7.5.2.

-----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?