| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 28.2 |
| Source:* | C-DOT |
| Date:* | 2017-04-26 |
| Contact:* | Poornima(poornima@cdot.in), Siddharth (strikha@cdot.in) |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* | CDT-commonTypes-v2_11_0.xsd |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR:<PRO-2017-0089> : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### expirationTime is a universal attributes as highlighted below so it should be handled as part of complexType=”resource”

TS-0001

Table 9.6.1.3.1-1: Universal Attributes

| Attribute Name | Description |
| --- | --- |
| resourceType | Resource Type. This Read Only (assigned at creation time. and then cannot be changed) attribute identifies the type of the resource as specified in clause 9.6. Each resource shall have a resourceType attribute. |
| resourceID | This attribute is an identifier for the resource that is used for 'non-hierarchical addressing method', i.e. this attribute shall contain the 'Unstructured-CSE-relative-Resource-ID' format of a resource ID as defined in table 7.2-1. This attribute shall be provided by the Hosting CSE when it accepts a resource creation procedure. The Hosting CSE shall assign a resourceID which is unique in that CSE. |
| resourceName | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. See clause 7.2 for more details. This attribute may be provided by the resource creator. The Hosting CSE shall use a provided resourceName as long as it does not already exist among child resources of the targeted parent resource. If the resourceName already exists, the Hosting CSE shall reject the request and return an error to the Originator. The Hosting CSE shall assign a resourceName if one is not provided by the resource creator. |
| parentID | This attribute is the resourceID of the parent of this resource. The value of this attribute shall be NULL for the <CSEBase> resource type. |
| creationTime | Time/date of creation of the resource. This attribute is mandatory for all resources and the value is assigned by the system at the time when the resource is locally created. Such an attribute cannot be changed. |
| lastModifiedTime | Last modification time/date of the resource. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| expirationTime | Time/date after which the resource will be deleted by the Hosting CSE. This attribute can be provided by the Originator, and in such a case it will be regarded as a hint to the Hosting CSE on the lifetime of the resource. The Hosting CSE can however decide on the real expirationTime. If the Hosting CSE decides to change the expirationTime attribute value, this is communicated back to the Originator. The lifetime of the resource can be extended by providing a new value for this attribute in an UPDATE operation. Or by deleting the attribute value, e.g. by updating the attribute with NULL when doing a full UPDATE, in which case the Hosting CSE can decide on a new value. This attribute is mandatory when specified. If the Originator does not provide a value in the CREATE operation the system shall assign an appropriate value depending on its local policies and/or M2M service subscription agreements. A resource is known as 'obsolete' when the resource contains the attribute "expirationTime" and the lifetime of this resource has reached the value of this attribute |

Previously, expirationTime was a common attribute (in TS-0001 2.4.1 release), it was changed to universal attribute in TS-0001 2.5 release. But the same change is not reflected in XSD.

So this CR proposes changes in CDT-commonTypes XSD for expirationTime universal attribute.

### -----------------------Start of change 1-------------------------------------------

### <!-- Resource type definitions. These types include the "common attributes" that are used by oneM2M Resources. Each oneM2M 
        Resource has a resource type that is defined in a separate schema, but each resource type extends one of the types that is 
        defined below --> 
    
    <xs:complexType name="resource"> 
        <xs:sequence> 
            <xs:element name="resourceType" type="m2m:resourceType" /> 
            <xs:element name="resourceID" type="m2m:ID" /> 
            <xs:element name="parentID" type="m2m:nhURI" /> 
            <xs:element name="creationTime" type="m2m:timestamp" /> 
            <xs:element name="lastModifiedTime" type="m2m:timestamp" /> 
            <xs:element name="labels" type="m2m:labels" minOccurs="0" />

### <xs:element name="expirationTime" type="m2m:timestamp" />
        </xs:sequence> 
        <xs:attribute name="resourceName" type="m2m:resourceName" use="required" /> 
    </xs:complexType> 

    <xs:complexType name="regularResource"> 
        <xs:complexContent> 
            <xs:extension base="m2m:resource"> 
                <xs:sequence> 
                    <xs:element name="accessControlPolicyIDs" type="m2m:acpType" minOccurs="0" /> 
                                       <xs:element name="dynamicAuthorizationConsultationIDs" type="m2m:listOfURIs" minOccurs="0" /> 
                </xs:sequence> 
            </xs:extension> 
        </xs:complexContent> 
    </xs:complexType> 

    <xs:complexType name="announceableResource"> 
        <xs:complexContent> 
            <xs:extension base="m2m:regularResource"> 
                <xs:sequence> 
                    <xs:element name="announceTo" type="m2m:listOfURIs" minOccurs="0" /> 
                    <xs:element name="announcedAttribute" minOccurs="0"> 
                        <xs:simpleType> 
                            <xs:restriction> 
                                <xs:simpleType> 
                                    <xs:list itemType="xs:NCName" /> 
                                </xs:simpleType>     
                                <xs:minLength value="1" /> 
                            </xs:restriction> 
                        </xs:simpleType> 
                    </xs:element> 
                </xs:sequence> 
            </xs:extension> 
        </xs:complexContent> 
    </xs:complexType> 

    <xs:complexType name="announcedResource"> 
        <xs:complexContent> 
            <!-- AccessControlPolicyIDs is mandatory for announced resources but not for the original ones --> 
            <xs:extension base="m2m:resource"> 
                <xs:sequence> 
                    <xs:element name="accessControlPolicyIDs" type="m2m:acpType" /> 
                    <xs:element name="link" type="xs:anyURI" /> 
                    <xs:element name="dynamicAuthorizationConsultationIDs" type="m2m:listOfURIs" minOccurs="0" /> 
                </xs:sequence> 
            </xs:extension> 
        </xs:complexContent> 
    </xs:complexType> 

    <xs:complexType name="announceableSubordinateResource"> 
        <xs:complexContent> 
            <xs:extension base="m2m:resource"> 
                <xs:sequence> 
                    <xs:element name="announceTo" type="m2m:listOfURIs" minOccurs="0" /> 
                    <xs:element name="announcedAttribute" minOccurs="0"> 
                        <xs:simpleType> 
                            <xs:restriction> 
                                <xs:simpleType> 
                                    <xs:list itemType="xs:NCName" /> 
                                </xs:simpleType> 
                                <xs:minLength value="1" /> 
                            </xs:restriction> 
                        </xs:simpleType> 
                    </xs:element> 
                </xs:sequence> 
            </xs:extension> 
        </xs:complexContent> 
    </xs:complexType> 
    
    <xs:complexType name="subordinateResource"> 
        <xs:complexContent> 
            <xs:extension base="m2m:resource"> 
                <xs:sequence> 
                </xs:sequence> 
            </xs:extension> 
        </xs:complexContent> 
    </xs:complexType> 

    <xs:complexType name="announcedSubordinateResource"> 
        <xs:complexContent> 
            <xs:extension base="m2m:resource"> 
                <xs:sequence> 
                    <xs:element name="link" type="xs:anyURI" /> 
                </xs:sequence> 
            </xs:extension> 
        </xs:complexContent> 
    </xs:complexType>

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?