| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO#30.0 |
| Source:* | Nobu Uchida, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Date:* | 2017-07-07 |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: PRO-2017-0160 STE Small Technical Enhancements / < Work Item number (optional) Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.12.0 (XSD only impact) |
| Clauses * | CDT-responsePrimitive-v2_12_0.xsd |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In CDT-responsePrimitive-v2_12_0.xsd, there are minor errors in the listOfChildResourceRef as follows;

- xs:element name="childResource" ( "resourceRef”

- minOccurs="0" ( "1"

This CR proposes to fix those errors.

#### m2m:listOfChildResourceRef

Table 6.3.5.49-1: Type Definition of m2m:listOfChildResourceRef

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| resourceRef | m2m:childResourceRef | 1..n | References of resources with name and type |

### -----------------------Start of change 1-------------------------------------------

<?xml version="1.0" encoding="UTF-8"?>

<!--

Copyright Notification

The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices contained in the original materials on any copies of the materials and that you comply strictly with these terms.

This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document.

© 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS.

NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

-->

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

targetNamespace="http://www.onem2m.org/xml/protocols"

xmlns:m2m="http://www.onem2m.org/xml/protocols"

elementFormDefault="unqualified" attributeFormDefault="unqualified" >

<xs:include schemaLocation="CDT-commonTypes-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-accessControlPolicy-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-activeCmdhPolicy-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-AE-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-areaNwkDeviceInfo-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-areaNwkInfo-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-battery-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhBuffer-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhDefaults-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhDefEcValue-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhEcDefParamValues-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhLimits-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhNetworkAccessRules-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhNwAccessRule-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-cmdhPolicy-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-container-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-contentInstance-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-CSEBase-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-delivery-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-deviceCapability-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-deviceInfo-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-eventConfig-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-eventLog-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-execInstance-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-firmware-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-group-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-locationPolicy-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-m2mServiceSubscriptionProfile-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-memory-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-mgmtCmd-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-node-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-notification-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-pollingChannel-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-reboot-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-remoteCSE-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-request-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-requestPrimitive-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-responsePrimitive-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-schedule-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-serviceSubscribedAppRule-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-serviceSubscribedNode-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-software-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-statsCollect-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-statsConfig-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-subscription-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-timeSeries-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-timeSeriesInstance-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-role-v2_12_0.xsd" />

<xs:include schemaLocation="CDT-token-v2_12_0.xsd" />

<xs:element name="responsePrimitive" >

<xs:complexType>

<xs:sequence>

<!-- Response Code and Status Code primitive parameters defined in TS-0001 have been merged into

Response Status Code  in TS-0004 -->

<!-- parameter "Response Status Code" -->

<xs:element name="responseStatusCode" type="m2m:responseStatusCode" minOccurs="1"/>

<!-- parameter "Request Identifier" -->

<xs:element name="requestIdentifier" type="m2m:requestID" minOccurs="1"/>

<!-- parameter "Content" -->

<xs:element name="primitiveContent" type="m2m:primitiveContent" minOccurs="0"/>

<!-- parameter "To" -->

<xs:element name="to" type="m2m:ID" minOccurs="0"/>

<!-- parameter "From" -->

<xs:element name="from" type="m2m:ID" minOccurs="0"/>

<!-- parameter "Originating Timestamp" -->

<xs:element name="originatingTimestamp" type="m2m:timestamp" minOccurs="0"/>

<!-- parameter "Result Expiration Timestamp" -->

<xs:element name="resultExpirationTimestamp" type="m2m:absRelTimestamp" minOccurs="0"/>

<!-- parameter "Event Category" -->

<xs:element name="eventCategory" type="m2m:eventCat" minOccurs="0" />

<!-- parameter "Content Status" -->

<xs:element name="contentStatus" type="m2m:contentStatus" minOccurs="0" />

<!-- parameter "Content Offset" -->

<xs:element name="contentOffset" type="xs:positiveInteger" minOccurs="0" />

<!-- parameter "Assigned Token Identifiers -->

<xs:element name="assignedTokenIdentifiers" type="m2m:dynAuthLocalTokenIdAssignments" minOccurs="0" />

<!-- parameter "Token Request Information -->

<xs:element name="tokenRequestInformation" type="m2m:dynAuthTokenReqInfo" minOccurs="0" />

<!-- parameter "Authorization Signature Request Information -->

<xs:element name="authorSignReqInfo" type="xs:boolean" minOccurs="0" />

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="resource" type="m2m:resourceWrapper"  />

<xs:element name="URIList" type="m2m:listOfURIs"  />

<xs:element name="URI" type="xs:anyURI"  />

<xs:element name="aggregatedResponse" type="m2m:aggregatedResponse" />

<xs:element name="resourceRefList" type="m2m:listOfChildResourceRef" />

<xs:element name="debugInfo" type="xs:string" />

<xs:complexType name="resourceWrapper">

<xs:sequence>

<xs:choice minOccurs="1" maxOccurs="1">

<xs:element ref="m2m:sg_resource" />

<xs:element ref="m2m:sg_regularResource" />

<xs:element ref="m2m:sg_announcedResource" />

<xs:element ref="m2m:sg_announceableResource" />

<xs:element ref="m2m:sg_subordinateResource" />

<xs:element ref="m2m:sg_announcedSubordinateResource" />

<xs:element ref="m2m:sg_announceableSubordinateResource" />

<xs:element ref="m2m:sg_mgmtResource" />

<xs:element ref="m2m:sg_announcedMgmtResource" />

<xs:element ref="m2m:sg_flexContainerResource" />

<xs:element ref="m2m:sg_announcedFlexContainerResource" />

</xs:choice>

<xs:element name="URI" type="xs:anyURI" />

</xs:sequence>

</xs:complexType>

<xs:complexType name="aggregatedResponse">

<xs:sequence>

<xs:element name="resourceID" type="xs:anyURI" minOccurs="0"/>

<xs:element ref="m2m:responsePrimitive" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="listOfChildResourceRef">

<xs:sequence>

<xs:element name="resourceRef" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />

</xs:sequence>

</xs:complexType>

</xs:schema>

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?