| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO 31 |
| Source:* | Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Zhuo Chen, Convida Wireless, Chen.Zhuo@ConvidaWireless.com Bob Flynn, Convida, Flynn.Bob@convidawireless.com |
| Date:* | 2017-09-11 |
| Reason for Change/s:* | Add more descriptions on how a CSE forward a request into TS-0004 as agreed from TS-0001 |
| CR against: Release* | Release 3 |
| CR against: WI* | Active (WI-0062) MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision) Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 Version 3.3.0 |
| Clauses * | 7.3.2.6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

R01- corrected the Meeting ID in template.

This contribution adds support for the new descendantCSEs attribute for the <remoteCSE> resource.  This attribute has been agreed in both TS-0001-V3_4_0 and TR-0030-Service Layer Forwarding-V0_2_0.

The motivation for adding this new attribute is to address the issue that oneM2M lacks support for forwarding a request downward in a hierarchy which spans across multiple CSE hops. This is because oneM2M registration only shares information between a registrar and registree CSE.  It does not provide a registrar CSE with information regarding a registree CSE’s descendant CSEs.

For example, when ASN-CSE-1 sends a message to ASN-CSE-2, ASN-CSE-1 first sends the message to MN-CSE-1 (ASN-CSE-1’s registrar CSE). MN-CSE-1 re-targets the message to IN-CSE (MN-CSE-1’s Registrar CSE). However, IN-CSE does not know how to retarget the message since ASN-CSE-2 does not register to IN-CSE and MN-CSE-2 does not provide information about its descendant CSEs (i.e. ASN-CSE2) to IN-CSE. Therefore, ASN-CSE-1 cannot send a message to ASN-CSE-2 in the currently defined oneM2M Release 1 or Release 2 architecture without using proprietary mechanisms.  This causes interoperability issues.  This contribution provides a solution to this issue.

## ----------------------- Start of change  1 -----------------------

#### 7.3.2.6 		Forwarding

When a receiver CSE is not the Hosting CSE, i.e. the CSE-ID of the receiver CSE is different from the CSE-ID in the “To” field,  the receiver CSE shall attempt to forward the message. The Receiver CSE checks each of its <remoteCSE> resources to find whether the CSE-ID in the “To” field of the message matches the CSE-ID attribute or one of the CSE-IDs in the descendantCSEs attribute. If a match is found, the CSE shall retarget the request to the pointOfAccess of the matching <remoteCSE> resource.

If a match is not found, and the CSE received the request from an AE or a descendant CSE, and the CSE is not the IN-CSE, then it shall retarget the request to its Registrar CSE.

If a match is not found and the CSE is the IN-CSE, then the CSE shall not forward the request and it shall respond with an error (e.g. 4004 NOT_FOUND).

If a match is not found and the CSE is not the IN-CSE and the CSE receives the request from its registrar CSE, then the CSE shall not forward the request and it shall respond with an error (e.g. 4004 NOT_FOUND).

If the Request Expiration Timestamp, Result Expiration Timestamp or Operation Execution Time is set in the request, the receiver CSE should forward the request before the earliest of the times. If the any of the timestamps are in the past, it shall reject the request with a "REQUEST_TIMEOUT" Response Status Code parameter value and not forward the request.

Acting as an originator the CSE shall perform the following procedures:

- "Send a Request to the receiver CSE". Please refer to clause 7.3.1.2 for details.

- "Wait for Response primitive". Please refer to clause 7.3.1.3 for details.

When the Response is received the receiver CSE shall:

- Primitive specific procedure: Forward the Response to the original CSE.

## ----------------------- End of change  1 -----------------------