| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO#32 |
| Source:* | Yongjing Zhang, Huawei, zhangyongjing@huawei.com |
| Date:* | 2017-11-03 |
| Reason for Change/s:* | This contribution fixes a wrong attribute name in the <semanticDescriptor> resource UPDATE procedure. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0053 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004. v3.4.0 |
| Clauses * | 7.4.34.2.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

# Introduction

This contribution fixes a wrong attribute name in the <semanticDescriptor> resource UPDATE procedure.

### -----------------------Start of change 1------------------------------------------

#### 7.4.34.2	<semanticDescriptor> resource specific procedure on CRUD operations

##### Introduction

This clause describes <semanticDescriptor> resource specific primitive behaviour for CRUD operations.

##### Create

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2 with the following exception:

- Primitive specific operation on Recv-6.4 "Check validity of resource representation for the given resource type":

- The Hosting CSE shall check that the descriptor attribute conforms to the RDF/XML syntax as defined in RDF 1.1 XML Syntax [33]

- If the descriptor attribute does not conform, the Hosting CSE shall return failure information with additional error information as defined in clause 7.2.1.2.

- Primitive specific operation on Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed":

- The hosting CSE shall set the validationEnable attribute of the addressed <semanticDescriptor> resource based on the value provided in the request and its local policy. Note that the local policy may override the suggested value provided in the request from the originator to enforce or disable the following semantic validation procedures. There are different cases depending on how the local policy is configured (which is out of the scope of this specification) and whether/how the validationEnable attribute is provided in the request:

      - validationEnable attribute is not present if not provided in the request or the local policy doesn’t allow for the validationEnable attribute.

      - validationEnable attribute is set as ‘True’ or ‘False’ according to the local policy no matter whether and how the value is provided in the request;

      - validationEnable attribute is set as ‘True’ or ‘False’ according to the value provided in the request;

- If the validationEnable attribute is set as ‘True’, the hosting CSE shall perform the semantic validation process in the following steps according to clause 7.10.2 in TS-0034 [50]. Otherwise, skip the following steps.

- Check if the addressed <semanticDescriptor> resource is linked to other <semanticDescriptor> resources on a remote CSE according to the relatedSemantics attribute or triples with annotation property m2m:resourceDescriptorLink in descriptor attribute. This process shall consider the recursive links.

      - If yes, the Hosting CSE shall generate as an Originator an Update request primitive with the Content parameter set to the addressed <semanticDescriptor> resource representation, and send it to the <semanticValidation> virtual resource URI on the CSE which hosts the referenced ontology (following the ontologyRef attribute) of the addressed <semanticDescriptor> resource (see details in clause 7.4.z.2.3). After receiving the response primitive, i.e. the validation result, go to step k. If no response primitive received due to time out or other exceptional cases, the hosting CSE shall generate a Response Status Code indicating a “TARGET_NOT_REACHABLE” error.

      - If no, perform the following steps.

- Retrieve the semantic triples from the descriptor attribute of the received <semanticDescriptor> resource;

- Retrieve the referenced ontology following the URI in ontologyRef attribute of the received <semanticDescriptor> resource.

      - If the URI is de-referenced as a <ontology> resource, the Hosting CSE procedure shall retrieve it according the procedure specified in clause 7.4.y.2.2;

      - If the URI is de-referenced as an external ontology, the Hosting CSE may retrieve it by other means that is out of the scope of current specification.

      - If the referenced ontology cannot be retrieved within a reasonable time (which is subject to a local policy), the Hosting CSE shall generate a Response Status Code indicating a “ONTOLOGY_NOT_AVAILABLE” error.

- Retrieve any local linked <semanticDescriptor> resources of the received <semanticDescriptor> resource following the URI(s) in the relatedSemantics attribute (if exists) and the URI(s) in the triples with annotation property m2m:resourceDescriptorLink (if exists).

    - Repeat this step recursively to Retrieve any further local linked <semanticDescriptor> resources.

    - If the local linked <semanticDescriptor> resources cannot be retrieved within a reasonable time (which is subject to a local policy), the Hosting CSE shall generate a Response Status Code indicating a “LINKED_SEMANTICS_NOT_AVAILABLE” error.

- Retrieve the semantic triples from the descriptor attribute of the local linked <semanticDescriptor> resource;

- Retrieve the referenced ontologies of the local linked <semanticDescriptor> resources following the URI(s) in ontologyRef attribute of the linked <semanticDescriptor> resources; If the referenced ontologies cannot be retrieved within a reasonable time (which is subject to a local policy), the Hosting CSE shall generate a Response Status Code indicating a “ONTOLOGY_NOT_AVAILABLE” error.

- Combine all the semantic triples of the addressed and local linked <semanticDescriptor> resources as the set of semantic triples to be validated, and combine all the referenced ontologies as the set of ontologies to validate the semantic triples against;

- Check all the aspects of semantic validation according to clause 7.10.3 in TS-0034[x] based upon the semantic triples and referenced ontology. If any problem occurs, the Hosting CSE shall generate a Response Status Code indicating a “INVALID_SEMANTICS” error.

- After the semantic validation process, the Hosting CSE shall set the semanticValidated attribute of the addressed <semanticDescriptor> resource according to the validation result (i.e. set to ‘True’ if the no error occurs until now, otherwise ‘False’).

- Base on its local policy, the Hosting CSE may also update the value of the semanticValidated attributes of the local linked <semanticDescriptor> resources according to the validation result.

##### Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2 with the following exception:

The semanticOpExec attribute is never returned in the response.

##### Update

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exception:

The descriptor attribute can be updated using SPARQL as follows:

Primitive specific operation on Orig-1.0 "Compose Request primitive": The originator creates a request to update the semanticOpExec attribute. The value of this attribute is set to a SPARQL request that includes INSERT, DELETE, or DELETE/INSERT with conditional SPARQL statements as defined in the SPARQL query language [33].

Receiver:

No change from the generic procedures in clause 7.2.2.2 with the following exceptions:

- Primitive specific operation on Recv-6.4 "Check validity of resource representation for the given resource type":

- If both semanticOpExec and descriptor attributes exist, the Receiver shall generate a Response Status Code indicating a "NOT_ACCEPTABLE" error.

- If semanticOpExec attribute exists in the Request check that the syntax of its content corresponds to a valid SPARQL query request [33]. If the content does not correspond to a valid SPARQL query request, the Receiver shall generate a Response Status Code indicating a "NOT_ACCEPTABLE" error.

- If the descriptor attribute exists in the Request, check that the syntax of its content corresponds to a valid the RDF/XML syntax as defined in RDF 1.1 XML Syntax [34]. If the content does not correspond to a valid RDF/XML syntax, the Receiver shall generate a Response Status Code indicating a "NOT_ACCEPTABLE" error.

- Primitive specific operation on Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed" in addition:

- If semanticOpExec attribute exists in the Request, the Hosting CSE shall update the semantic triples in the descriptor attribute according to SPARQL update request in the semanticOpExec attribute. If the SPARQL update request can not be executed, the Hosting CSE shall create an unsuccessful Response primitive" with the Response Status Code indicating "SPARQL_UPDATE_ERROR", otherwise proceed to step Recv-6.6.

- The hosting CSE shall set the validationEnable attribute of the addressed <semanticDescriptor> resource based on the value provided in the request and its local policy. Note that the local policy may override the suggested value provided in the request from the originator to enforce or disable the following semantic validation procedures. There are different cases depending on how the local policy is configured (which is out of the scope of this specification) and whether/how the validationEnable attribute is provided in the request:

      - no change to the existing validationEnable attribute if it’s not provided in the request;

      - validationEnable attribute is not present if the local policy doesn’t allow for the validationEnable attribute.

      - validationEnable attribute is set as ‘True’ or ‘False’ according to the local policy no matter how the value is provided in the request;

      - validationEnable attribute is set as ‘True’ or ‘False’ according to the value provided in the request;

- The hosting CSE shall perform step 2b-2l as specified in clause 7.4.29.2.1.

- If validationEnable attribute is changed from ‘True’ to ‘False’, then the hosting CSE shall set the semanticValidated attribute of the addressed <semanticDescriptor> resource as ‘False’.

##### Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

No change from the generic procedures in clause 7.2.2.2.

### -----------------------End of change 1------------------------------------------