| CHANGE REQUEST |
| --- |
| Meeting:* | PRO TP32 |
| Source:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Date:* | 2017-10-17 |
| Contact:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Reason for Change/s:* | Add new function of 3GPP location reporting for <locationPolicy> |
| CR against: Release* | <Release3> |
| CR against: WI* | Active <WI-0058 - 3GPP & Cellular IoT Interworking> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V3_4_0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is updated according to the agreed CR ARC-2017-0272R03-TS-0001-locationPolicy_updating_for_MonitoringEvent(UE_Location_Report)  and ARC-2017-0275R03-TS-0026-UE_Location_Reporting_Solution.

### -----------------------Start of change 1-------------------------------------------

### Annex G (normative): 
Location request

### G.3 Location request by means of 3GPP MonitoringEvent API

    - G.3.1 Introduction

This 3GPP MonitoringEvent API for Terminal Location reproting[xx] is generally used to open up service capabilities, especially location capability, in the underlying network toward applications. This clause introduces the API interface and parameters to handle the oneM2M-specified location request. In addition, since this 3GPP MonitoringEvent API uses only HTTP as underlying message protocol, some binding mapping are mentioned in the procedures in the clause G.3.3.

G.3.2 Resource structure of 3GPP MonitoringEvent API for terminal location

When a CSE needs to request the geographical or physical location information of a target CSE or AE hosted in a M2M Node toward a location server located in the Underlying Network over Mcn reference point. The CSE shall request Terminal Location Query following Procedures for Terminal Location (see G.3.3 ).

The3GPP MonitoringEvent API for Terminal Location allows CSE to obtain information about geographical location of a terminal (e.g. Node in oneM2M TS-0001 [6]). In order to obtain location information, CSE shall use one of two services of the Terminal Location API(more detail is specified in the clause7.5.3 of TS-0026[yy]):

request the current Terminal Location in a single query toward a Location Server;

subscribe to notifications of Terminal Location updates.

Since oneM2M system utilizes the two services mentioned above, this clause introduces the capabilities that is related to the services from 3GPP MonitoringEvent API for Terminal Location [xx].

A CSE and a Node shall act as an application and a terminal respectively as described in in the clause7.5.3 of TS-0026[yy].

Table G.3.2-1: Applicable 3GPP MonitoringEvent API for Terminal Location

| Capability | Resource Type | Operations |
| --- | --- | --- |
|  |  | C | R | U | D |
| Location Monitoring | MonitoringEventSubscription | create a new subscription | return all subscriptions | no | no |
| Location Quering | MonitoringEventSubscription | no | return latest location of the terminal | no | no |

Based on Table G.3.2-1, the resource type, MonitoringEventSubscription shall be used for the location request specified in the oneM2M system. The resource type is described in the tables below. The table also contains the relevant attributes column that is correlated with either <locationPolicy> or <accessControlPolicy> resource type defined (3GPP TS 29.122 [xx]). Only attributes that may be utilized by oneM2M system are described. For the detailed information, see the [xx].

# Table G3.2-2: Definition of type MonitoringEventSubscription for Terminal Location

| Attributes | 3GPP MonitoringEvent API Defined Type | Description | Relevant Attribute defined by oneM2M |
| --- | --- | --- | --- |
| scsAsId | xs:integer | Identifies the IN-CSE |  |
| tltrId | xs:integer | Identifies the long-term transaction that identifies the present resource. |  |
| ttrId | xs:integer | Identifies the short-term transaction that can be used to correlate a request with its response. A new TTRI shall be assigned by the IN-CSE each time its sends an HTTP request. |  |
| externalIds | m2m:externalID |  | locationTargetID in the <locationPolicy> resource type |
| monitoringTypes | m2m:monitoringType | When it is used for Terminal Location, the value shall be LOCATION_REPORTING. |  |
| locationType | m2m:locationType | Only when the result of quering "Current Location" fail and the retrieveLastKnownLocation of <locationPolicy> is TRUE, the IN-CSE shall re-send the request to the Location Server and the locationType value shall be set to LAST_KNOWN_LOCATION. |  |
| accuracy | m2m:locationAccuracy | It’s based on a pre-provisioned policy setting. |  |

G.3.3 Procedures for terminal location

G.3.3.1 Request in a single query toward a location server

This procedure shows how to request and return location for a M2M Node. The details of this procedure is specified in the clause7.5.3.1 TS-0026[yy]

Figure G.3.3.1-1: Single Query Toward Location Server

- A Hosting CSE requests location for a single terminal (Node) by means of 3GPP MonitoringEvent for terminal location API. This request message shall contain terminal address and Request URL with the address of Location Server using RETRIEVE operation.
In this step, the MonitoringEventSubscription resource type described in Table G.3.2-2 shall be used with RETRIEVE operation and the locationType attributes of MonitoringEventSubscription resource shall be set CURRENT_LOCATION.

NOTE1: 	GET operation is used for this RETRIEVE operation.

- The Location Server shall retrieve the current location information of the terminal.

- After the successful retrieve, the Hosting CSE receives the location information.

- If the step 3 is failed and the retrieveLastKnownLocation attribute of <locationPolicy> is TRUE, the Hosting CSE shall retry the terminal  last location.

- A Hosting CSE requests location for a single terminal (Node) by means of 3GPP MonitoringEvent for terminal location API. This request message shall contain terminal address and Request URL with the address of Location Server using RETRIEVE operation.
In this step, the MonitoringEventSubscription resource type described in Table G.3.2-2 shall be used with RETRIEVE operation and the locationType attributes of MonitoringEventSubscription resource shall be set LAST_KNOWN_LOCATION.

NOTE2: 	GET operation is used for this RETRIEVE operation.

- The Location Server shall retrieve the last known location information of the terminal.

- After the successful retrieve, the Hosting CSE receives the location information.

G.3.3.2 Subscribe to notifications for area updates

This procedure shows how to subscribe to area update notification. he details of this procedure is specified in the clause7.5.3.2 TS-0026[yy]

Figure G.3.3.2-1: Subscribe to Notification for Area Updates

- Based upon the location configuration by the Hosting CSE , the Hosting CSE shall create a new area notification subscription to track the terminal's movement in relation to the geographical area update. In this step, the MonitoringEventSubscription resource type described in Table G.3.2-2  shall be used with CREATE operation.

NOTE 1: 	POST operation is used for this CREATE operation.

- After the successful creation of subscription, the Hosting CSE shall receive the response.

- When the target terminal location area updates, the location server shall notify the application of current location information.

In this step, the notification message shall be used as NOTIFY operation.

NOTE 2: 	POST operation is used for this NOTIFY operation

- After the successful receiver of notification, the Hosting CSE shall send a response to the location server.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?