| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO #32 |
| Source:* | Bob Flynn, Convida, Flynn.Bob@convidawireless.com Dale Seed, Convida, Seed.Dale@convidawireless.com |
| Date:* | 2017-10-19 |
| Reason for Change/s:* | Mapping of oneM2M and 3GPP parameters for Device Trigger |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <WI-0058> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v 3.4.0 |
| Clauses * | Annex B.1. |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides changes for parameter data type mapping between oneM2M and 3GPP for Device Trigger request/response and Notification messages via the 3GPP defined T8 interface APIs.

Note, TS-0004 currently describes the device trigger procedure and the APIs over Mcn using the 3GPP defined Tsp interface. This contributions adds a new sub-section for device triggering over the T8 interface.

### -------------- start of change to 1 ----------------------------------

  - Device triggering

    - Providing device triggering service by means of 3GPP networks (Tsp)

      - Introduction

3GPP Underlying Network has defined a dedicated interface for requesting device triggering. The normative references for applicable interfaces are as follows: 3GPP TS 23.682 [15]. The specification for the interface Tsp is described in 3GPP TS 29.368 [16]. Tsp interface uses Diameter Base Protocol as specified in IETF RFC 3588 [13], in order to use such an interface the CSE shall act as a Diameter client as described in IETF RFC 6733 [14].

Before the CSE initiates the device triggering, the CSE and MTC-IWF shall execute the procedures once as specified in 3GPP TS29.368 [16].

      - Device action request command

When a CSE needs to issue a device triggering request to the MTC-IWF, the CSE shall send a Device-Action-Request (DAR) command (for detail, see TS 29.368 [16]). The following list provides the parameters mapping between the oneM2M and 3GPP.

Either External-Id or MSISDN: the CSE maps it to the M2M-Ext-ID, see clause 6.2.

SCS identifier: the CSE maps it to the CSE-ID, see clause 6.2.

Application Port Identifier: the CSE maps it to Trigger-Recipient-ID, see clause 6.2.

Payload: the CSE maps it to the Trigger Payload, see clause 9.2.  The payload is provided to the 3GPP network as an OctetString via the payload AVP of the DAR command.

      - Device action answer command

As a result of device triggering request to MTC-IWF, the CSE receives a Device-Action-Answer (DAA) command (for detail, see TS 29.368 [16]).

      - Device notification request command

As a report of the result for device triggering delivery by 3GPP network, the CSE receives a Device-Notification-Request (DNR) command (for detail, see TS 29.368 [16]).

      - Device notification answer command

As a result of device notification request to MTC-IWF, the CSE sends a Device-Notification-Answer (DNA) command (for detail, see TS 29.368 [16]).

    - Providing device triggering service by means of 3GPP networks (T8 Interface)

      - Introduction

3GPP also supports device triggering via the T8 interface defined in TS 23.682 [15]. The protocol specification for the T8 interface is described in 3GPP TS 29.122 [45]. Additional details are provided in clause 7.5 of TS-0026[44].

      - Device Triggering Request/Confirmation

The CSE may initiate a Device Trigger Request to an ASN/MN-CSE or ADN-AE to have it establish a connection to the IN-CSE, enrol to a MEF, register to the IN-CSE, update its PoA, or perform a CRUD operation on a specified resource. The message shall include procedure-specific parameters which are derived as indicated in the following table. The data formats need to be converted accordingly.

Table B.3.2-1: Device Triggering Mapping

| 3GPP parameter | oneM2M attribute/dataType | References and notes |
| --- | --- | --- |
| scsAsId | m2m:ID | Identifier of the SCS/AS. Pre-provisioned to IN-CSE. |
| tltrId | xs:positiveInteger | Long term transaction identifier. Assigned by IN-CSE based on internal policies/pre-provisioning. |
| ttrId | xs:positiveInteger | Short-term transaction identifier to correlate request and response. Assigned by IN-CSE based on internal policies/pre-provisioning. |
| self | xs:anyURI | Assigned by SCEF and returned in Monitoring Event Subscription response. |
| trigger reference number | xs:positiveInteger | Uniquely identifies the device trigger transaction. Assigned by the CSE. |
| validity period | m2m:timestamp | Assigned based on internal IN-CSE policies or via the triggerValidityTime atribute of <triggerRequest> |
| priority | xs:nonNegativeInteger | Identifies priority of the device trigger. 0 indicates trigger is non priority and 1 indicates priority. Assigned based on internal IN-CSE policies |
| applicationPortId | m2m:triggerRecipientID | Assigned based on internal IN-CSE policies or via the Trigger-Recipient-ID attribute of <triggerRequest> |
| triggerPayload | See clause 9.2.1 |  |
| notificationDestination | xs:anyURI | Assigned by IN-CSE. May contain the corresponding <triggerRequest> resource URI. |

      - Device Triggering Delivery Report Notification

The SCEF receives a device triggering delivery report notification as a result of device triggering. The following table provides the parameter mappings between oneM2M and 3GPP.

Table B.3.3-1: Device Triggering Delivery Report Notification Mapping

| 3GPP parameter | oneM2M attribute | References and notes |
| --- | --- | --- |
| tltrId | xs:positiveInteger |  |
| result | m2m:triggerStatus |  |

### -----------------end of change 1 ----------------------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?