| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO #32 |
| Source:* | Bob Flynn, Convida, Flynn.Bob@convidawireless.com Dale Seed, Convida, Seed.Dale@convidawireless.com Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com |
| Date:* | 2017-10-31 |
| Reason for Change/s:* | Mapping of oneM2M and 3GPP parameters for Monitoring Events |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <WI-0058> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v 3.4.0 |
| Clauses * | Annex B.1. |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides changes for parameter mapping between oneM2M and 3GPP for Montioring Event request/response and Notification messages. The mappings are w.r.t the T8 interface APIs defined for Monitoring Events procedure.

This contributions adds a section for Monitoring events over T8 interface.

R01 and R02 changes synchronize these changes with the content of PRO-2017-0319 and the fact that other contributions introduced additional B.x clauses

### -------------- start of change to 1 ----------------------------------

  - Monitoring Events

    - Providing monitoring service by means of 3GPP networks (T8 Interface)

      - Introduction

The 3GPP T8 interface supports monitoring events as defined by TS 23.682 [15]. The protocol specification for the T8 interface is described in 3GPP TS 29.122 [45]. Additional details are provided in clause 7.4 of TS-0026[44].

      - Monitoring Event Subscription

The monitoring event subscription message is sent from the IN-CSE to the SCEF. The following table is a mapping of the paramters of this message between oneM2M and 3GPP.

Table B.4.1.2-1: Monitoring Event Subscription Mapping

| 3GPP parameter | oneM2M dataType | References and notes |
| --- | --- | --- |
| scsAsId | m2m:ID | Identifier of the SCS/AS. Pre-provisioned to IN-CSE. |
| tltrId | xs:positiveInteger | Long term transaction identifier. Assigned by IN-CSE based on internal policies/pre-provisioning |
| ttrId | xs:positiveInteger | Short-term transaction identifier to correlate request and response. Assigned by IN-CSE based on internal policies/pre-provisioning |
| self | xs:anyURI | Assigned by SCEF and returned in Monitoring Event Subscription response. |
| externalId | m2m:externalID | Configured by IN-CSE with the M2M-Ext-ID of the UE to be monitored. |
| msisdn | - | Not currently used by IN-CSE |
| externalGroupId | m2m:externalID | Configured by IN-CSE with the externalGroupID of the group being monitored. |
| notificationDestination | xs:anyURI | Set to a URI of the IN-CSE to which the SCEF should forward the Monitoring Event Notifications to. Assigned by IN-CSE based on internal policies/pre-provisioning |
| monitoringTypes | xs:positiveInteger | Type of monitoring subscription. Assigned by IN-CSE based on type of monitoring that is applicable. Permitted Values: LOSS_OF_CONNECTIVITY (0) UE_REACHABILITY (1) LOCATION_REPORTING (2) CHANGE_OF_IMSI_IMEI_ASSOCIATION (3) ROAMING_STATUS (4) COMMUNICATION_FAILURE (5) AVAILABILITY_AFTER_DDN_FAILURE (6) NUMBER_OF_UES_IN_AN_AREA (7) |
| maximumNumberOfReports | xs:positiveInteger | Identifies the max number of requested monitoring reports. Assigned by IN-CSE based on internal policies/pre-provisioning |
| monitoringTime | m2m:timestamp | Identifies the absolute time at which the related monitoring event request is to expire Assigned by IN-CSE based on internal policies/pre-provisioning |
| groupReportingGuardTime | m2m:timestamp | Identifies the absolute time for which the SCEF can aggregate the monitoring event reports detected by the UEs in a group and report them together to the IN-CSE. Assigned by IN-CSE based on internal policies/pre-provisioning |
| maximumDetectionTime | xs:positiveInteger | If "monitoring-Type" is “LOSS_OF_CONNECTIVITY”, this parameter may be included to identifiy the maximum period of time (in seconds) after which the UE is considered to be unreachable Assigned by IN-CSE based on internal policies/pre-provisioning |
| reachabilityType | xs:string | If "monitoring-Type" is “UE_REACHABILITY”, this parameter shall be included to identifiy whether the request is for Reachability for SMS or Reachability for Data, or both. Assigned by IN-CSE based on internal policies/pre-provisioning. Permitted Values: “SMS” - Reachability for SMS “DATA” - Reachability for Data "SMS_AND_DATA" - Both |
| maximumLatency | - | Not currently used by IN-CSE. |
| maximumResponseTime | - | Not currently used by IN-CSE. |
| suggestedNumberOfDlPackets | - | Not currently used by IN-CSE. |
| idleStatusIndication | xs:boolean | If "monitoringType" is set to " “UE_REACHABILITY"” or "AVAILABILITY_AFTER_DDN_FAILURE", this parameter may be included to indicate the notification of when a UE, for which PSM is enabled, transitions into idle mode. - "true": indicate enabling of notification - "false": indicate no need to notify Default: "false". Assigned by IN-CSE based on internal policies/pre-provisioning and <schedule> child resource of <node> resource if present. |
| locationType | xs:string | If "monitoringType" is " “LOCATION_REPORTING"” or " NUMBER_OF_UES_IN_AN_AREA ", this parameter shall be included to identify whether the request is for Current Location or Last known Location. Permitted values: "CURRENT_LOCATION": The request is for “Current Location” "LAST_KNOWN_LOCATION": The request is for “Last known Location”. Assigned by IN-CSE based on retrieveLastKnownLocation in locationPolicy resource. The value will be set to "CURRENT_LOCATION" if the retrieveLastKnownLocation is false and set to "LAST_KNOWN_LOCATION" if retrieveLastKnownLocation value is true in loctionPolicy resource. |
| accuracy | xs:string | If "monitoring-Type" is “LOCATION_REPORTING”, this parameter may be included to identify the desired level of accuracy of the requested location information. Permitted values: “CGI_ECGI”: The reporting accuracy is at cell level; “ENODEB”: The reporting accuracy is at eNodeB level; “TA_RA”: The reporting accuracy is at the TA/RA level. PLMN": The reporting accuracy is at the PLMN level. Assigned by CSE based on internal policies/pre-provisioning |
| minimumReportInterval | xs:positiveInteger | If "monitoring-Type" is “LOCATION_REPORTING”, this parameter may be included to identify a minimum time interval (in seconds) between Location Reporting notifications. Assigned by CSE based on the locationUpdatePeriod attribute defined in the corresponding <locationPolicy> resource and/or internal policies/pre-provisioning. |
| associationType | xs:string | If "monitoring-Type" is “CHANGE_OF_IMSI_IMEI_ASSOCIATION”, this parameter shall be included to identify whether the change of IMSI-IMEI or IMSI-IMEISV association shall be detected. Permitted values: “IMEI”: The value shall be used when the change of IMSI-IMEI association shall be detected; “IMEISV”: The value shall be used when the change of IMSI-IMEISV association shall be detected; Assigned by CSE based on internal policies/pre-provisioning |
| PLMNIndication | xs:boolean | If "monitoring-Type" is “ROAMING_STATUS”, this parameter may be included to indicate the notification of UE's Serving PLMN ID. Permitted values: "true": The value shall be used to indicate enabling of notification; "false": The value shall be used to indicate disabling of notification. Default: "false". Assigned by CSE based on internal policies/pre-provisioning |
| geographicArea | See Note. | If "monitoring-Type" is “NUMBER_OF_UES_IN_AN_AREA”, this parameter shall be included to indicate the area within which the IN-CSE requests the number of UEs. Assigned by CSE based on internal policies/pre-provisioning |

Note: TS 29.122 [45] is still under active development.  Hence there may be some discrepancies between TS 23.682 [15] and TS 29.122 [45] which need to be resolved and in turn the above table and/or TS-0026 may need to be updated accordingly (e.g. monitoringDuration, geographicArea)

      - Monitoring Event Notification

The monitoring event notification message is sent from SCEF to the IN-CSE. The following table provides the mapping between the oneM2M and 3GPP data types. The message shall include procedure-specific parameters which are derived as indicated in the following table.

Table B.4.1.3-1: Monitoring Event Notification Mapping

| 3GPP parameter | oneM2M dataType | References and notes |
| --- | --- | --- |
| tltrId | xs:positiveInteger | Long term transaction identifier corresponding to the monitor event subscription. |
| ttrId | xs:positiveInteger | Short-term transaction identifier to correlate request and response. Assigned by SCEF |
| externalId | m2m:externalID | M2M-Ext-ID of the UE being monitored. |
| msisdn | - | Not currently used by IN-CSE |
| monitoringType | xs:positiveInteger | Type of monitoring notification Permitted Values: LOSS_OF_CONNECTIVITY (0) UE_REACHABILITY (1) LOCATION_REPORTING (2) CHANGE_OF_IMSI_IMEI_ASSOCIATION (3) ROAMING_STATUS (4) COMMUNICATION_FAILURE (5) AVAILABILITY_AFTER_DDN_FAILURE (6) NUMBER_OF_UES_IN_AN_AREA (7) |
| idleTimestamp | m2m:scheduleEntry | Clause 7.4.9 - the start of the scheduleElement is based on the Idle Timestamp |
| TAUTimer | m2m:scheduleEntry | Clause 7.4.9 - periodicity of the scheduleElement equal to the TAU/RAU Timer |
| activeTimer | m2m:scheduleEntry | Clause 7.4.9 - the duration of the scheduleElement indicates the Active Time value |
| associationType | xs:string | If "monitoring-Type" is “CHANGE_OF_IMSI_IMEI_ASSOCIATION”, this parameter shall be included to identify whether the change of IMSI-IMEI or IMSI-IMEISV association shall be detected. Permitted values: “IMEI”: The value shall be used when the change of IMSI-IMEI association shall be detected “IMEISV”: The value shall be used when the change of IMSI-IMEISV association shall be detected; |
| PLMNId | m2m:networkID | Indicates the PLMN ID to which the UE is attached. |
| roamingStatus | xs:string | If "monitoringType" is “ROAMING_STATUS”, this parameter shall be included to indicate whether the UE is on roaming status or not. Enumeration of Roaming Status. Permitted values: “ROAMING”: The UE is roaming “NOT_ROAMING”: The UE is not roaming |
| latitude | xsd:float | If "monitoringType" is “LOCATION_REPORTING”, this parameter indicates the latitude value for the UE. |
| longitude | xsd:float | If "monitoringType" is “LOCATION_REPORTING”, this parameter indicates the longitude value for the UE. |

Note: TS 29.122 [45] is still under active development.  Hence there may be some discrepancies between TS 23.682 [15] and TS 29.122 [45] which need to be resolved and in turn the above table and/or TS-0026 may need to be updated accordingly (e.g. idleTimestamp, TAUTime, activeTimer, associationType, PLMNId)

### -----------------end of change 1 ----------------------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?