| Input contribution Use case |
| --- |
| Use Case Title:* | Smart Meter Reading Use Case |
| Group Name:* | WG1 (REQ) |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Dilip Krishnaswamy, Qualcomm, dilipk@qti.qualcomm.com Farrokh Khatibi, Qualcomm, fkhatibi@qti.qualcomm.com Yenamandra Rao, Qualcomm, ysrao@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Mark Klerer, Qualcomm, mklerer@qualcomm.com |
| Date:* | 2013-2-25 |
| Abstract:* | This contribution provides selected Smart Grid use cases extracted from the work done in Smart Grid Interoperability Panel (SGIP) and OpenSG users group |
| Agenda Item:* | 4.2 |
| Work item(s): | WI 0001 |
| Document(s) Impacted* | TR ‘oneM2M use case collection’ |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to include the proposed use case description into the use cases TR. |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Smart Meter Reading Use Cases

## Description

### This contribution provides selected Smart Meter Reading use cases

## Source

### Qualcomm (contributor), use case information extracted from SGIP/OpenSG

## Actors

### Smart Meters (SM), Data Aggregation Points (DAPs), Advanced Metering Infrastructure (AMI) Head-end, Meter Data Management System (MDMS), Customer Information System (CIS)

## Pre-conditions (if any)

### Availability of meter data

## Triggers (if any)

### Smart meter on-demand or bulk interval meter read request events

## Smart Grid Use Case Overview

Smart Grid Interoperability Panel (SGIP)(http://www.sgip.org) and OpenSG users group (http://osgug.ucaiug.org/default.aspx)  have been leading this effort in North America. An informative document has been submitted to OneM2M based on the SGIP activity. In general, a number of external organizations such as the SGIP or the SGCG (Smart Grid Coordination Group) in Europe have been working to define use cases for Smart Grid (SG). Portals such as the SGI Clearing House (http://www.sgiclearinghouse.org) to assist with distributing information about smart grid initiatives in the US. The use-cases presented are derived in part from the above publicly available information.

## The SG-NET Diagram

Figure 1  shows the conceptual actors/data flow diagram based on a more detailed diagram developed by SG-Net. The more detailed diagram developed by SG-Net can be seen in the associated submission related to SGIP-based Smart Grid Use Cases.

In Figure 1, each element is an “actor” that is communicating with another actor using the shown data flows. As an example, consider “Smart Meter” in the “Customer” quadrant (lower right). Smart Meter (SM) communicates with a number of other actors, such as a Data Aggregation Point (DAP) located in the AMI Network. The DAP can then transmit the aggregated data to the Utility Service Provider using the Wide Area Network. The meter reading information can reach the data center for the Utility Service Provider via the AMI Headend which can forward the information to the MDMS which can coordinate with the CIS to store/retrieve meter data and to determine customer billing information. In certain variations such as cellular-based smart metering systems, a DAP entity may be bypassed, or merely serve as a pass-through for the information flow between the utility data center and the smart meter.

Figure 1 - Conceptual Actors/Data Flow Diagram

## 1.7    Typical Flows

Flow A                                                                  Flow B

Figure 2: Typical Smart Meter Reading Flows

Typically, a utility data center processing application communicates end-to-end via the AMI Headend with a smart meter data application at the edge. Figure 2 shows two possible flows A and B depending on whether there is a DAP entity along the path from the Utility Data Center / AMI Headend and the Smart Meter.

In flow A, the Utility Data Center / AMI Headend can make a request to the Smart Meter directly. Typically there may be 3 to 6 such requests per day (typically < 10 times per day). The request could indicate that the current meter reading is desired. Alternatively, multiple meter readings over a period of time such as for a few hours (e.g. from 2 p.m. to 8 p.m.) for a given day or across days could be requested. The Smart Meter completes the request and communicates it back to the Utility Data Center / AMI HeadEnd. Typical in such on-demand or bulk-interval read requests, a reasonably immediate response is desired of the order of a few seconds, so that there is not necessarily any significant delay tolerance allowed for the response. However, it is possible that, in current systems or in future systems, such requests could optionally carry a delay tolerance associated with the request depending on the urgency of the request. The size of the meter reading response can be of the order of a few tens to hundreds of bytes, and is also implementation dependent.

In flow B, the Utility Data Center / AMI Headend can make a request to the Smart Meter that can be received via the DAP. Typically there may be 3 to 6 such requests per day (typically < 10 times per day). The request could indicate that the current meter reading is desired or that multiple meter readings over a period of time are desired. The Smart Meter completes the request and sends its response to the DAP. This response from the Smart Meter to the DAP is typically desired in the order of 15 to 30 seconds, as suggested in the submitted informative document related to SGIP-based Smart Grid Use Cases. However the actual delay in processing can be implementation dependent across smart metering systems across the world. The size of the meter reading response can be of the order of a few tens to hundreds of bytes, and is also implementation dependent. The DAP entity can subsequently buffer the data for some time, receive data from many meters, and then submit the aggregated data across meters to the Utility Data Center / AMI Head End. The duration for which the DAP may buffer data can be implementation dependent, and could last for several seconds or minutes. In some variants, the DAP may serve merely as a router, so that it directly forwards the smart meter response to the Utility Data Center / AMI HeadEnd without performing any aggregation tasks. In further variants, the DAP entity could be merely a virtual processing entity and not a physical one, where such a virtual entity could even potentially reside on the other side (not shown) of the wide area network associated with the Utility Data Center / AMI Head End.

## 1.8   Summary

To summarize, meter reading requests could request a single meter reading or a set of meter readings. Such requests may occur a few times (typically < 10) per day and can be of the order of a few tens of bytes. Meter reading responses can be of the order of a few 10s to 100s of bytes typically.  Meter reading responses are typically expected in the order of a few seconds after reception of the request at the meter. Any delay tolerance associated with such requests can be optional or implementation dependent. In some system variants, a DAP entity may not exist at all so that the Utility Data Center / AMI Head End communicates directly with the smart meter. In other end-to-end system variants, a DAP entity may serve as an intermediate processing or forwarding entity between the Smart Meter and the Utility Data Center / AMI Head End. In such cases, the DAP entity may be either a physical or virtual processing entity in the end-to-end system and can assist with buffering and aggregating meter reading responses. The duration of buffering or aggregation at the DAP entity can be implementation dependent and could be of the order of a few seconds or minutes typically.