| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Potential Requirements (from LG Electronics’ Use Cases) |
| Source:* | LG Electronics |
| Contact: | Hongbeom Ahn, LG Electronics, hongbeom.ahn@lge.com Seungmyeong Jeong, LG Electronics, seungmyeong.jeong@lge.com |
| Date:* | 2013-03-29 |
| Abstract:* | This contribution consists of potential requirements from LG Electronics’ use cases (Car/Bicycle Sharing and Smart Parking). This also includes a new requirement. |
| Agenda Item:* | REQ |
| Work item(s): |  |
| Document(s) Impacted* | Requirement TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

| ID | Classification | Use Case | Requirement Text |
| --- | --- | --- | --- |
| R-001 | Overall System – Various Devices Support | REQ-2013-0132R01 | The M2M System shall support mobile/portable M2M Gateway and/or M2M Device. |
| R-002 | Functional-Collecting/ Reporting | REQ-2013-0132R01 | The M2M System shall support to distinguish the event levels for collecting, storing and reporting. |
| R-003 | Functional-Collecting/ Reporting | REQ-2013-0132R01 | Based on the condition of the M2M Gateway and/or Device, the M2M System shall provide the capability to change the report and/or notification configurations. (e.g., schedule of the report and condition of the notification). Note: for example, if the battery of Gateway is remained only 10% or below, the M2M System will automatically change the report and/or notification configurations to make the Gateway operate longer. |
| R-004 | Access Right | REQ-2013-0132R01 | The M2M System shall support to process access right requests of a resource and grant the requests if the requests are appropriate. |
| R-005 | Charging | REQ-2013-0169R01 | The M2M System shall support mechanisms to correlate charging data/records collected from different M2M Application Service Providers. |
| R-006 | Access Right | REQ-2013-0169R01 | The M2M System should support mechanisms to provide data to the authorized stakeholder (e.g., police center) without grant of the data owner. Note: Privacy of individual parties must be respected as appropriate. |
| R-007 | Triggering | REQ-2013-0169R01 | The M2M System shall support triggering M2M Devices to report on-demand regarding collected data from other M2M Devices. |
| R-008 | Functional-Connectivity | N/A | The M2M System shall support seamless replacement/switching for M2M Devices as well as M2M Gateways. |

Note (Definitions from REQ TS draft):

- M2M Application Service: an M2M Application Service is realized through the service logic of an M2M Application and is operated by the end user or an M2M Application Service Provider.

- M2M Service: is the set of functionalities that a M2M Service Capability Layer makes available through the standardized interfaces.