| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Input requirements on management for REQ-2012-0035 |
| Source:* | Alcatel-Lucent (ETSI) |
| Contact: | timothy.carey@alcatel-lucent.com |
| Date:* | 2013-02-23 |
| Abstract:* | This contribution provides the aggregated comments for management requirements that were part of oneM2M-REQ-2012-0035R04. |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | WI0001 |
| Document(s) Impacted* | Technical Specification - M2M Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Status update for discussion of oneM2M Requirement TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Background

The following table shows the changes made to original requirements based on comments received in the requirement evaluation matrix.

| Temporary Req ID | Description | Comments Received |
| --- | --- | --- |
| HLR-136 | The M2M System shall provide the capability to discover the capillary network including the device information and network topology. | Telecom Italia Why the topology? Seems application specific InterDigital Redundant HLR51,HLR52 Fujitsu Needs confirmation of the necessity of having the "network topology" info. NTT Items related to "discovery" should be merged as a unique "high level requirements". LGE Terms are too technical and specific Cisco Disagree ALU Duplicate of HLR 13, 14, 15 Motorola Superseded by HLR-138 |
| HLR-138 | The M2M System shall provide the capability to maintain and describe the information model of devices and topology of a capillary network. | Telecom Italia Why the topology? Seems application specific KDDI Needs clarification for topology. InterDigital Could it be re-worded so it is not as application/vertical specific? Fujitsu Shall -> may LGE Superseded by row 83; overlap row 105, 155 Cisco Out of scope topology of a capillary network Overlap Superseded by HLR-136 ALU Overlap with HLR-56 Motorola why you need info on the whole topology? Model for device and the parameters of capillary network are enough |

| HLR-143 | The M2M System shall be capable of administering services provided to the M2M System by the underlying Communication Network. | Telecom Italia As exposed byt the underlying network and authorized by the underlaying network operator. InterDigital Needs clarification. Is the point that it needs to provide the communication Network the capability to administer its services? If not see text proposal Overlap with HLR-32, HLR-33 Gemalto May need to clarify "administering services" Fujitsu Shall -> may LGE What is administering services? And why the services are provided by underlying comms network? ALU Redundant HLR 56 Sprint what do you mean by "administering services"? I need to understand this before being able to decide that I agree. |
| --- | --- | --- |
| HLR-137 | The M2M System shall provide the capability to notify the changes of the capillary network including the device information and network topology. | Telecom Italia Why the topology? Seems application specific Fujitsu shall -> may LGE Capillary network can be reworded. Change notification can be included in maintainence (124). Superseded by HLR-138 Cisco Disagree Overlap with HLR-136 Motorola To whom the notification could be provided to needs to be clarified and there are undefined terms such as capillary network Sprint Specify an object of the notification in order to make this requirement more clear. |
| HLR-144 | The M2M System shall be capable of maintaining configuration information of M2M Gateways/M2M Devices associated with a M2M service subscription. | NTT DoCoMo Needs definition on "M2M Service Subscription". LGE Too specific as a function, not a REQ. Cisco The M2M System shall be capable of maintaining configuration information of M2M Devices associated with a M2M service subscription. ALU The M2M System shall be capable of maintaining configuration information of M2M Applications associated with a M2M service subscription. |
| HLR-133 | The M2M System shall be capable of executing the following types of diagnostics initiated by a M2M Device: · One-time, on demand, synchronous · One-time, on demand, asynchronous · Scheduled, synchronous · Scheduled, asynchronous | KDDI "shall" should be changed to "should" or "may". NTT_DoCoMo Patterns listed here seems not cover all cases. Need clarification or note. Fujitsu shall -> may NTT Items related to "diagnostic" should be merged as a unique "high level requirements". LGE Device initiation only? Can be initiated by M2M System/Gateways, too. Cisco The M2M System shall be capable of executing diagnostics as requested by a M2M Device: ALU The M2M System shall be capable of executing the following types of diagnostics initiated by a M2M Application: Motorola Compared to 168, this is more specific about the type of diagnostic expected, but why initiated by the device? |
| HLR-155 | The M2M System shall be capable of executing diagnostics initiated by a M2M Device to assess connectivity within the Connectivity Layer. | KDDI "shall" should be changed to "should" or "may". InterDigital Redundant with HLR-156 Fujitsu shall -> may NTT Items related to "diagnostic" should be merged as a unique "high level requirements". LGE Not understandable. What does assessment of connectivity within the Connectivity Layer mean? ALU The M2M System shall be capable of executing the following types of diagnostics initiated by a M2M Application: Motorola Compared to 168, this is more specific about the type of diagnostic expected, but why initiated by the device? |
| HLR-156 | The M2M System shall be capable of executing diagnostics initiated by a M2M Device to assess connectivity within the M2M Service Capability Layer. | LGE Not understandable. What does assessment of connectivity within the M2M Service Capability Layer mean? ALU The M2M System shall be capable of executing diagnostics initiated by a M2M Application to assess connectivity within the M2M Service Capability Layer. Motorola Compared to 168, this is more specific about the type of diagnostic expected, but why initiated by the device? |
| HLR-019 | The M2M System shall be capable of retrieving events and information logged by a M2M Gateway or Device. | Gemalto "M2M system" = which stakeholders? Some applications may not want anyone to access their "information" ALU Overlap HLR-016 Motorola The requirement is written in a manner internalised manner, therefore suggest that the M2M system provides the capability (i.e. to an entity using the M2M system) of retriving logged events and information Sprint Disagree – Overlap HLR-018 |
| HLR-167 | The M2M System shall be capable of retrieving events and information logged by a M2M Application . | Gemalto "M2M system" = which stakeholders? Some applications may not want anyone to access their "information" LGE M2M Application in Device Domain? Motorola Would it not be the M2M system that logged application events, or is the intention that the M2M system provides specific event logging capabilities to applications? The requirement is written in a manner internalised manner, therefore suggest that the M2M system provides the capability (i.e. to an entity using the M2M system) of retriving logged events and information. Sprint Disagree – Overlap HLR-018 |
| HLR-161 | The M2M System shall be capable of retrieving information related to the environment (e.g., battery, memory, current time) of a M2M Gateway or Device. | InterDigital The M2M System shall be capable of providing the context aware service related to the environment (e.g., battery, memory, current time) Gemalto Not all applications want a third party provider, as implied by "M2M System", to access such information "M2M system shall enable applications to…" Cisco Superseded by HLR-033 ALU The M2M System shall be capable of retrieving information related to the environment (e.g., battery, memory, current time) of a device that hosts the M2M Application. Sprint The M2M System shall be capable of retrieving information related to the operating condition (e.g. battery level, memory usage, current time, etc.) of a M2M Gateway or M2M Device. |
| HLR-169 | The M2M System shall provide the capability to manage devices enabled by different management technologies in a unified manner. | InterDigital example for our clarification? Motorola Concern that it's too open ended, since there are no bounds on the number of management technologies. What would appear useful is a generic means to add support for additional management technologies. |
| HLR-170 | The M2M System shall provide the capability to manage multiple devices in a grouped manner. |  |
| HLR-171 | The M2M System shall provide the capability to manage the devices in a capillary network when supported by the device, including: · Provisioning & configuration · Diagnostics · Software Management · Device Reset | Motorola Missing definition of capillary network. Such services would seem to be supported via the gateway, which is not mentioned. "supported by the device" - which device? LGE define "capillary network" or delete "in a capillary network" Cisco List is not complete The M2M System shall provide the capability to manage devices when supported by the device, including: · Provisioning & configuration · Diagnostics · Software Management · Device Reset ALU The M2M System shall provide the capability to manage the devices in a M2M Area Networkk when supported by the device, including: · Provisioning & configuration · Diagnostics · Software Management · Device Reset Sprint Split this into separate requirements: 1) The M2M System shall provide the capability to manage management-enabled devices in a capillary network. 2) The M2M System shall provide the capability to provision and configure management-enabled devices in a capillary network. 3) ... |
| HLR-172 | The M2M System shall provide the capability to manage the network topology of a capillary network when supported by the capillary network technology, including: · Adding/removing devices to/from the capillary network · Modifying the interconnection relationship between devices | Motorola It's not clear that network topology is within the scope of oneM2M, however it would seem reacting and managing changes to the capillary network triggered by the capillary technology would be. LGE Disagree – Out of Scope Cisco Disagree ALU The M2M System shall provide the capability to manage the network topology of a M2M Area Network when supported by the M2M Area Network technology, including: · Adding/removing devices to/from the M2M Area Network · Modifying the interconnection relationship between devices Sprint Split this into separate requirements: |
| HLR-157 | The M2M System shall be capable of updating the firmware of a M2M Gateway or Device . | Orange The M2M System shall be capable of updating the firmware of a M2M Gateway or Device in the respect of the M2M Gateway / Device operator rules. ATT The M2M System shall be capable of updating the firmware of a M2M Gateway or Device with the coordination of underlying networks . Gemalto Is it the M2M System or M2M application that is in charge of devices and their firmware? "shall enable authorized entities to update the firmware…", use generic wording to combine with 195 and 197: " software or firmware on devices/gateways/servers" Fujitsu Shall->may NTT Items related to "software/firmware distribution" should be merged as a unique "high level requirements". Cisco The M2M System shall be capable of updating the firmware/software of an M2M Device . ALU The M2M System shall be capable of updating the firmware of a device or server that hosts the M2M Application. Motorola It appears likel y that device management enablers such as OMA-DM & BBF-069 will be reused and therefore it seems that the M2M system would faciliate the use of such enablers, rather than trigger such actions itself. |
| HLR-158 | The M2M System shall be capable of scheduling an update for the firmware of a M2M Gateway or Device . | Orange The M2M System shall be capable of scheduling an update for the firmware of a M2M Gateway or Device taking due account of M2M Gateway / Device operator needs. ATT The M2M System shall be capable of scheduling an update for the firmware of a M2M Gateway or Device with the coordination of underlying networks Gemalto "…upon request from authorized entities", use generic wording to combine with 196 and 198 Fujitsu Shall->may NTT Items related to "software/firmware distribution" should be merged as a unique "high level requirements". Cisco The M2M System shall be capable of scheduling an update for the firmware/software of an M2M Device . ALU The M2M System shall be capable of scheduling an update for the firmware of a a device o rserver that hosts the M2M Application . Motorola Dup of HLR-157 Does not appear to be sufficiently distinct |
| HLR-159 | The M2M System shall be capable of updating software modules that execute within the M2M Gateway or Device. | Orange The M2M System shall be capable of updating software modules that execute within the M2M Gateway or Device, in the respect of the M2M Gateway / Device operator rules. ATT The M2M System shall be capable of updating software modules that execute within the M2M Gateway or Device with the support of underlying networks. Gemalto "...updating executable software or firmware modules on devices/gateways/servers...": Combine with 193 and 197 Fujitsu Shall->may NTT Items related to "software/firmware distribution" should be merged as a unique "high level requirements". Cisco Superseded by HLR-157 ALU The M2M System shall be capable of updating software modules for M2M Applications. Motorola It appears likel y that device management enablers such as OMA-DM & BBF-069 will be reused and therefore it seems that the M2M system would faciliate the use of such enablers, rather than trigger such actions itself. |
| HLR-160 | The M2M System shall be capable of scheduling an update of software modules within the M2M Gateway or Device. | Orange The M2M System shall be capable of scheduling an update of software modules within the M2M Gateway or Device, taking due account of M2M Gateway / Device operator needs. ATT The M2M System shall be capable of scheduling an update for the firmware of a M2M Gateway or Device with the coordination of underlying networks Gemalto "…upon request from authorized entities", use generic wording to combine with 194 and 198 Fujitsu Shall->may NTT Items related to "software/firmware distribution" should be merged as a unique "high level requirements". Cisco Superseded by HLR-157 ALU The M2M System shall be capable of scheduling an update of software modules for M2M Applications. Motorola Dup HLR-159 |
| HLR-164 | The M2M System shall be capable of updating M2M Applications that execute within a Server . | ATT Definition of a server Gemalto "upon request from authorized entities", use generic wording to combine with 193 and 195 Fujitsu Shall->may NTT Items related to "software/firmware distribution" should be merged as a unique "high level requirements". LGE O, M2M Application in Network Domain is not in the Server. Network M2M Application just have a link to the Server Cisco Disagree updating the application software or forwarding device info? Motorola Our expectation is the application would trigger it's own update Sprint vague. What servers? Where? Any servers? Please update/rewrite. |
| HLR-165 | The M2M System shall be capable of scheduling an update for M2M Applications that execute within a Server. | Gemalto "…upon request from authorized entities", use generic wording to combine with 194 and 196 Fujitsu Shall->may NTT Items related to "software/firmware distribution" should be merged as a unique "high level requirements". LGE O, M2M Application in Network Domain is not in the Server. Network M2M Application just have a link to the Server Cisco updating the application software or forwarding device info? Motorola Dup HLR-164 |
| HLR-162 | The M2M System shall be capable of rebooting a M2M Gateway or Device. | Orange (to reword in order to express the fact that there shall not be intempestive rebooting; to check the authorization before rebooting…) ATT is the control initiated from service layer or from applications? The M2M System shall be capable of rebooting a M2M Gateway or Device. Gemalto What is the actual intention, e.g. "system shall support rebooting of..." or "application shall be capable of rebooting..." , why not also applicable to servers? Fujitsu Shall->may NTT Items related to "remote control" should be merged as a unique "high level requirements". Cisco Superseded by HLR-171 ALU The M2M System shall be capable of rebooting a device that hosts a M2M Application. |
| HLR-163 | The M2M System shall be capable of resetting a M2M Gateway or Device to a factory default configuration. | Orange (to reword in order to express the fact that there shall not be intempestive rebooting; to check the authorization before rebooting…) ATT The M2M System shall be capable of resetting a M2M Gateway or Device to a factory default configuration. Gemalto "upon request from authorized entities" Fujitsu Shall->may NTT Items related to "remote control" should be merged as a unique "high level requirements". Cisco Superseded by HLR-171 ALU The M2M System shall be capable of resetting a device that hosts a M2M Application to a factory default configuration. |
| HLR-166 | The M2M System shall be capable of administrating an M2M Application (start, stop, install, uninstall, restart) that executes within a Server. | Orange not clear enough NTT_DoCoMo Administration of an M2M Application is not limited to server but also applicable to device? ATT is the control initiated from service layer or from applications? Gemalto M2M application provider, not M2M SP, should be in control of M2M application on server side. Fujitsu Shall->may NTT Further clarification is required. Cisco Disagree Sprint Before I agree on this item, I need to understand what the intended function of this "Server" is. Right now this is too ambiguous for my taste. |

Proposed Requirements

The following table lists the proposed requirement text for oneM2M requirement TS.

TBD