| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Traffic Accident Information Collection |
| Source:* | CATT (CCSA) |
| Contact: | Wei Zhou, CATT, zhouwei@catt.cn Hui Xu, CATT, xuhui@catt.cn |
| Date:* | 2013-APR-03 |
| Abstract:* | This contribution contains some potential requirements to the M2M system when it is used for collecting traffic accident information through intelligent transportation system. |
| Agenda Item:* | Requirements |
| Work item(s): | WI 0001 - Requirements TS |
| Document(s) Impacted* | oneM2M-TR-0001-Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval and incorporation into oneM2M Requirement TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# 1. Proposal

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-0001 | General Requirements | A M2M device shall be able to connect WAN directly or via a gateway. |
| R-0002 | General Requirements | A M2M device shall be able to relay information among M2M devices. |
| R-0003 | General Requirements | A M2M device shall be able to automatically trigger a process when a predefined event happens. |
| R-0004 | General Requirements | A M2M device’s process can be manually triggered by the owner of device. |
| R-0005 | General Requirements | A M2M application can push information to another M2M application. |
| R-0006 | General Requirements | A M2M application shall be able to send service request to M2M platform. |
| R-0007 | Security Requirements | A M2M System shall support mutual-authentication among M2M device, M2M gateway and M2M platform. |
| R-0008 | Security Requirements | The information sent by M2M device or M2M platform shall use cryptographic technology to assure information authentication and information integrity. |
| R-0009 | Security Requirements | When M2M devices are used for collecting public information, the privacy of the device owner shall be protected. |
| R-0010 | Security Requirements | The commands given to M2M devices shall have time restriction and geography restriction. |