| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ#26 |
| Title:* | Editorial alignment of current requirements with definitions |
| Source:* | Joerg Swetina, NEC, Joerg.swetina@neclab.eu Walter Featherstone, Motorola, Josef Blanz, QualComm, jblanz@qti.qualcomm.com Rorand Hechwartner, Deutsche Telekom, roland.hechwartner@t-mobile.at |
| Contact: |  |
| Date:* | 2013-04-15 |
| Abstract:* | Consistency check and alignment of current requirements with existing definitions. New definitions are proposed where needed. Corresponding definitions are in oneM2M-REQ-2013-0161R02. This is the output of a 3 days workshop of the authors |
| Agenda Item:* |  |
| Work item(s): | Requirements, Vocabulary, Roles and Focus Areas for oneM2M Technical Work |
| Document(s) Impacted* | Requirements specification (oneM2M-TP-2012-0091-Draft_Requirement_TS) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss and adopt the proposed changes to the oneM2M Requirements TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

During 3 days the authors held a face-to-face meeting to check consistency of existing requirements in the requirements specification oneM2M-TS-0002-Requirements-V0_0_1  (currently available in oneM2M-TP-2012-0091-Draft_Requirement_TS) and seek alignment with definitions.

This activity resulted in proposed changes to the text of the requirements – contained in this document – and definitions and in the creation of missing definitions – contained in oneM2M-REQ-2013-0161R02-Essential_definitions_for_oneM2M.

The following changes to existing requirements proposed to be included into oneM2M-TS-0002-Requirements-V0_0_1.

In addition it is proposed to move all existing definitions of the requirements specification into the newly created oneM2M-TR-0004-Definitions_and_Acronyms-V0_0_1 to avoid duplication and potential inconsistency.

Begin Change

# 6	Functional Requirements

## 6.1	Overall System Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-001 | The M2M System shall support communication between M2M Applications and/or M2M Service Capabilities in the Infrastructure Domain, and the M2M Applications and/or M2M Service Capabilities in the Field Domain, by using communication means based on IP Access. NOTE: M2M Area Networks within the Field Domain need not support IP Access. | 1.0 |
| OSR-002 | The M2M System shall support communication means that can accommodate devices with constrained computing (e.g. small CPU, memory, battery) or communication capabilities (e.g. 2G wireless modem, certain WLAN node) as well as rich computing (e.g. large CPU, memory) or communication (e.g. 3/4G wireless modem, wireline) capabilities. | 1.0 |
| OSR-003 | The M2M System shall support the ability for two M2M Applications and/or M2M Service Capabilities to communicate through a session that enables: sequential delivery of data required QoS use of session handles (open / close) optionally, a persistent security context | 1.0 |
| OSR-004 | The M2M System shall support the ability for two M2M Applications and/or M2M Service Capabilities to communicate using requests and responses without the need for a session described in OSR-003 | 1.0 |
| OSR-005 | The M2M System shall be able to expose the services offered by Underlying Networks (SMS, USSD, geo-positioning, subscription configuration, authentication (e.g. Generic Bootstrapping Architecture), etc.) to M2M Applications. | 1.0 |
| OSR-006 | The M2M System shall be able to reuse the services offered by Underlying Networks by means of open access models (e.g. OMA, GSMA OneAPI framework). An example of available services is: IP Multimedia communications Messaging Geo-positioning Charging and billing services Device information and profiles Configuration and management of devices Triggering, monitoring of devices Small data transmission Group management Editor’s note: to be verifiable “open access models” need to be specific (with references). Also “shall be able to reuse” is unclear. Does it mean (a) it shall not be prevented or (b) oneM2M needs to specify a mapping to the open access interface ? | 1.0 |
| OSR-007 | Subject to access control, communication among M2M Applications and/or M2M Service Capabilities shall be supported across boundaries of M2M Service Capability Sets (MSCS) of different M2M Service Providers via oneM2M specified reference points. | 1.0 |
| OSR-008a | The M2M System shall provide the capability for M2M Applications and/or M2M Service Capabilities hosted on two or more entities out of the following M2M Service Infrastructure M2M Gateways M2M Devices to communicate with each other without the need for the M2M Applications to be aware of the Underlying Network technology. | 1.0 |
| OSR-008b | The M2M System shall support a mechanism that enables M2M Applications and/or M2M Service Capabilities to access information (obtain from / transmit to) of Edge Equipment without the need for the M2M Applications and/or M2M Service Capabilities to be aware of the specific communication protocol of the Edge Equipment. | 1.0 |
| OSR-009 This should go before OSR-007 | The M2M System shall support the ability for single or multiple M2M Applications and/or M2M Service Capabilities to interact with each other subject to access control. NOTE: equipment in the Field Domain (M2M Devices, M2M Gateways) and in the Infrastucture Domain host M2M Applications and/or M2M Service Capabilities. | 1.0 |
| OSR-010 | The M2M System shall support a confirmation mechanism for those M2M Applications requesting either acknowledged delivery of information and/or delivery of information within a given time constraint. | 1.0 |
| OSR-011 | The M2M System shall be able to request different communication paths from the Underlying Networks based on Network Operator and/or M2M Service Provider policies, routing mechanisms for transmission failures, or based on request from M2M Applications. | 1.0 |
| OSR-012 | The M2M System shall support communications among M2M Applications and/or M2M Service Capabilities via reference points specified by oneM2M, irrespective of whether they are continuously or non-continuously reachable via these reference points. | 1.0 |
| OSR-013a | Based on policies, the M2M System shall determine the delay tolerance for initiating individual information exchanges and shall schedule the communication accordingly or request the underlying network to do it. | 1.0 |
| OSR-013b | The M2M System shall enable M2M Applications and/or M2M Service Capabilies to provide preferences for acceptable delay tolerance as a default and/or for initiating individual information exchanges. NOTE: Such preferences can be overruled by policies as in requirement OSR-013a | 1.0 |
| OSR-014 | Using reference points specified by oneM2M, the M2M Gateway shall support communication with M2M Applications and/or Service Capabilities on M2M Devices that are connected to the M2M Gateway via its M2M Area Network. The M2M Gateway shall not require M2M Applications and/or M2M Service Capabilities involved in that communication to be aware of the specific communication protocols used between that M2M Gateway and the connected M2M Devices. | 1.0 |
| OSR-015 | The M2M System shall support different communication patterns including infrequent communications, small data transfer, large file transfer, streamed communication. Editor’s Note: This requirement cannot be verified without refinement | 1.0 |
| OSR-016a | The M2M System shall provide the capability to notify M2M Applications and/or M2M Service Capabilities about the availability of, and changes to, data made accessible by M2M Applications and/or M2M Service Capabilities. NOTE: Such data could include management data | 1.0 |
| OSR-016b This requirement fits better to management section | The M2M System shall provide the capability to notify M2M Applications and/or M2M Service Capabilities about changes in the topology of the M2M Area Network. | 1.0 |

Table 1 Overall System Requirements

## 6.2	Management Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| MGR-001 | M2M System shall support management and configuration of resource constrained devices. | 1.0 |
| MGR-002 | The M2M System shall provide the capability to discover information about its M2M Area Networks including information about euipment on those networks and the parameters (e.g. topology, protocol) of those networks using a common, oneM2M defined, Information Model for M2M Area Networks. | 1.0 |
| MGR-003 | The M2M System shall provide the capability to maintain and make available management information of equipment and parameters (e.g. topology, protocol) of M2M Area Networks using the Information Model for M2M Area Networks. | 1.0 |
| MGR-004 | The M2M System shall support common means to manage equipment enabled by different management technologies (e.g. OMA DM, BBF TR069) using a common, oneM2M defined, Information Model. | 1.0 |
| MGR-005 | The M2M System shall provide the capability to manage equipment in a grouped manner using a common, oneM2M defined, Information Model. | 1.0 |
| MGR-006 | The M2M System shall provide the capability for provisioning and configuration of equipmenton M2M Area Networks using a common, oneM2M defined, Information Model. | 1.0 |
| MGR-007 | The M2M System shall provide the capability for monitoring of equipment and performing diagnostics of equipment in M2M Area Networks using a common, oneM2M defined, Information Model. | 1.0 |
| MGR-008 | The M2M System shall provide the capability for software management of equipment in M2M Area Networks using a common, oneM2M defined, Information Model. | 1.0 |
| MGR-009 | The M2M System shall provide the capability for resetting equipment in M2M Area Networks using a common, oneM2M defined, Information Model. | 1.0 |
| MGR-010 | The M2M System shall provide the capability for authorizing equipment to access M2M Area Networks | 1.0 |

Table 2 Management Requirements

## 6.3	Data Model & Semantics Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| DSR-001 | For the purpose of exchanging data among M2M Applications and/or M2M Service Capabilities the M2M System shall provide a generic Information Model for data representation that is independent of any specific M2M Application and/or M2M Service Capabilitiy. | 1.0 |
| DSR-002 | The M2M System shall be able to support translation mechanisms between data, used by M2M Applications and Edge Equipment, structured according to Information Models not specified in oneM2M and data structured according to Information Models specified in oneM2M | 1.0 |

Table 3 Data Model & Semantics Requirements

## 6.4	Security Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| SER-001 | The M2M System shall incorporate protection against threats to its availability such as ‘denial of service’ attacks. | 1.0 |
| SER-002 | The M2M System shall be able to ensure the Confidentiality of data. Editor’s note: Definition missing for Confidentiality | 1.0 |
| SER-003 | The M2M System shall be able to ensure the Integrity of data. Editor’s note: Definition missing for Integrity | 1.0 |
| SER-004 | In cases where the equipment in the Field Domainsupport USIM / UICC and the underlying networks support network layer security, the M2M System shall be able to leverage device’s USIM / UICC credentials and network’s security capability e.g. 3GPP GBA for establishing the M2M Services and M2M Applications level security through interfaces to underlying network. Editor’s note: Suggest to extend the requirement to Underlying Networks that support secure environments other than UICC / USIM | 1.0 |
| SER-005 | In cases where the equipment in the Field Domain support USIM/UICC and the Underlying Networks support network layer security, and when the M2M System is aware of Underlying Network’s bootstrapping capability e.g. 3GPP GBA, the M2M System shall be able to expose this capability to M2M Applications and/or M2M Service Capabilities through a set of oneM2M specified reference points. Editor’s note: Suggest to extend the requirement to Underlying Networks that support secure environments other than UICC / USIM | 1.0 |
| SER-006 | In cases where the equipment in the Field Domain support USIM / UICC and the Underlying Networks support network layer security, the M2M System shall be able to leverage those credentials when available to bootstrap m2m security association. Editor’s note: Suggest to extend the requirement to Underlying Networks that support secure environments other than UICC / USIM This requirement implicitly assumes that oneM2M specifies a bootstrapping procedure for establishing security associations but a requirement for bootstrapping is missing. | 1.0 |

Table 4 Security Requirements

## 6.5	Charging Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| CHG-001 | The M2M System shall support collection of charging specific information related to the individual services facilitated by the system (e.g. data management, device management and/or connectivity management), and concurrently with the resource usage. The format of the recorded information shall be fully specified including mandatory and optional elements. Editor note: this requirement requires further work on the wording. | 1.0 |
| CHG-002 | The M2M System shall support mechanism to facilitate correlation (e.g. subscriber identity) of charging information collected for different services, including those provided by the underlying network operator. Editor note: this requirement requires further work on the wording. | 1.0 |

Table 5 Charging Requirements

End Change