| Input contribution Use case |
| --- |
| Use Case Title:* | Use Case on collection of non-application data |
| Group Name:* | <WG1> |
| Source:* | ChinaUnicom, Huawei technologies |
| Contact: | Changwei Hu, China Unicom, hucw5@chinaunicom.cn Peng Wang, China Unicom, wangpeng@chinaunicom.cn Xueqin Jia, China Unicom, jiaxq11@chinaunicom.cn Yi Chen; Huawei technologies ; yi.chen@huawei.com |
| Date:* | <2013-04-01> |
| Abstract:* | This proposal is to provide a use case of non-application data collection. |
| Agenda Item:* | N/A |
| Work item(s): | N/A |
| Document(s) Impacted* | N/A |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Use Case on collection of non-application data.

## Description

### M2M Operators face two problems：

### the first is that we do not have enough M2M-Apps’s data, because the industrial customers do not want to share their data with operator

### the ARPU of M2M communication  is very low, so operators must get an additional income from the m2m network services.

### It is very difficult to collect application data, so we want to collect non-application data instead. Then we can process these data by BigData method,  and so we can provide more valuable services.

### We describe the process of non-application data collection by m2m gateway, m2m module, m2m platform and m2m network equipment.

## Source (as applicable)

### China Unicom

## FFSActors (as applicable)

## front-end data-collection equipment ：

## management platform

## monitor center

## vehicle state data demand department

## non-application data collection center

## Pre-conditions (if any)

### <Conditions that must exist for the use case or scenario to be executed>

## Triggers (if any)

## time trigger: collecting data at a specific time;

## position trigger: collecting data when position changed;

## behavior trigger: collecting data when certain behavior happened;

## others

## Normal Flow (as applicable)

## front-end devices need to be registered in the vehicle platform.

## after registration, those devices can send data to the vehicle platform by some protocol.

## the vehicle platform  collect data of the those devices. and then the vehicle platform  can get the position of those devices, send alarm to those devices and broadcast some information to those devices, etc.

## If the application vendors are reluctant to share data, the platform needs use a built-in data collector to collect non-application data and send to the  non-application data collection center.

### Alternative flow (if any)

## Post-conditions (if any)

### <Conditions resulting from the execution of the use case or scenario>

## High Level Illustration (as applicable)

### Figure1：Vehicle Operation Management System

### Vehicle Operation Management System provide users a new telecommunications business with remote collection, transmission, storage, processing of the image and alarm signals.

### front-end data-collection equipment include front-end 3G camera, electronic station, Car DVR, costumed car GPS , wcdma wireless routers and other equipment.

### management platform with business management function, include:

### forwarding, distribution, or storage of images

### linkage process of alarms

### management and maintenance of the vehicle status data.

### monitor center：consists of   TV wall, soft / hardware decoder,  monitor software, etc.

### vehicle state data demand department: such as  auto 4S shop, vehicle repair shop, vehicle management center, automobile and parts manufacturers, government regulatory platform, etc.

### non-application data collection center: use  built-in data collectors resided in network equipment, m2m platform costumed m2m modules and costumed m2m terminal devices to collect non-application data.

## Potential requirements (as applicable)

### Figure2: Non-application data collection processing flow

### As illustrated in Figure 1, Data collector of m2m system should include these roles: PDataCollector、NDataCollector、GDataCollector、MDataCollector and M2M BigDataCenter.

## PDataCollector: non-application data collector residing in the m2m platform, which may collect non- application data from m2m-apps and m2m platform;

## NDataCollector: non- application data collector residing in the m2m network equipment, which may collect non- application data from network equipment;

## GDataCollector: non- application data collector residing in the m2m gateway devices, which may collect non- application data from gateway devices;

## MdataCollector: non- application data collector residing in the m2m communication module, which may collect non- application data from m2m communication module;

## M2M BigDataCenter: the data center that process m2m non- application data using BigData method;

### Data collector may collect m2m base data beyond application data, such as position data、time data、 speed data、 direction data、behaviour  data and other base data.

## NdataCollector may collect non- application data without GdataCollector and MdataCollecor;

## NdataCollector may collect much more  non- application data with GdataCollector and MdataCollecor;

# Comments

### Because the m2m vertical applications providers  are unwilling to share their business data(or application data) with telecom operators, and they want telecom operators to be only communication channels.

### so we want to collect data that do not need the m2m vertical applications providers  to share, such as  location info、behaviour info、time info、 speed info、 direction info and other anonymous information.

### we call these  “non-application”data collection.

these stand from  the premise that we do not  make security threats and invasion of privacy

operator can do:

- m2m data analysis by operator without knowledge of application data(by means of collection of data such as device behaviour etc ).

Make m2m service layer more intelligence: we can Infer the "correct"  state of the application or the network status changes, by the analysis of the non-application data, and then  trigger some kinds of optimization mechanisms.