| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Security Requirements – Security Mechanisms |
| Source:* | François Ennesser, Gemalto (ETSI), francois.ennesser@gemalto.com Madjid Nakhjiri, Motorola Mobility, vxt746@motorola.com Hui Xu, CATT (CCSA), xuhui@catt.cn |
| Contact: | François Ennesser, Gemalto (ETSI), francois.ennesser@gemalto.com |
| Date:* | 2013-04-08 |
| Abstract:* | Service access security requirements proposed but not examined during TP3 |
| Agenda Item:* | REQ/SEC joint session |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirements TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree on proposed requirements |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

| Requirement ID | Source | Requirement Text | Rationale or Related use cases (where applicable) |
| --- | --- | --- | --- |
| HLR 211 Rev | Gemalto (REQ-0195) | M2M System shall provide interoperable mechanisms to setup and operate connections between entities where security services (authentication, integrity or confidentiality) are involved. |  |
| R-xxxx | Oberthur, ZTE (REQ-0288r1) | The M2M System should support means to assure the confidentiality of the data transferred across underlying networks. |
| R-xxxx | Oberthur, ZTE (REQ-0288r1) | The M2M System shall support means to assure the integrity of the data transferred across underlying networks. |
| RS-14 | CATT (REQ-0194) Light weight security mechanism | The M2M System shall support standard light weight security mechanism (authentication, encryption, integrity protection and so on) in M2M Devices. | An environmental monitoring system comprises many environmental monitor sensor units that can monitor temperature, humidity, wind speed, rain meter etc. These sensor units are distributed in wide area and self-powered, many of them are located in the area where the sensor units cannot connected to the public networks, e.g. the internet or wireless network. These units have to build a multi-hop network through which the collected data are accumulated to the points where can connect to the public networks. Normally these kinds of sensor units are low-cost, their power supply is limited, and their computing capability is weaker, so the whole monitoring system, including the security subsystem, must be power efficient. |
| HLR 212 rev | Gemalto (REQ-0195) | The M2M System shall be able to provide M2M entities with secure updates of software / firmware (including application level). |  |
| RS-12 | Motorola (REQ-0194) | Any software client, especially those performing security functions (e.g. authentication clients) shall be integrity protected (signed) and verified after device power up/reset or before launch. Widely deployed proven standards such PKCS#7 or CMS should be used for code signing. | e-health application security |
| RS-13 rev | CATT (REQ-0194) Audit | The M2M System shall support security audit in the M2M Device/Gateway and infrastructure. |  |