| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Requirements from use case oneM2M-REQ-2013-0260R02 on Leveraging Broadcasting/Multicasting Capability of Underlying Networks |
| Source:* | NEC |
| Contact: | Takanori Iwai, NEC, <t-iwai@hx.jp.nec.com> Joerg Swetina, NEC, <joerg.swetina@neclab.eu> Ataru Kobayashi, NEC, <a-kobayashi@df.jp.nec.com> |
| Date:* | 2013-06-06 |
| Abstract:* | This contribution collects the requirements from use case oneM2M-REQ-2013-0260R02 which were agreed at REQ#26 (TP#4) for inclusion into the Requirements specification TS-0002 |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirements Specification: oneM2M-TS-0002-Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to include the requirements into oneM2M Requirements Specification. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

Use case REQ-2013-0260R02, which was agreed at REQ#26 (TP#4), illustrates interworking of oneM2M with mobile networks (e.g. 3GPP, 3GPP2 ..) to leverage broadcast/multicast capabilities of the underlying mobile network.

While it is not clear yet, if interfaces to underlying mobile networks – e.g. 3GPP– that are dedicated for M2M usage will be available for that purpose (see LS oneM2M-TP-2013-0251R01 to 3GPP SA2), an M2M Solution may still make use of existing services (e.g. Cell Broadcast Service or MBMS Service) of underlying mobile networks through network specific interfaces or open access models (e.g. OMA, GSMA OneAPI framework). [See also requirements OSR-005 and OSR-006]

Proposed Requirement:

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| tbd | Overall System Requirements | The M2M System SHALL enable a M2M Application Service to request to send data to M2M Applications of a group of M2M Devices and M2M Gateways in geographic areas that are specified by the M2M Application. The M2M System shall support that request to be independent of the types of the Underlying Networks. |
| tbd | Overall System Requirements | Depending on availability of suitable interfaces provided by the Underlying Network the M2M System shall be able to request the Underlying Network to broadcast / multicast data. This request may include related broadcast/multicast parameters that are relevant to the Underlying Network, e.g. the area to be covered, the targeted group of M2M Devices/Gateways the option whether the broadcast should be repeated, including repetition interval, stopping conditions etc. |
| tbd | Overall System Requirements | If the targeted group of M2M Devices/Gateways supports connectivity by multiple Underlying Networks then, for each broadcast/multicast request, the M2M System shall be able to select an appropriate Underlying Network depending on the network’s broadcast/multicast support. |
| tbd | Charging Requirements | The M2M System shall be able to support Accounting of an M2M Application for support of broadcasting/multicasting of data. |