| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | WG1 REQ |
| Title:* | Input Requirements for Lightweight Communication Protocols between Intranet M2M Device and back-end system |
| Source:* | <China Telecom>, <CCSA> |
| Contact: | Tang Jianjun, <China Telecom><tangjj@ctbri.com.cn> Zhou Kaiyu, <China Telecom>, zhouky@ctbri.com.cn Mao Tong, <China Telecom>, Maotong@ctbri.com.cn |
| Date:* | <2013-5-31> |
| Abstract:* | This contribution provides some requirements for Lightweight Communication Protocols between Intranet M2M Device and back-end system |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval and incorporation into oneM2M Requirement TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement..

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-001 | <Protocol)> | The M2M System shall be able to control M2M device in the intranet. Note: Due to the exhaustion of IPv4 address and limited IPv6 deployment, a large number of M2M end devices will be deployed inside the Intranet. The M2M device is generally resource-constrained equipment, so if the standard Network Address Translation (NAT) traversal technology is used to access the device in the intranet, the high requirement for the device processing ability will cause an increase in cost. To solve this problem, the M2M system shall provide a general lightweight remote control protocol adapt to the application case that M2M device is in the intranet, instead of the complex NAT traversal technology, to efficiently control these M2M devices. |