| CHANGE REQUEST |
| --- |
| Group Name:* | WG1 |
| Source:* | FUJITSU (TTC), NTT DOCOMO |
| Format:* | Physical meeting |
| Date:* | 2013-06-10 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com Takashi Koshimizu, NTT DOCOMO, koshimizu@nttdocomo.co.jp |
| Reason for Change/s:* | Requirements related with ‘Underlying Network’ should be described as depending on the availability of interfaces for interwork with ‘Underlying Network’. |
| Clause/Sub Clause Affected* | 6.1 and 6.2. |
| Agenda Item:* | oneM2M requirement TS |
| Work item(s): | WI 0001 |
| Document(s) Impacted* | oneM2M-TS-0002-Requirements-V0_2_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree on proposed changes. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Change 1

## 6.1 Overall System Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-001 | The M2M System shall be able to allow communication between M2M Applications in the Network Domain, and the M2M Applications in the Device Domain, by using multiple communication means based on IP Access. |  |
| OSR-002 | The M2M system shall support communication means that can accommodate devices with constrained computing (e.g. small CPU, memory, battery) or communication capabilities (e.g. 2G wireless modem, certain WLAN node) as well as rich computing (e.g. large CPU, memory) or communication (e.g. 3/4G wireless modem, wireline) capabilities. |  |
| OSR-003 | The M2M system shall support the ability to maintain M2M session in coordination with application session for those M2M applications that require it. Editor’s Note: M2M session need to defined. |  |
| OSR-004 | M2M system shall support the ability to support session-less application communications for those M2M applications that require it. |  |
| OSR-005 | The M2M system shall be able to expose the services offered by telecommunications networks to Applications (e.g. SMS, USSD, localization, subscription configuration, authentication (e.g. Generic Bootstrapping Architecture), etc), subject of restriction based on network operator’s policy. |  |
| OSR-006 | The M2M System shall be able to reuse the services offered by underlying networks to M2M Applications and/or M2M Service Layer, by means of open access models (e.g. OMA, GSMA OneAPI framework). An example of available services is: IP Multimedia communications Messaging Location Charging and billing services Device information and profiles Configuration and management of devices Triggering, monitoring of devices Small data transmission Group management The set of features or APIs to be supported depends on the M2M Service Capabilities and access to available APIs. |  |
| OSR-007 | The M2M system shall provide a mechanism for applications to interact with the applications and data belonging to another M2M system, subject to permission. |  |
| OSR-008 | The M2M System shall provide the capability for M2M Applications to communicate with a device (i.e. application in the device) without the need for the M2M Applications to be aware of the network technology and the specific communication protocol of the device. |  |
| OSR-009 | The M2M System shall support the ability for single or multiple M2M Applications to interact with a single or multiple M2M Devices/Gateways (application in the device/gateway). Editor’s Note: The relation M2M Network Application to M2M Device/Gateway can be 1:1, 1:n, n:1 and/or n:m |  |
| OSR-010 | The M2M system shall support mechanisms for message delivery notification to those M2M Applications requesting reliable delivery or timely delivery notification. |  |
| OSR-011 | The M2M System shall be able to request Underlying Network to use different communication paths, from the Underlying Network based on Underlying Network Operator and/or M2M Service Provider policies, routing mechanisms for transmission failures or request from M2M Applications. |  |
| OSR-012 | The M2M System shall support communications between M2M Applications and Devices supporting M2M services by means of continuous or non-continuous connectivity. |  |
| OSR-013 | The M2M System shall be aware of the delay tolerance acceptable by the M2M Application and shall schedule the communication accordingly or request the underlying network to do it, based on policies criteria. |  |
| OSR-014 | The M2M System shall be able to communicate with M2M Devices, behind an M2M Gateway that supports heterogeneous M2M area networks. |  |
| OSR-015 | The M2M system shall support different communication patterns including infrequent communications, small data transfer, large file transfer, streamed communication. |  |
| OSR-016 | The M2M System shall provide the capability to notify M2M Applications of the availability of, and changes to, available M2M Application/management data on the M2M Device/Gateway, including changes to the M2M Area Network, subject to restriction from availability of related features on th M2M Area Network. |  |
| OSR-017 | The M2M System shall be capable of offering access to different sets of M2M services to M2M Application providers. The minimum set of services are: Connectivity management Device management (service level management) Application Data management The M2M System shall facilitate different deployment scenarios by offering access to different sets of services independently, to a group of those or to all of them. |  |
| OSR-018 | The M2M System shall be capable of offering M2M Services to M2M Devices roaming across Underlying cellular Networks, subject of restriction based on operator’s policy. |  |
| OSR-019 | The M2M System shall support the capabilities to collect/store and report data from one or more M2M Devices or M2M Gateways, in ways requested by the M2M Application Infrastructure as listed below: action initiated either by an M2M Device, M2M Gateway, M2M Services Infrastructure, or M2M Application Infrastructure when triggered by schedule or event; for specified data for delivery to one or more M2M Gateways, M2M Services Infrastructure, or M2M Application Infrastructure Editor’s Note: Agreed in principle with the understanding that currently undefined terms will be addressed. |  |
| OSR-020 | The M2M System shall be able to support policies and their management regarding the aspects of storage and retrieval of data. |  |
| OSR-021 | The M2M system shall provide mechanisms for storing and enable sharing of information among multiple M2M Applications, i.e. information provided from M2M Applications (information provider) to be made available to one or more M2M Applications (information consumer), subject to access control. When sharing information among applications, the M2M system shall provide the capability for an M2M Application to selectively share information (e.g. access control). |  |
| OSR-022 | When some of the components of M2M System are not available (e.g. WAN connection lost), the M2M System shall be able to support the normal operation of components of the M2M System that are available. |  |
| OSR-023 | The M2M System shall be capable of identifying the M2M Services to be used by M2M service subscriptions. Editor’s Note: The subscriptions are M2M Service subscriptions (e.g., Device Management, Service Transport) not Application subscriptions (e.g., Home Energy Management). |  |
| OSR-024 | The M2M System shall be capable of identifying the devices used by M2M service subscriptions. |  |
| OSR-025 | The M2M System shall be capable of identifying the M2M Applications used by M2M service subscriptions. |  |
| OSR-026 | If provided by the Underlying Network, the M2M System shall be capable of associating the device used by a M2M System with the device identifiers offered by the Underlying Network and the device. |  |
| OSR-027 | The M2M System shall provide a generic mechanism to support transparent exchange of information between the M2M Application and the Underlying network, subject of restriction based on M2M Service Provider’s policy and/or Underlying Network operator ‘s policy. Editor’s Note: Transparent exchange of information implies information that is mainly interpreted by the M2M application and the underlying network provider. |  |
| OSR-028 | The M2M system shall be able to trigger a series of commands to actuators on behalf of applications. |  |
| OSR-029 | The M2M system shall support sending common command(s) to each actuator or sensor via a group. |  |
| OSR-030 | The M2M system shall support the management (i.e. addition, removal, retrieval and update) of the membership of a group. |  |
| OSR-031 | The M2M system shall support a group as a member of another group. |  |
| OSR-032 | The M2M System shall support event categorization (e.g., normal, urgency) associated with data for M2M applications when collecting, storing and reporting that data. Note: Based on the event categories and via interworking with underlying networks, the M2M System can support differentiated services (by providing Quality-of-Service) requested by M2M applications. Editor’s Note: ‘event categorization’ needs to be defined. |  |
| OSR-033 | Based on the local context (e.g., low battery) of the M2M Gateway and/or Device and the defined event categorization, the M2M System shall provide the capability to dynamically adjust the scheduling of reporting and notification of the M2M Device/Gateway. Note: for example, if the battery of Gateway is remained only 10% or below, the Gateway notifies the M2M service platform of the status. The M2M Application in the Infrastructure node will adjust the scheduling of reporting and notification based on the event categorization associated with each message. Consequently, the M2M Gateway operates longer. Editor’s Note: ‘local context’ needs to be defined. |  |
| OSR-034 | The M2M System shall support seamless replacement of M2M Devices as well as M2M Gateways (e.g., redirecting traffic, connection, recovery, etc.). |  |
| OSR-035 | The M2M System shall support the exchange of non-Application related relevant information (e.g. Device/Gateway classes) between M2M Device/Gateway and M2M infrastructure for the purpose of efficient communication facilitation. capability for M2M device to report device class to M2M service infrastructure and for M2M service infrastructure to inform device of the M2M platform capabilities |  |

Table 1 Overall System Requirements

Chage-2

## 6.2 Management Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| MGR-001 | M2M System shall support management and configuration of resource constrained devices. |  |
| MGR-002 | The M2M System shall provide the capability to discover the M2M Local Area Networks including information about devices on those networks and the parameters (e.g. topology, protocol) of those networks, subject of restriction based on availability of related capabilities in M2M Local Area Network.. |  |
| MGR-003 | The M2M System shall provide the capability to maintain and describe the management information model of devices and parameters (e.g. topology, protocol) of M2M Local Area Networks, subject of restriction based on availability of management interfaces . |  |
| MGR-004 | The M2M System shall support common means to manage devices enabled by different management technologies (e.g. OMA DM, BBF TR069). |  |
| MGR-005 | The M2M System shall provide the capability to manage multiple devices in a grouped manner. |  |
| MGR-006 | The M2M System shall provide the capability for provisioning and configuration of devices in M2M Local Area Networks . |  |
| MGR-007 | The M2M System shall provide the capability for monitoring and diagnostics of devices in M2M Local Area Networks . |  |
| MGR-008 | The M2M System shall provide the capability for software management of devices in M2M Local Area Networks. |  |
| MGR-009 | The M2M System shall provide the capability for resetting devices in M2M Local Area Networks. |  |
| MGR-010 | The M2M System shall provide the capability for authorizing devices to access M2M Local Area Networks |  |
| MGR-011 | The M2M System shall provide the capability for modifying the topology of devices in M2M Local Area Networks, subject of restriction based on management policy of M2M Local Area Network . |  |
| MGR-012 | Upon detection of a new device the M2M Gateway SHALL be able to be provisioned by the M2M Service Infrastructure with an appropriate configuration which is required to handle the detected device. |  |

Table 2 Management Requirements

Editor’s Note: it is FFS to determine if further subdivision is required.