| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ WG |
| Title:* | Requirements from Use cases of Electronic Toll Collection(ETC) service and use case Car/Bicycle Sharing Services in TR-001 v0.0.5(Use case) |
| Source:* | ZTE |
| Contact: | Yingjie Hong, hong.yingjie@zte.com.cn; Rajesh Bhalla, rabhalla@ztetx.com; |
| Date:* | 2014-04-03 |
| Abstract:* | Potential requirements from ETC use case and section 8.3 use case in TR-0001-UseCase-V0_0_5. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* | Release 1 Requirements TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate requirement(s) if agreed/approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

| ID | Classification | Use Case | Requirement Text |
| --- | --- | --- | --- |
| R-001 | OSR | REQ-2014-XXXX and section 8.3 in TR-0001(UseCase-V0_0_5) | M2M system shall provide the capability for support M2M entity multi-registrations. |
| R-002 | OSR | REQ-2014-XXXX and section 8.3 in TR-0001(UseCase-V0_0_5) | M2M system shall provide a lightweight registration function and a lightweight registration resource type for communication capability |

Requirement from Car/Bicycle Sharing Services in document TR-oo1 v0.0.5(use case) .

In this use case, Sensors shall register to the M2M service platform, so Service Provider could subscribe to the Sensors resource built in car. At the same time Sensors need to register to Smartphone for connecting to M2M service platform via Smartphone.

Since Sensors register to Smartphone only for communication, a lightweight registration and a lightweight registration resource type are suggested.

Note: Lightweight registration has the similar procedure as  “Registration”  which was defined in  the  TS-001(Functional Architecture), but lightweight registration  would create a simpler registration resource.

A  half-baked normal flow of the car/bicycle sharing services is as below.

- Sensors built in the car register to the M2M Service Platform and created themselves resources.

- Service Provider subscribe to the resource in the Service Platform.

- Smartphone register for taking sharing  car service.

- Sensors lightweight register to the smartphone. And user take the ownership of the car.

- Open the car door and turn on the ignition.

- The sensors report the changed status to the M2M Service Platform via Smartphone  when specific condition is triggered.

- Smartphone forward the request.

- The M2M Service Platform notifies the Service Provider of the changed status.