| Input contribution Use case |
| --- |
| Use Case Title:* | Intelligent shoes |
| Group Name:* | WG1 |
| Source:* | ChinaUnicom |
| Contact: | Changwei Hu (hucw5@chinaunicom.cn) Peng Wang (wangpeng@chinaunicom.cn) Junling Mao (maojl11@chinaunicom.cn) |
| Date:* | 2014-3-27 |
| Abstract:* | A user case named “Intelligent shoes” is described in this document, which involves a new requirement that the M2M systems shall support the capability of reusing the SIM card activation and deactivation capability in underlay network.. |
| Agenda Item:* | TBD |
| Work item(s): | TBD |
| Document(s) Impacted* | TBD |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential network API over mcn |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

### Intelligent shoes

## Description

### The intelligent shoes can monitor the motion parameter of users and report the information to intelligent shoes application server. The users can log in the application server and check their motion parameter.

### A SIM card will be embedded in the intelligent shoes to support  the mobile communication. The intelligent shoes manufacturer usually only subscribe the mobile network service for one-year or shorter, and the users can extend the subscription by themselves.  To prolong the actual usage time of subscribed mobile network service, the intelligent shoes manufacturer wants that the SIM card is only activated when the shoes are sold out and in use. Therefore, the intelligent shoes module should be able to trigger the activation of the SIM card when the shoes are in use. On the other hand, the users also have the requirement to trigger the deactivation of the SIM card if they do not need the motion monitoring function of their intelligent shoes.

## Source (as applicable)

## Chinaunicom

## Actors (as applicable)

### Mobile network operator

### Intelligent shoes application server

### M2M platform

### Intelligent shoes module

### User terminal

## Pre-conditions (if any)

### The mobile network operator opens the service interface for remotely changing the state (e.g. card information, association relationship with mobile number) of target SIM cards. This interface can support the activation and deactivation of SIM cards.

## Triggers (if any)

### The following triggers could initiate exchange of information.

### The intelligent shoes module initiates the activation request (Trigger A). In this case, the module in the intelligent shoes detects that the intelligent shoes are in use, and intends to active the SIM card and report location information to intelligent shoes application server.

### The user terminal initiates the deactivation request (Trigger B). In this case, the user intends to terminate the monitoring function of intelligent shoes.

## Normal Flow (as applicable)

### SIM card activation  (Trigger A)

### The intelligent shoes module initiates the activation request to M2M platform.

### The M2M platform use the SIM card activation capability provided by the mobile network operator to active the SIM card in corresponding intelligent shoes module and feedback the activation information to intelligent shoes module.

### The intelligent shoes module collects the motion information and reports the motion information to intelligent shoes application server in certain rules (e.g. periodically report).

### SIM card deactivation (Trigger B)

### The user terminal initiates the deactivation request to intelligent shoes application server.

### Intelligent shoes application server forward the deactivation request to M2M platform.

### The M2M platform use the SIM card deactivation capability provided by the mobile network operator to terminate the usage of the SIM card in target intelligent shoes module and feedback the deactivation information to intelligent shoes application server.

### Intelligent shoes application server forward the deactivation information to user terminal.

## Post-conditions (if any)

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

### The M2M systems shall support the capability of  reusing the SIM card activation and deactivation capability in underlay network.

### The M2M system shall support device addressing mechanism.

### The M2M system shall support the notification and subscription mechanism for information report.