| Input contribution Use case |
| --- |
| Use Case Title:* | Use case for Conflict Management in Home Automation System |
| Group Name:* | WG1 |
| Source:* | KETI |
| Contact: | Sungchan Choi (csc@keti.re.kr) Yong-Suk Park (yspark@keti.re.kr) Jaeho Kim (jhkim@keti.re.kr) |
| Date:* | 2014-09-15 |
| Abstract:* | Propose to include the use case for Home Domain Enablement TR. |
| Agenda Item:* |  |
| Work item(s): | WI 0017 – Home Domain Enablement |
| Document(s) Impacted* | Technical Specification TR 0013 – Home Domain Enablement TR |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval of the Use case for the Home Domain Enablement TR |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## 5.x	Use case for Conflict management in Home Automation System

## 5.x.1 Description

### Smart Home Service is usually based on home automation system along with home monitoring system. For example, in this kind of system, when a person comes into a house from outside, lights in a front room turns on and on the other hand, when a person goes out of the room, the lights in the room turns off.

### In home domain environments, there are a variety of home appliances which are connected to a home gateway or a home server and those home appliances could be managed and controlled through home automation system/application.

### For example, we can consider this kind of situation as follows. A smart home application could control a window blind in a home according to the time of day. Based on this rule, if it is sunset time, the window blind can be unfolded and if it is sunrise time, the window blind can be folded. On the other hand, another smart home application may control the window blind based on the amount of the sun light.

### In this situation, if the one application is willing to pull down the window blind according to the time of the day and the other application is willing to draw up the window blind according to the amount of sunlight. This causes the following problem: which rule has the priority over the other rule? This kind of situation which is called conflict problem and it could happen frequently in smart home system.

### OneM2M gateway/server would manage a number of registered home appliances and it control these home appliances such as window blind, home door, thermostat, sprinkler etc. In this situation, each home appliance could be managed and controlled in a harmonized way for providing user with comfortable home environments.

### For example, we can think of this kind of a home automation system which includes sprinkler, temperature sensor, moisture sensor, water main valve controller, etc. In these configurations, we suppose that a fire breaks out in the house and the temperature sensor detects the fire. As soon as this situation occurs, the home automation system may activate the sprinkler to extinguish the fire. However, if the sprinkler sprays water for some times, this might cause the moisture sensor to detect getting wet in the floor.

### Through the information form the moisture sensor, the home automation system regards this situation as flood conditions and tries to control the water main to be closed. So this causes the sprinkler not to work and the house may be damaged by the fire. This kind of situation is not a desired situation in home automation system. Therefore, in oneM2M system, when the home automation system is adapted, it should have means to control home devices harmoniously.

## 5.x.2 Source

### KETI

## 5.x.3 Actors

## Home appliances which include temperature sensor, moisture sensor, sprinkler, water main pump, refrigerator, washing machine, etc.

## Home gateway which is connected through home appliances and manage resources about registered home appliances.

## Smart home server is an oneM2M platform provided by a service provider in the infrastructure domain

## Smart home automation service which manages and controls the registered devices and resources based on the service policy and rule.

## 5.x.4. Pre-condition

### Every home appliances is registered with home gateway or smart home server. Each home appliances is controlled via home gateway or smart home server through smart home applications.

## 5.x.5 Triggers

### None

## 5.x.6 Normal Flow

## A fire breaks out in one of rooms at home. In this situation, a temperature sensor detects the fire from one of rooms.

## The home automation system/application controls a sprinkler and the sprinkler is activated and sprays water over the fire.

## At this time, the floor of the room is getting wet because of the water from sprinkler and then, a moisture sensor detects the water in the floor and the home automation system/application misunderstands this situation and controls a water main valve to be closed.

## However, because the fire is not extinguished, the temperature sensor reports the fire detection again.

## Using this kind of information, the home automation system detects a conflict problem regarding controlling resources in home. Therefore, based on the priority and policy rule, the home automation system activates the sprinkler again and ignore alarm from moisture sensor until the fire is all extinguished.

## 5.x.7 Post-conditions (if any)

### The fire is successfully extinguished and home appliances are managed and controlled in a harmonious way.

## 5.x.8 High Level Illustration (as applicable)

## 5.x.9 Potential requirements (as applicable)

### The M2M System shall provide capabilities of detecting and solving a conflict problem when controlling M2M devices/resources.