| CHANGE REQUEST |
| --- |
| Meeting:* | REQ#16 |
| Source:* | Joerg Swetina, NEC, joerg.swetina@neclab.eu |
| Date:* | 2015-03-23 |
| Contact:* | Joerg Swetina, NEC, joerg.swetina@neclab.eu |
| Reason for Change/s:* | The requirements on Abstraction and Semantics have been re-evaluated by WG5 and need to be updated for normative work in release 2. Note that in release 1 none of the original requirements had been implemented. |
| CR against: Release* | 2 |
| CR against: WI* | Active Wi-0005 “Abstraction & Semantics Capability Enablement” MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 v1.0.1 Note: Implementation of this CR should create v2.0.0 |
| Clauses/Sub Clauses* | 6.3 (Abstraction and Semantics Requirements) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As the result of the work described in TR-0007 “Study of Abstraction and Semantics Enablements”, the original requirements have been refined, new requirements have been added and the overall consistency has been checked.

The requirements have been categorized according to key semantic aspects identified in Section 7.1 of TR-0007,
 i.e. semantics annotation, ontology, semantics query, semantics mashup, data analytics and semantic reasoning

### -----------------------Start of change 1-------------------------------------------

## 6.3	Semantics Requirements

### 6.3.1	Ontology related Requirements

Table 3: Ontology Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| ONT-001 | The M2M System shall support a standardized format for the rules/policies used to define service logic. |  |
| ONT-002 | The M2M System shall support modelling semantic descriptions of Things (including relationships among them) by using ontologies. |  |
| ONT-003 | The M2M System shall support a common modeling language for ontologies (e.g. OWL). |  |
| ONT-004 | The M2M System should be able to provide translation capabilities from different modeling languages for ontologies to the language adopted by oneM2M if the expressiveness of the imported ontology allows. |  |
| ONT-005 | The M2M System shall provide the capability to retrieve semantic descriptions and ontologies stored outside of the M2M System. |  |
| ONT-006 | The M2M System shall provide support for linking ontologies defined in the context of the M2M System with ontologies defined outside this context. |  |
| ONT-007 | The M2M System shall be able to support extending ontologies in the M2M System. |  |
| ONT-008 | The M2M System shall be able to use ontologies that contain concepts representing aspects (e.g. a room) that are not represented by resources of the M2M System. |  |
| ONT-009 | The M2M System shall be able to re-use common ontologies (e.g., location, time ontologies, etc.) which are commonly used in M2M Applications. |  |
| ONT-010 | The M2M System shall be able to support simultaneous usage of multiple ontologies for the same M2M resource. |  |
| ONT-011 | The M2M System shall provide the capability for making ontology available in the M2M System, e.g. through announcement. |  |
| ONT-012 | The M2M System shall be able to support mechanisms to import external ontologies into the M2M System. |  |
| ONT-013 | The M2M System shall be able to support update of ontologies. |  |
| ONT-014 | The M2M System shall enable functions for data conversion based on ontologies. |  |
| ONT-015 | The M2M System shall be able to model devices based on ontologies which may be available outside the M2M System (e.g. HGI device template). |  |
| ONT-016 | The M2M System shall support storage, management and discovery of ontologies. |  |

### 6.3.2	Semantics Annotation Requirements

Table 4: Semantics Annotation Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| ANN-001 | The M2M System shall provide capabilities to manage semantic information about the oneM2M resources, e.g, create, retrieve, update, delete, associate/link. |  |
| ANN-002 | The M2M System shall support a common language for semantic description, e.g. RDF. |  |
| ANN-003 | The M2M System shall support semantic annotation of oneM2M resources for example application related data contained in containers. |  |
| ANN-004 | The M2M System shall support semantic annotation based on related ontologies. |  |
| ANN-005 | The M2M System shall provide the capability for making semantic descriptions available in the M2M System, e.g. announcement. |  |
| ANN-006 | The M2M System shall enable applications to retrieve an ontology representation related to semantic information used in the M2M System. |  |

### 6.3.3	Semantics Query Requirements

Table 5: Semantics Query Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| QRY-001 | The M2M System shall provide capabilities to discover M2M Resources based on semantic descriptions. |  |

### 6.3.4	Semantics Mashup Requirements

Table 6: Semantics Mashup Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| MSH-001 | The M2M System shall provide the capability to host processing functions for mash-up. |  |
| MSH-002 | The M2M System shall enable Applications to provide processing functions for mash-up. |  |
| MSH-003 | The M2M System itself may provide pre-provisioned or dynamically created processing functions for mash-up. |  |
| MSH-004 | The M2M System shall be able to create and execute mash-ups based on processing functions. |  |
| MSH-005 | The M2M System shall be able to expose mash-ups as resources e.g. virtual devices. |  |

### 6.3.5	Semantics Reasoning Requirements

Table 7: Semantics Reasoning Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| RES-001 | The M2M System shall be able to update ontologies as a result of the ontology reasoning. |  |
| RES-002 | The M2M System shall be able to support semantic reasoning e.g. ontology reasoning or semantic rule-based reasoning. |  |
| RES-003 | The M2M System shall be able to support adding and updating semantic information based on semantic reasoning. |  |

### 6.3.6	Data Analytics Requirements

Table 8: Data Analytics Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| ANA-001 | The M2M System shall be able to support capabilities (e.g. processing function) for performing M2M data analytics based on semantic descriptions from M2M Applications and /or from the M2M System. |  |
| ANA-002 | The M2M System shall provide the capability of interpreting and applying service logic (e.g. rules/policies of triggering operations upon other resources or attributes according to the change of the monitored resource) described with semantic annotation and ontology. |  |
| ANA-003 | The M2M System shall support a standardized format for the rules/policies used to define service logic. |  |

### -----------------------End of change 1---------------------------------------------