| CHANGE REQUEST |
| --- |
| Meeting:* | REQ#17 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wei Zhou, Datang, zhouwei@catt.cn |
| Date:* | 2015-05-21 |
| Contact:* | As above |
| Reason for Change/s:* | End-to-End security requirements coming out of WI-0016 |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 v1.0.1 |
| Clauses/Sub Clauses* | 6.4 “Security” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution provides generic requirements on “end-to-end” security – although the requirements themselves no-longer refer to that term. This is motivated by work in WI-0016.

### -------------Start of change 1: insert at appropriate place in table 5----------------

## 6.4	Security Requirements

Table 5: Security Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| SEC-0xx | The oneM2M System shall allow security protocol end-points to protect portions of the messages or data so that intermediate entities (whether trusted or untrusted) can forward the messages or data (between the security protocol end-points) without accessing the protected portions of messages or data in clear text. |  |
| SEC-0xx | The oneM2M System shall allow security protocol end-points to protect portions of messages or data so that security protocol end-points can detect modification of the protected portions of messages or data by intermediate service layer entities (whether trusted or untrusted) forwarding the messages or data (between the security protocol end-points). |  |
| SEC-0xx | The oneM2M System shall allow security protocol end-points to authenticate each other without relying on intermediate service layer entities (whether trusted or untrusted) between the security protocol end-points. |  |

### -----------------------End of change 1---------------------------------------------