| Input contribution Use case |
| --- |
| Use Case Title:* | Quality of Sensor Data |
| Group Name:* | WG1 Requirements |
| Source:* | Hitachi |
| Contact: | Toshiko Matsumoto, toshiko.matsumoto.jz@hitachi-solutions.com |
| Date:* | 2015-July-13 |
| Abstract:* | This contribution proposes a use case ‘Quality of Sensor Data’ for TR-0001. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0015 |
| Document(s) Impacted* | oneM2M-TR-0001-Use Case Collection |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

Quality of Sensor Data

### Description

It is quite popular to transmit observation values of the sensor as a form of time series data in social infrastructure, i.e. factories, power plants, water systems, or railroad systems. In these handling of sensor values, observation value is transmitted with “quality bit”, which represents quality of data, i.e. the observation value is valid or not.

The quality bit is used as a quality indicator of observation value of sensor, in order words, basis for considering whether the value is usable or not, or how the value should be used.

Here we consider an example case where water is stored in a tank and is conveyed by a pump. The water level of a tank is observed by a sensor. The observation value is not adequate to be utilized when there is any abnormality in the electric power source of the sensor, controller, oneM2M MN, or in underlying network. Therefore information “the observation value of sensor of water level lacks quality” is added to make application be able to work as intended.

### Source

None

### Actors

- Tank: Tank stores water

- Pump: Pump conveys water

- Water level sensor: It observes water level of a tank and transmit the observation value to PLC/DCS at fixed time intervals

- Electric power source of water level sensor: It supplies electric power which is required for the water level sensor to work correctly

- PLC(Programmable Logic Controller)/DCS(Distributed Control System): PLC/DCS receives two observation values, i.e. water level of a tank and status signal of electric power source, and transmit a form of water level data with a quality bit at a fixed time intervals. When the electric power source is abnormal, the water level observation value is considered to be incorrect and the quality bit is set to “not good.”

- oneM2M MN:  oneM2M MN receives time series data and its corresponding quality bit from PLC/DCS and transmit them to oneM2M platform. When PLC/DCS or Real-time Ethernet has some abnormality, the received observation value is considered to be incorrect and quality bit is set to “not good.”

- oneM2M platform:  oneM2M platform receives time series data and its corresponding quality bit from oneM2M MN and transmit them to Application. When oneM2M MN or underlying network has some abnormality, the received observation value is considered to be incorrect and the quality bit is set to “not good.”

- oneM2M Application: oneM2M Application receives time series data and its corresponding quality bit, and performs user-defined procedure(s) referring quality bit value.

- Real-time Ethernet: Real-time Ethernet connects PLC/DCS and oneM2M MN.

- Underlying network: it connects oneM2M MN and oneM2M platform.

### Pre-conditions

Observation value of sensor is coupled with its quality bit and correspondence relation is defined.

### Triggers

PLC/DCS receives observation value at fixed time intervals and receives status signal of electric power supply of the water volume sensor.

### Normal Flow

1.	When the electric power source is normal, the observation value is considered to represent correct water level and to be usable. In this case, PLC/DCS adds quality bit of “good” to the observation value and transmit them.

2.	oneM2M MN receives time series data and its corresponding quality bit from PLC/DCS, and transmit them.

3.	oneM2M platform receives time series data and its corresponding quality bit from oneM2M MN, and transmits them.

4.	Application receives time series data and its corresponding quality bit from oneM2M platform and performs user-defined procedure(s).

### Alternative flow

1.	When the electric power source is abnormal, the observation value is considered to be incorrect water level, and to cause problematic result in application. In this case, PLC/DCS transmit the data with a quality bit “not good.”

2.	oneM2M MN receives time series data and its corresponding quality bit from PLC/DCS, and transmit them.

3.	oneM2M platform receives time series data and its corresponding quality bit from oneM2M MN, and transmits them.

4.	Application receives time series data and its corresponding quality bit to perform user-defined procedure(s). Usually, observation value with quality bit “not good” is not used to monitoring or controlling functions.

### Post-conditions

None.

### High Level Illustration

### Potential requirements

The oneM2M system shall provide capability to manage data quality description of resource.