| CHANGE REQUEST |
| --- |
| Meeting:* | REQ 21 |
| Source:* | Shelby Kiewel, iconectiv, skiewel@iconectiv.com |
| Date:* | 2016-01-17 |
| Contact:* | Shelby Kiewel, iconectiv, WG1 Chairman |
| Reason for Change/s:* | This contribution is to add an informative annex to TS-0002 Requirements. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <WI-00XX > MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 |
| Clauses/Sub Clauses* | New Annex at end of document |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

### Introduction

### This contribution is to add an informative annex to TS0002 per agreement detailed below from TP20

### Agreed Path Forward on TS-0002 between Stage 1 and Stage 3 Freeze (any release … currently X = 2)

### A)	Requirement confirmed as normative, but not met in Release X-1

### These requirements will remain in the main body of TS-0002, but be noted as “Targeted for Release X” (Regardless of if we think it will actually happen or not)

### B)	Requirements “Partially Met in Release X-1”

### These requirements will remain unchanged until after Stage 3 freeze of Release X

### After Stage 3 freeze, these requirements will be reviewed for inclusion in Release X

### If they are not fully met in Release X, they will remain in the main body of TS-0002, and will be updated to reflect “Partially Met”, not indicating a release.  Footnotes will continue to reflect how the requirement was partially met.

### If the requirement is fully met, it will be updated to say “Met in Release X”

### C) Requirement developed after Stage 1 freeze and before Stage 3 freeze of Release X

### Requirements intended for Release X+1 will be added to TS-0002 in an Informative Annex

### After Stage 3 freeze, contributions may be uploaded to move these requirements individually from the Informative Annex to the main body of TS-0002

### When moved to the main body, they will reflect “Targeted for Release X+1”

### If requirements are added to the Informative Annex and are later determined not to become part of the oneM2M System, they may be removed from the Informative Annex via contribution

### -----------------------Start of change 1-------------------------------------------

### _____________________________________________________________

### Annex A (informative):

The requirements contained in this Annex are gathered and targeted for the next release of oneM2M.

# 1	Functional Requirements

## 1.1	Overall System Requirements1.2	Management Requirements1.3	Semantics Requirements1.3.1	Ontology Related Requirements1.3.2	Semantics Annotation Requirements1.3.3	Semantics Query Requirements1.3.4	Semantics Mashup Requirements1.3.5	Semantics Reasoning Requirements

### 1.3.6	Data Analytics Requirements

## 1.4	Security Requirements

## 1.5	Charging Requirements

## 1.6	Operational Requirements

## 1.7	Communication Management Requirements

## 1.8	LWM2M Interworking Requirements

### -----------------------End of change 1--------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?