| CHANGE REQUEST |
| --- |
| Meeting ID:* | REQ27, joint session with ARC |
| Source:* | Miodrag Djurica, TNO, miodrag.djurica@tno.nl |
| Date:* | 2017-02-14 |
| Reason for Change/s:* | Introducing new use case on Autonomous driving in TR0026 |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR0026 and 0.6.0 |
| Clauses * | Section 6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR in introducing new use case on Autonomous driving that refers to the capability of the vehicle to drive from one location to another, without intervention from humans, and in a safe way, without incurring damage to surroundings (pedestrians, buildings, other vehicles) and to its (vehicle’s) passengers.

Use case will also define potential requirements, regarding timing and packet losses (reliability of transfer) which will have wider use and impact on other domains.

### -----------------------Start of change 1-------------------------------------------

### 6.X 	Autonomous driving

Autonomous driving (AD) refers to the capability of the vehicle to drive from one location to another, without intervention from humans, and in a safe way, without incurring damage to surroundings (pedestrians, buildings, other vehicles) and to its (vehicle’s) passengers.

Different levels of automation are shown in the figure 1, section 5.4 of this document. From top to bottom we can see increasing levels of automation, with ‘Full automation’ (level 5)  being autonomous driving.

### 6.X.1	Connected car and surroundings / devices

Modern vehicles are equipped with number of sensors which are increasing comfort, fuel efficiency and safety of vehicles. That is done by using a variety of sensors that measure and collect data about vehicle (ABS sensors, brake switch, wheel angle sensor, …), vehicle’s current state (speed, location),. but are also equipped with sensors to observe state of its surroundings – using radar, camera, short range distance measurement sensors, lidar, …

Further, the roads and surrounding infrastructure are becoming more instrumented with sensors and communicating devices. The possibility of interconnecting infrastructure sensors (cameras, traffic light radars, road sensors, …) and thus exchanging data with vehicles may lead to new ways to design autonomous vehicle systems, thereby reducing cost and increasing robustness and reliability of autonomous driving vehicles.

Other connected objects may also  act as an additional sources of data for autonomous driving vehicle, thereby contributing to improved efficiency, accuracy and safety of the Autonomous driving functions.

System supporting combining all these sources of data will enable pushing the driving automation to the full automation, one where the driver is out of the (control/driving) loop. Furthermore, by making autonomous cars an  IoT entity, this will enable developers to create IoT/AD services as easy as for any other IoT application.

### 6.X.2 	Source

This document.

### 6.X.3 	Actors

- Vehicle Driver:

Driver sits in its normal (driving) position, and is in position to take corrective action (level 3) when prompted to do so by the autonomous driving system..

- IoT platform provider:

It operates a IoT platform which is collecting data from vehicles, other participants in traffic (pedestrians, cyclists), from roads and associated infrastructure (traffic lights, cameras,...).

- Autonomous driving application provider:

Party that is providing Autonomous driving application (ADApp) which is running on AS (Application Servers). AS connects to the IoT platform(s), and collect relevant data needed to run an ADApp – for example LDM (Local Dynamic Map).

- Communication Network provider / operator:

Provides and facilitates connectivity between vehicles,  roads and associated infrastructure. This covers both wireless (for example LTE, LTE-V2X or ITS-G5) and fixed connections. Network MUST support receiving requests for data transfers with required latency and with required packet losses. It is not expected or mandated that single network operator provides all of connectivity.

- IoT Device:

IoT devices are embedded in a vehicles, roads and associated infrastructure, as well as in devices used by other participants in traffic (pedestrains, cyclists). Each IoT device collects and sends data to IoT platform(s), and can receive data from platform.

### 6.X.4	Pre-conditions

- The vehicle supports autonomous driving – is capable of transmitting and receiving data from other vehicles, road and other infrastructure,other participants in traffic (pedestrians, cyclists) and  making decision on own actions based on collected data and data received from ADApp, and act upon those decisions.

### 6.X.5	Triggers

Autonomous driving mode can be activated by vehicle driver, or it can be activated by default (keeping vehicle permanently in autonomous driving mode)  – how the HMI (Human Machine Interface) works and which commands are given to the vehicle is out of scope.

### 6.X.6		Normal Flow

- The vehicle continuously collects data from sensors within the vehicle and sends it to the IoT platform. The collected  data includes information from Engine and Transmission System, Stability Control System, Air Bag System, Emission System, Antilock Brake System and so on. Further, data is collected on surroundings of the vehicle – from vehicle’s sensors such as radar, lidar, …

- Road infrastructure (roads, traffic lights, cameras, …) continuously collects data from its sensors and sends it to the IoT platform.

- Devices belonging to other participants in traffic (pedestrians, cyclists,…) continuously collect data from its sensors and send it to the IoT platform.

- The IoT platform hosts  the collected data, and upon request from AS (Application Server) where Autonomous driving applicatiuon (ADApp) is running. ADApp is subscribed to particular sources of data, and receives and analyzes the IoT data from all partticipants in traffic.

- Processed information from ADApp is sent back to IoT platform, and is made available to all ADApp subscribed participants in traffic.

- Each participant in traffic is responsible for  collection and  interpretation of received ADApp data, and acting upon it.

### 6.X.7	Alternative Flow

None

### 6.X.8	Post-conditions

Vehicle stays  in autonomous driving mode until removed from it by driver.

### 6.X.9	High Level Illustration

Figure 2: Example of IoT data streams and corresponding communication networks

### 6.X.10	Potential Requirements

- The M2M system shall support the IoT data to be transmitted to IoT platform with highest priority, with strict timing requirements and packet loss  requirements, with requirements defined by application (here – ADApp).

- The M2M system shall support the application (here ADApp) data transmissions to subscribed with highest priority, with strict timing and packet loss requirements, with requirements defined by application (here – ADApp).

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

<If the text is new text, turn on "Track Changes" and start typing or paste the new text>

<If the CR is changing existing text.

- Select the text from the latest baseline TS or TR.

- Turn  "Track Changes" off.

- Paste the existing text from the baseline.

- Turn "Track Changes" on.

- Make the proposed changes.>

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change n-------------------------------------------

<If the text is new text, turn on "Track Changes" and start typing or paste the new text>

<If the CR is changing existing text.

- Select the text from the latest baseline TS or TR.

- Turn  "Track Changes" off.

- Paste the existing text from the baseline.

- Turn "Track Changes" on.

- Make the proposed changes.>

### -----------------------End of change n---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf))

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

IoT platform

Application

Platform

(ADApp)

V2V/V2I communication (LTE-V, ITS-G5)

Cellular communication (LTE, 5G)

Fixed connectivity