MADRID 3

| CHANGE REQUEST |
| --- |
| Meeting ID:* | REQ 29 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com |
| Date:* | 2017-04-04 |
| Reason for Change/s:* | TS002 new reqs from TR-0026, not implemented |
| CR against: Release* | Release 3 |
| CR against: WI* | Active MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision) Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 V 2.9.3 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TR-0026 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This document proposes to move requirements pertaining to Vehicular Domain from TR-0026 clause 7 to TS-0002.

The requirements contained in this CR pertain to Release 3 or future releases, i.e. have not yet been implemented. For that reason, this move is aimed at:

- Accurately capturing Vehicle Domain requirements which will be fulfilled in Release 3 for an accurate release description

- Capturing requirements identified in the Vehicle Domain WI to be covered in future releases

Initially the text is shown as existing for ease of reading and commenting. All the text in each change will be new in TS-0002.

oneM2M is invited to:

- Provide feedback about which of these requirements should be designated as Release 3 requirements

- Propose necessary text changes in order to achieve clear requirements

R01 contains notes received offline and uses cross-referencing based on REQ-2017-0034, in order to sync up with REQ-2017-0030 and REQ-2017-0033 as well.

R03 includes ARC agreements on changes 1 and 3 (except the highlighted requirements)

R04 includes SEC agreements on the SER requirements .

### -----------------------Start of Change 1 -------------------------------------------

| OSR-yy1 | The oneM2M System shall enable exchanges of diagnostic data periodically between M2M Devices and the Infrastructure Domain. | Rel-3/ future releases |
| --- | --- | --- |
| OSR-yy2 | The oneM2M system shall support a mechanism to describe the syntax and semantics format of the diagnostics data exchanged between the M2M Devices and the InfrastructureDomain. | Rel-3/ future releases? |
| OSR-yy3 | Provisioning, installation, configuration and registration method of terminal system. Especially for the case of overlapping two different system for DTG management system (owns and manages the device) and the application system using DTG data (utilising the data from the device). | Rel-3/ future releases? |
| OSR-yy4 | DTG/FMS data storing method and delivery protocol. There is no dominant standard specifying data formats and protocols for vehicle related applications. | Rel-3/ future releases? |
| OSR-yy5 | The oneM2M System shall be able to provide the service capability for location based services | Implemented |
| OSR-yy6 | The oneM2M System shall be able to provide the service capability supporting Over The Air management. | Implemented |
| OSR-yy7 | The oneM2M system shall provide the capability for an M2M Device to maintain registration with multiple entities simultaneously. | Rel-3/ future releases? |
| OSR-yy8 | The registration shall be able to include information that identify the peer entity, and other information such as its management privilege, subscription etc., that are necessary for the conduct of the respective peer relationships. | Rel-3/ future releases? |
| OSR-yy9 | It shall be possible for some registrations to hold the complete set of information context about the peer entity. This is referred to as "full registration". | Rel-3/ future releases? |
| OSR-y10 | It shall be possible for some registrations to hold only a subset of information context about the peer entity. This is referred to as "lightweight registration". | Rel-3/ future releases? |
| OSR-y11 | It shall be possible for "lightweight registration" at different entities that pertain to a common peer entity, to hold different sets of information, if needed, about the common peer entity. | Rel-3/ future releases? |
| OSR-y12 | It shall be possible to correlate the "full registration" and the "lightweight registration" that pertain to a common peer entity. | Rel-3/ future releases? |
| OSR-y13 | It shall be possible to distinguish the "full registrations" and the "lightweight registrations" that pertain to a common peer entity. | Rel-3/ future releases? |
| OSR-y14 | The oneM2M System shall enable exchange of information with the intended vehicles by unicast, multicast and/or broadcast. | Partially Implemented (Note x) |
| OSR-y15 | The oneM2M System shall be able to transfer time critical information. . For example for feeding back current road states to automatic driving control,the feedback time should be less than a few seconds (the distance between vehicles normally corresponds to a few seconds) to avoid unnecessary speed down/stop of following vehicles. (Note y) | Rel-3/ future releases? |
| OSR-y16 | The oneM2M System shall be able to guarantee its reliability in order to receive/feedback messages from/to related M2M Devices (e.g. for Vehicular Domain) . (Note y) | Rel-3/ future releases? |
| OSR-y17 | The oneM2M System shall enable sharing of service information between devices/GWs based on proximity. (Note y) | Rel-3/ future releases? |
| OSR-y18 | The oneM2M System shall enable sending and receiving of service information between devices/GWs with minimized interruption. (Note y) | Rel-3/ future releases? |
| OSR-y19 | The oneM2M System shall support mobile/portable M2M Gateway and/or Device. | Rel-3/ future releases? |
| OSR-y20 | The oneM2M System shall enable changing of the reporting (or subscription) mechanisms and/or configurations related to a service. | Rel-3/ future releases? |
| OSR-y21 | The oneM2M System shall support triggering M2M Devices for on-demand reporting regarding collected data. | Rel-3/ future releases? |
| OSR-y22 | The oneM2M System shall enable the M2M Infrastructure to facilitate direct communication between two or more different M2M devices without having registered with one another. | Rel-3/ future releases? |
| OSR-y24 | The oneM2M System shall be able to verify geographical location information from moving objects regardless of information accuracy. | Rel-3/ future releases? |
| OSR-y25 | The oneM2M System shall be able to verify time synchronization | Rel-3/ future releases? |
| OSR-y26 | The oneM2M System shall be able to coordinate end-to-end reliable communications for applications that can have safety impacts. | Rel-3/ future releases? |

Note x: Unicast communications have been implemented in Release 1

Note y: Definition of “real time” and how to specify timing and reliability requirments is TBD.

### -----------------------End of Change 1 ---------------------------------------------

### -----------------------Start of Change 2 -------------------------------------------

| SER-yy1 | The oneM2M system shall be able to support authentication using device key and the integrity check ofM2M Device(s). | Rel-3? |
| --- | --- | --- |
| SER-yy2 | The oneM2M system shall be able to support anonymization of the t information being provided, when requested by M2M Applications.. | Rel-3/ future releases? |
| SER-yy3 | The oneM2M system shall be able to request the Underlying Network to perform, on behalf of the oneM2M System, privacy policy decisions concerning the location information, if the location information is obtained by the Underlying Network location service. | Rel-3/ future releases? |
| SER-yy4 | The oneM2M System shall apply appropriate security levels for Applications that can have safety impacts (e.g. protection from malicious attacks) | Rel-3/ future releases? |

### -----------------------End of Change 2 ---------------------------------------------

### -----------------------Start of Change 3 -------------------------------------------

| CHG-yy1 | The oneM2M System shall support mechanisms to correlate charging information (e.g. data/records) from different M2M Application Service Providers. | Rel-3/ future releases? |
| --- | --- | --- |

### -----------------------End of Change 3 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?