| Input Contribution |
| --- |
| Meeting ID* | REQ30 |
| Title:* | TR-0026 key issue about security for credential |
| Source:* | Norihiro Okui, KDDI, no-okui@kddi.com Yutaka Miyake, KDDI, miyake@kddi.com Kenichi Yamamoto, KDDI, kc-yamamoto@kddi.com François Ennesser, Gemalto, francois.ennesser@gemalto.com |
| Date:* | 2017-07-11 |
| Input related to* | WI-0046 TR-0026 V 0.9.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | Agree for inclusion in TR-0026. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This document provides new security key issue about security for credential.

### ---------------------- Start of change 1-------------------------------------------

### 9.4.X	Security for credential

In almost all of the use cases described in clause 6, it is necessary to authenticate between entities before a service starts. In vehicle domain, there are many use cases that impact safety (particularly use cases at clause 6.2, 6.8 and 6.11), so that a trusted credential should be used for authentication. Figure 9.4.x.1 shows examples of authentication between infrastructure node and communication module. If a credential in communication module is compromised, malicious node can connect with communication module. After establishment of connection, malicious node may be able to receive vehicle information such as version of installed software and may be able to send malicious message.

Figure 9.4.x.1 Example of authentication betweem infrastructure node and communication module

Figure 9.4.x.2 shows an example of authentication between gateway and ECU. A credential is used for authentication between gateway and ECU. If the credential in gateway or ECU is compromised, unauthorized ECU can be installed.

Figure 9.4.x.2 Example of authentication between Gateway and ECU

In addition to authentication, some data such as ECU software/middleware/firmware also impact the in-vehicle system, so the data shoud be verified for integrity using a trusted credential. Figure 9.4.x.3 shows an example of integrity check of software/middleware/firmware on gateway. If boot key and boot MAC are compromised, unauthorized software/middleware/firmware can be installed.

Figure 9.4.x.3 Example of integrity check of software/middleware/firmware on gateway

Figure 9.4.x.4 shows an example of verification of ECU integrity. ECU creates digests of software/middleware/firmware and digital signatures of each digests using ECU private key, then ECU send the digests and signatures to gateway. Gateway verifies the digital signatures using ECU public key. If ECU private key is compromised, unauthorized ECU can be installed.

Figure 9.4.x.4 Example of verification of ECU integrity

To protect the credentials from compromising and tampering, it is important to store the credentials in tamper resistant storage and protect cryptgraphic operation from side channel attack.

### -----------------------End of Change 1 ---------------------------------------------