## Slide 1: REQ-2017-0072-Autopilot_IoT_architecture_slideset
Miodrag Djurica (TNO)
13-11-2017

## Slide 2: PILOT SITE BRAINPORT (NL)
A total of 10 vehicles used:
  TNO/Tass: 3 Toyota Prius
  TU/e: 1 Toyota Prius and 3 VFLEX
  VALEO: 1 VW Tiguan
  NEVS: 3 electric vehicle (D-class)
  TT: 1 mobile mapping van
Partners involved:

## Slide 3: Brainport architecture overview
ITS-G5 RSU
ITS-G5
RSU
TASS
systems
Fiber backbone
eNB
(4G) Helmond
Pre 5G core network
(TNO)
Huawei IoT platform
Application server
Time critical
data via G5
(10-20ms)
Tactical
data via LTE
(100ms+)
MEC-node with IoT (oneM2M)
platform
local breakout
REST API
REST API
MEC applications platform
DLR drone
eNB (commercial)
Helmond
Image
processing
Sensinov IoT
(oneM2M) platform
Public internet
Brainport applications platform (TNO, NEC, IBM)
WATSON IoT platform
REST API
FIWARE IoT platform
REST API
In-vehicle IoT
and Apps Platform

## Slide 4: IoT stack and initial functionality
AD functions
Vehicle IoT node
Collect vehicle state data and run AD functions – lane assist, platooning (keep distance, speed,…). Pass vehicle state data to vehicle’s IoT node.
Pass vehicle state data to MEC and IN IoT node.
Collect global (IoT) non-time critical data relevant for AD functions (waypoints, traffic lights states, platooning,…)
Tactical
services
MEC IoT node
Run services relevant for vehicle on a given road segment (HD maps distribution, current state of traffic lights, …), platoon management (cars joining / leaving).
Pass road and vehicles data from MEC to IN IoT node.
Collect global (IoT) non-time critical local (for given road segment covered by MEC node) data relevant for AD functions.
In-vehicle non-time critical services
In vehicle non-time critical services: navigation based on waypoints
Strategic
services
IN IoT node
Run services relevant for vehicle globally – for example platoon subscription, road planning, waypoint calculation, targeting rendezvous for joining platoon,…
Get parking places for AVP (from smart city / smart garage platforms, …)
Collect global (IoT) non-time critical local from other data sources and platforms

## Slide 5: Autopilot In-vehicle IoT platform