| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) |
| Title:* | Application Registration Handing Procedure on Security CSF |
| Source:* | FUJITSU (TTC) |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-01-14 |
| Abstract:* | This contribution propose procedure on Registration Handling on Security CSF |
| Agenda Item:* | CSF Procedure |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 member should discuss on this topic, and determines final form to be included as part of security TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposed the procedure for application registration on CSE by AE.

After registration is done, ether delivery for notification message targeted AE, or API call at Mca reference point is by requested AE itself or delegated AE, are enabled.

x.x	Procedures in Security CSF

x.x. 1	Application Registration Handing

Name:

Registration Handling”

Short Description:

AEs will be required to register itself on hosting CSE for use of Mca reference point.

Residing On

Application hosting CSE

Scope (Multiplicity)

Number of Application hosting CSEs

Called by

AE or other CSE

Trigger Condition

An AE starts to use M2M Service

Prerequisites / Starting state

- Master credential is provisioned and become ready to use

- Secure communication channel between AE and hosting CSE  is established

- Preferred method of notification is determined by AE

Input parameters

Service Subscription ID (Account)

ID associated with credential to be authenticated the originator’s identity

AE contact address

Contact address to receive notification message. Optionality is depends on chosen transport protocol.

AE master credential

The Credential to be authenticated as the identity for use of service on reference point Mca.

Type of registration

Specifies the type of registration (‘notification’, or ‘authorization’)

Duration for registration validity

Optionally specified to limit the validity length. Hosting CSE should provide determined value no matter this parameter is specified or not.

Output parameters / final state

Status

Indicate status of registration

Authorization token
Optional. The temporal credential to use for API calls or delegated use of M2M service.

Duration for registration validity

Determined duration for registration which is expressed as expiration time

Registration ID

ID which is assigned to manage the requested registration. Existing registration may be deleted (revoked), or updated

External Interactions

Request to issue the authorization token to infrastructure node

Setup the timer event to delete the registration on its expiration

Distribute (or register) issued token to targeted CSE which is associated with authorized activity for token holder.

Constraints

(FFS)