| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) |
| Title:* | Provisioning Procedure for ASN/MN |
| Source:* | Gemalto |
| Contact: | Francois Ennesser, Gemalto, francois.ennesser@gemalto.com |
| Date:* | 2014-01-20 |
| Abstract:* | This contribution proposes a description of the provisioning procedure with an M2M Service Provider for an ASN/MN, based on the template in contribution oneM2M-SEC-2014-0086R01 |
| Agenda Item:* | Contributions impacting ARC TS-0001 |
| Work item(s): | ARC WI-0002, SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) and Architecture TS (TS-0001) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 member should discuss on this topic, and determines final forms to be included as part of Security TS and/or Architecture TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposes a high-level (generic) description of the procedure for ASN/MN security bootstrapping to an IN of a target M2M Service Provider. This procedure is only needed if the ASN/MN was not initially pre-provisioned with credentials shared with the infrastructure of the target M2M Service Provider.

x.x	Procedures in Security CSF

x.x. 1	M2M Service Bootstrapping

Name:

M2M Service Bootstrapping

Short Description:

In order to secure access between ASN/MNs and the infrastructure of an M2M Service Provider, an ASN/MN shall be provided with a long-term secret (key) shared with the infrastructure of the M2M SP. Note that this key is a root secret intended to remain protected in the long term, to be used to derive within a secure environment the specific short-term secrets that will be used to provide actual security services, such as Security association establishment.

Residing On

Application hosting CSE

Scope (Multiplicity)

When an ASN/MN is requested to use the services from an M2M Service Provider to an M2M SP, unless it was initially pre-provisioned for such service, it shall execute the M2M Service bootstrapping procedure once. Once it has been executed, the node will be provisioned for that M2M SP’s services, so no further execution of the procedure will be needed unless the M2M service subscription expires or is intended to be modified (e.g. change to a different M2M SP).

The M2M Service Infrastructure of the target M2M Service Provider shall provide an M2M Authentication Server functionality (MAS), and a specific functionality to support the M2M Service Bootstrapping Function (MSBF): These functions are accessed by the ASN/MN through the Infrastructure but only one instance of them needs to be available in the Infrastructure.

Called by

AE or CSE

Trigger Condition

An AE wish to use the services associated with a M2M Service subscription with a target M2M SP.

Prerequisites / Starting state

- The ASN/MN has not been pre-provisioned with a credentials to the target M2M SP. However, a pre-provisioned credential (ID and secret) is needed to perform the bootstrapping procedure. This may be provided by e.g.

- in the case of GBA bootstrapping,

- USIM/CSIM/ISIM credentials shared with a HSS/HLR/AAA.

- in the case of PKI bootstrapping,

- a root CA certificate (for authenticating the MSBF) and

- a private key and associated client certificate (by which the ASN/MN authenticates itself to the MSBF).

- Preferred method of bootstrapping may depend on ASN/MN configuration or be negotiated with the infrastructure.

- Once Bootstrapping has been performed, the MSBF is able to provision the MAS used to authenticate ASN/MN with the M2M Service Provider.

- In the case of GBA, an agreement enables the MSBF of the M2M SP to retrieve the NAF key from the BSF involved in the GBA procedure.

- In the case of PKI, the ASN/MN client certificate has a certificate chain to a root CA certificate trusted by the MSBF, and the MSBF has a certificate chain to a root CA certificate trusted by the ASN/MN.

Input parameters

An initial identifier pre-provisioned in the ASN/MN and associated secret (see first bullet in “Prerequisites / Starting state” above).

Identifier for the MAS.

Output parameters / final state

The following parameters are established with the assistance of the MSBF.

A Node ID associated to the ASN/MN by the M2M Service Provider

An M2M Long Term Service Key is now provisioned in a secure environment of the ASN/MN for the target M2M service provider.

In case of GBA, this is a NAF-specific key.

In case of PKI, this key is delivered securely (e.g. TLS + HTTP) by the MSBF to the ASN/MN.

The lifetime of the above key shall be indicated

Other ID may be provisioned by the M2M SP as part of bootstrapping, e.g. a CSE ID for the ASN/MN. The CSE ID of the IN may also be provided to the ASN/MN.

External Interactions

The MSBF in the M2M Service provider infrastructure is involved in the initial bootstrapping step with the ASN/MN. Once successful, the MAS used to authenticate ASN/MN with theM2M Service Provider shall be provisioned by the MSBF.

Constraints

(FFS)

# Comments

I think subscription is done before this request.

May “initially connect” ?

And I can see there are many “subscribe”, “subscription” terms in this contribution. We need to discuss this.

I think subscription here is done offline, and I think we need to use some technical term in TS. Bootstrap information is better term?

I agree that subscription is not quite right in some places, however I do se that subscription is appropriate in others. See my suggested changes

See Seongyoon’s comment below.

I agree with Seongyoon.

We need to separate two things: AE service bootstrap, CSE service bootstrap.

AE may need to have root key and ID (I’m not quite sure we need to cover this case yet. may be optionally?) and

CSE shall have root key and ID.

Therefore AE and CSE are the entities who can trigger service bootstrap

Agree with Seongyoon, subscriber’s is not appropriate here.

Authenticate Node?

We are in oneM2M system and We don’t have “subscriber” entity in the architecture.

We only need to talk within oneM2M entities (Node, AE, CSE) that defined in ARC TS.

I think Node ID is the initial identifier.

We only have Node ID, AE ID, CSE ID in ARC TS. We need to provide security solution based on those identifiers.

This text moved to the first bullet of “Pre-requisites/starting states”.

It wasn’t clear to me if this should be the identifier of the MAS or the IN. Since the IN is not really mentioned in the description, I guessed it was the MAS that should be identified

I think CSE ID or AE ID is appropriate

I think Node ID is appropriate here. CSE ID can optionally be provided (see point d).

In my opinion, these details can be left out of this description, as they may cause confusion and may be subject to change.