| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) |
| Title:* | Bootstrapping (i.e. Online Provisioning) of a device for M2M services, which results in the creation of a “node” equipped with a CSE in an M2M SP infrastructure |
| Source:* | Gemalto |
| Contact: | Francois Ennesser, Gemalto, francois.ennesser@gemalto.com |
| Date:* | 2014-02-03 |
| Abstract:* | This contribution (Update of SEC-2014-0016) proposes a description of the bootstrapping procedure of a non pre-provisioned device with an M2M Service Provider. This contribution is based on the procedure template in contribution oneM2M-SEC-2014-0086R01. |
| Agenda Item:* | Contributions impacting ARC TS-0001 |
| Work item(s): | ARC WI-0002, SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) and Architecture TS (TS-0001) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 member should discuss on this topic, and determines final forms to be included as part of Security TS and/or Architecture TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposes a high-level (generic) description of the procedure for the security bootstrapping of a subscription with a target M2M Service Provider, on an M2M device (useful e.g. for devices that can be acquired off-the-shelf). This procedure is only needed for devices not initially pre-provisioned with subscription credentials shared with the infrastructure of a target M2M Service Provider.

A device may or may not have been provisioned with M2M Applications when provisioned for M2M services. Whether applications have been instantiated on the device before or after the device is provisioned for M2M Services, an Application Instantiation procedure needs to be executed with the M2M Service Provider after their hosting device has been provisioned for M2M Services, before the applications can use the services of the selected M2M SP.

x.x	M2M Service Provisioning for M2M devices

Depending on deployment scenarios, M2M devices may be initially pre-provisioned to use the M2M Services of a specific M2M SP, by personalization e.g. during manufacturing, at point of sale, or in the distribution phase; or they may be acquired of the shelf with no initial link to an M2M SP, and will become part of an M2M System only when provisioned with an M2M service subscription. In any case the provisioning may be performed either locally or remotely. To enable devices deployed on the field to be remotely provisioned for M2M Service, the M2M Service Bootstrapping procedure described below may be supported. When supported, this procedure shall be implemented as specified in [TS-0003].

x.x. 1	M2M Service provisioning

[TBD]

x.x. 1	M2M Service Bootstrapping Procedure

Name:

M2M Service Bootstrapping procedure

Short Description:

This procedure is used to provision specific security credentials, such as a long-term secret key and a node identifier, that are shared between the device and the infrastructure of the M2M SP.

The long-term credential associated with an M2M subscription may typically be an M2M Service specific root key intended to remain protected in the long term, used to derive (within a secure environment) the shorter-term secrets used to provide actual M2M security services, such as Security association establishment.

Residing On

M2M device not yet provisioned for use with a chosen M2M SP. This procedure involves human actions such as associating the device with an M2M Service Subscription contracted with a chosen M2M SP. This may be done by establishing a secure out-of-band communication session between the M2M device and an M2M Service Bootstrap Function (MSBF) in the M2M System, relying on initial device credentials provided e.g. by the device manufacturer.

Scope (Multiplicity)

When a device is intended to use the M2M services from an M2M Service Provider, unless it was initially pre-provisioned for such service, it shall execute the M2M service bootstrapping procedure once, in order to instantiate a CSE associated with that M2M SP. Once the procedure has been executed, the initially unprovisioned device becomes an M2M node associated with an M2M Service Subscription with the target M2M SP, so no further execution of the procedure will be needed unless the M2M service subscription expires or is intended to be modified (e.g. change to a different M2M SP).

The M2M System shall provide an M2M Authentication Server functionality (MAS) that enables an M2M service provider to associate entities accessing the services with contracted M2M Service Subscriptions: This function is accessed through the M2M Infrastructure and like for the MSBF, only one instance of it needs to be available for each M2M Service Provider.

Called by

The human M2M service subscriber that contracts an M2M Service Subscription for use by the M2M device (Before M2M Service Provisioning, there is no notion of AE or CSE on a device).

Trigger Condition

An M2M Service Subscriber wish to use the services associated with a M2M Service subscription with a target M2M SP.

Prerequisites / Starting state

- The device has not been pre-provisioned with credentials for the target M2M SP. However, a pre-provisioned credential (Device ID and secret provided e.g. by the device manufacturer) is needed to perform the bootstrapping procedure.

(Note: This may be provided by e.g.

  - in the case of GBA bootstrapping, relying on a Network Operator

    - USIM/CSIM/ISIM credentials shared with a HSS/HLR/AAA.

  - in the case of PKI bootstrapping, relying on a trusted party

    - a root CA certificate (for authenticating the MSBF) and

    - a private key and associated client certificate (by which the ASN/MN authenticates itself to the MSBF).

- Preferred method of bootstrapping may depend on initial device configuration or be negotiated with the infrastructure. It is assumed that the device may already have been bootstrapped for Communication Services with a network operator prior to the M2M Service Bootstrapping procedure.

- Once Bootstrapping has been performed, the MSBF is able to provision the MAS used by the M2M Service Provider to associate the device with a valid M2M service subscription and authenticate it.

(Note:

  - In the case of GBA, an agreement enables the MSBF of the M2M SP to retrieve the NAF key from the BSF involved in the GBA procedure.

  - In the case of PKI, the device client certificate has a certificate chain to a root CA certificate trusted by the MSBF, and the MSBF has a certificate chain to a root CA certificate trusted by the ASN/MN.)

Input parameters

- An initial identifier already provisioned in the device and associated secret (see first bullet in “Prerequisites / Starting state” above).

- Identifier for the MAS.

Output parameters / final state

The following parameters are established with the assistance of the MSBF.

A Node ID associated to the physical device by the M2M Service Provider: This enables the M2M SP to use an abstract representation of the device as an ASN/MN supporting a CSE in its infrastructure.

An M2M Long Term Service Key is now provisioned in a secure environment of the device CSE for the target M2M service provider.

(Note:

- In case of GBA, this is a NAF-specific key.

- In case of PKI, this key is delivered securely (e.g. TLS + HTTP) by the MSBF to the ASN/MN.)

The lifetime of the above key shall be indicated

Other ID may be provisioned by the M2M SP as part of bootstrapping, e.g. a CSE ID for the ASN/MN. The CSE ID of the IN may also be provided to the ASN/MN.

Note that activation of the CSE on a device requires its provisioning for a subscription (enabling assignment of a CSE-ID). However it is assumed that when an application  is instantiated into an AE on an unprovisioned device, the assignment of the App-Inst-ID may be done using the pre-existing  device ID. If the CSE-ID or the Subscription-ID needs to be used to derive the App-Inst-ID from the App-ID, an application bootstrapping process (not considered here) may need to take place to enable assignation of the App-Inst-ID.

Related Question: Imagine an AE using services from 2 different SPs (implying different CSEs), can it use the same App-Inst-ID for both subscription?

External Interactions

The MSBF in the M2M Service provider infrastructure is involved in the initial bootstrapping step with the M2M device. Once successful, the MAS used to authenticate ASNs/MNs with theM2M Service Provider shall be provisioned by the MSBF.

Constraints

(FFS)