| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC8.0 (WG4 at TP#9) |
| Title:* | SEC CSF Architecture Figure Update for Security TS |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-02-17 |
| Abstract:* | This contribution aims to add some text that describes the layer structure of the SCE CSF architecture and update the SCE CSF Architecture Figure. |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add/replace the proposed text and figure into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to (1) add some text that describes the layer structure of the SCE CSF architecture and (2) update the SCE CSF Architecture Figure.

The Section 5.1 in the “oneM2M-TS-0003-Security_Solutions-V-0.2.0” defines three-layer SEC CSF architecture. However, it absents the detail description about these layers. This contribution provides some text for describing these layers.

The reasons for updating the SCE CSF Architecture Figure are:

- Current figure provides too much information that cannot be clearly defined in current stage, especially in the security environment;

- Some independent components are grouped, for example, authentication and authorization should belong to two independent components; in fact there is no access control component provided through the SEC CSF API.

2	Proposal

-----------------------Start of 1st   change-------------------------------

## 5.1	Overview

The following figure provides a high level overview of the Security CSF architecture.

The architecture consists of following layers:

- Security Functions layer

This layer contains a set of security functions that are exposed to the outside through the SEC CSF API (Mca, Mcc). A security service requester invokes a security function in this layer in order to get a corresponding security service. These security functions can be classified into six categories; they are Identification, Authentication, Authorization, Security Association, Sensitive Data Handling and Security Administration. For example, in a SEC CSF the Authentication category may contain password-based authentication function, PKI-based authentication function and symmetric key-based authentication function.

- Secure Environment Abstraction Layer

This layer implements security functions related to Secure Environments such as key derivation, data encryption/decryption, signature generation/verification, security credential read/write from/to the Secure Environments, and so on. The security functions in the Security Functions Layer invoke these functions in order to do the operations related to the Secure Environments. In addition this layer also provides physical access to the Secure Environments. Implementation of this is out of scope of the present document.

- Secure Environments layer

This layer may contain multiple independent secure environments that provide various security services related to sensitive data storage and sensitive function execution. The sensitive data includes SE capability, security keys, local credentials, security policies, identity information, subscription information, and so on. The sensitive functions include data encryption, data decryption, and so on.

-----------------------End of 1st  change-------------------------------