| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC8.0 (WG4 at TP#9) |
| Title:* | SEC CSF Authorization Description Update for Security TS |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-02-17 |
| Abstract:* | This contribution aims to replace some text and figures related to authorization description. |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add in TR-0008-Security the text provided in this contribution |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to replace some text and figures related to authorization description.

2	Proposal

-----------------------Start of 1st   change-------------------------------

## 2.2	Informative references

[x.1]	eXtensible Access Control Markup Language (XACML) Version 3.0. 22 January 2013. OASIS Standard.

-----------------------End of 1st  change-------------------------------

-----------------------Start of 2nd   change-------------------------------

## 3.1	Definitions

Policy Access Point: The system entity that finds applicable policy or policy set.

Policy Decision Point [x.1]: The system entity that evaluates applicable policy and renders an authorization decision.

Policy Enforcement Point [x.1]: The system entity that performs access control, by making decision requests and enforcing authorization decisions.

Policy Information Point [x.1]: The system entity that acts as a source of attribute values.

-----------------------End of 2nd  change-------------------------------

-----------------------Start of 3rd   change-------------------------------

## 3.4	Acronyms

PAP	Policy Access Point

PDP	Policy Decision Point

PEP	Policy Enforcement Point

PIP	Policy Information Point

-----------------------End of 3rd  change-------------------------------

-----------------------Start of 4th   change-------------------------------

#### 6.3.1.2	Authorization

The Authorization component provides authorization services for the CSFs that are located in the local CSE or remote CSEs. The following figure provides a high level overview of the Authorization component. The Authorization component consists of following entities:

- Policy Enforcement Point (PEP)

PEP coexists with the CSFs that need authorization services. The PEP intercepts resource access requests, makes access control decision requests, and enforces access control decisions.

- Policy Decision Point (PDP)

PDP interacts with the PAP and PIP to get applicable authorization polices and attributes needed for evaluating authorization policies respectively, and then evaluates access request using authorization policies for rendering an access control decision.

- Policy Access Point (PAP)

PAP obtains applicable authorization policies according to an access control decision request. These applicable policies should be combined in order to get a finial access control decision. These authorization policies may belong to different access control mechanisms, or written in different authorization languages.

- Policy Information Point (PIP)

PIP provides attributes that are needed for evaluating authorization policies, for example IP address of the requester, creation time of the resource, current time or location information of the requester.

Authorization Flow:

Step 001:	Access Requester sends an Access Request to a resource; this request is intercepted by the PEP.

Step 002:	PEP makes an Access Control Decision Request according to the user’s access request, and sends the decision request to the PDP.

Step 003: 	PDP sends an Authorization Policy Request that is generated based on the Access Control Decision Request to the PAP.

Step 004:	PAP finds all applicable authorization policies to the access request, and provides a policy combination algorithm so that a final access control decision can be calculated.

Step 005:	PAP sends the applicable policies back to the PDP.

Step 006	PDP sends Attribute Request to the PIP if any attributes are required for evaluating these authorization policies.

Step 007:	PIP gets required attributes.

Step 008:	PIP sends obtained attributes back to the PDP.

Step 009:	PDP evaluates Access Request using authorization policies, and calculates the final access control decision using the policy combination algorithm.

Step 010:	PDP returns the finial access control decision back to the PEP.

Step 011:	PEP either forwards the Access Request to the resource or denies this access according to the access control decision,

-----------------------End of 4th  change-------------------------------